# Component Summary

Device Name: Transceiver

Manufacturer: Nordic Semiconductor/Sparkfun

Part No: nRF2401A (sku: WRL-00152)

System: Stationary-to-Rotary Data Transfer

Supply Voltage: 1.9 V to 3.6 V

Average Power Usage: Tx: 35 mW, Rx: 60 mW

Operating Frequency: 2.4 GHz – 2.524 GHz

Operating Temperature Range: -40˚C to 85˚C

Input Sensitivity: -93 dBm

Communication: SPI

Inputs: Six: Chip Enable, Chip Select, Data Ready, Clock, Data, Power Up

Microcontroller Modules Needed: One Bi-directional SPI

Microcontroller Memory Needed: Enough to handle transfer of image, must include “data ready” input pin as variable in polling loop to know when information has been received.

Weight: n/a

Cost: $25 each

Lead Time: One week