## Slide 1: FE Exam: Dynamics review
D. A. Lyn
School of Civil Engineering
16 Sept. 2009

## Slide 2: Preliminaries
Units (relevant quantities: g, displacement, velocity, acceleration, energy, momentum, etc.)
Notation (dot, vector)
Vectors (components and directions/signs, addition (graphical), dot and cross products, vector polygons)
Coordinate systems (Cartesian and curvilinear, fixed and moving or relative)
Statics (free body diagram)

## Slide 3: Classification of dynamics and problems
Kinematics: description of motion without reference to forces
  Particle (no rotation about itself) and rigid-body
  Coordinate systems (Cartesian, curvilinear, rotation)
  Constraints on motion
Kinetics: inclusion of forces (mass, or momentum or energy)
  Types of forces: conservative (gravitational, spring, elastic collisions) and non-conservative (friction, inelastic collisions)
  Newton’s 2nd law: linear and angular momentum
    Use of free body diagram to deal with external forces
  Particles and rigid body (system of particles)
  Impulse (time involved) and momentum
  Work (distances involved) and energy

## Slide 4: Particle kinematics
General relations between displacement (r), velocity (u), and acceleration (a)
Given a formula for (or graph of) r as function of t, take derivatives to find u and a
  Given a formula for u or a as function of t, integrate to find r or u
    Special case: constant acceleration,

## Slide 5: Problems
The position of a particle moving horizontally is described by
, with s in m and t in s. At t = 2 s, what is its acceleration?
Soln: Take derivatives of s with respect to t, and evaluate at t=2s ( ) so a(t=2s) = 4 m/s2.
Projectile problem: A projectile is launched with an initial speed of v0=100 ft/s at q=30° to the horizontal, what is the horizontal distance, L, covered by the projectile when it lands again?
Soln: constant acceleration (only gravitational
acceleration involved) problem, so apply
formulae in two directions
wish to find L=xend-x0, for yend-y0=0, so we solve
L=v0xt end and 0=v0ytend+g(tend2/2) for tend and L;
tend=3.1 s and L=269.2 ft

## Slide 6: Curvilinear coordinates and motion
Plane motion (motion on a surface, i.e., in only two dimensions)
  Tangential (t) and normal (n) coordinates
  Radial (r) and transverse () or polar coordinates
  Special case: pure circular motion at an angular frequency, w(t):

## Slide 7: Constrained motion, reference frames, relative motion
Constrained-motion problems – choice of reference frames: relative motion (in a plane)
Choice of reference frames – motion relative to a point A in a moving reference frame
  For plane motion, note direction of components, e.g., WrB/A is perpendicular to rB/A, etc.
  For points on the same rigid body,

## Slide 8: Problem: Kinematics of rigid body example
The end A of rod AB of length L = 0.6 m moves at velocity VA = 2 m/s and acceleration, aA = 0.2 m/s2, both to the left, at the instant shown, when q = 60°. What is the velocity, VB ,and acceleration, aB , of end B at the same instant?
Pure kinematics problem:

## Slide 9: Kinetics of a particle
Linear momentum, L=mu (appearance of mass, i.e., inertia)
Newton’s 2nd law:
Forces determined from free body diagram (as in statics)
  Types of forces: gravitational, frictional, external
Angular momentum (about a point O) ,
Newton’s 2nd law:
Impulse (used in impact and collision problems),
  momentum conservation:
  mini-problem: A golf ball of mass 50-g is hit with a club. If the initial velocity of the ball is 20 m/s, what is the impulse imparted to the ball? If the contact duration was 0.05 s, what was the average force on the ball?

## Slide 10: Problem: kinetics of a particle (truck)
A truck of weight W = 4000 lbf moves down a q=10° incline at an initial speed of u0 = 20 ft/s. A constant braking force of Fbrk=1200 lbf is experienced by the truck from a time, t = 0. What is the distance covered by the truck before it stops from the time that the braking force is applied?
kinematics problem:
Notes: forces involved – kinetics problem, rectilinear (straight-line) motion: determine net force on truck in direction of motion, apply Newton’s 2nd law to evaluate distance covered
From free body diagram, sum of forces in direction of motion,

## Slide 11: Particle kinetics problem
Find the tension, T, in the string and the angular acceleration, a, if at the position shown the 10-kg sphere has a tangential velocity of v=4 m/s.
Choose a polar coordinate system, perform free body analysis to determine sum of forces, and set equal to ma.

## Slide 12: Kinetics of a system of particles (or rigid body)
For a system of particles (or a rigid body), analysis is performed in terms of the mass center, G, located at radial vector, rG, and total mass m
Equations of motions:
where aG is the acceleration of the mass center, and HG is the angular momentum about the mass center
  For a system with no external forces or moment acting, then linear momentum, L, and angular momentum, H, is conserved, i.e., remains constant
For a system of particles (or a rigid body), and where the mass moment of inertia I is defined by (Standard formulae for I = mk2, where k is the radius of gyration, for standard bodies are listed in tables; be careful about which axis I is defined, whether centroidal axis or not, remember parallel axis theorem)

## Slide 14: Problem: two-particle system
A particle A of mass m and and a particle B, of mass 2m are connected by rigid massless rod of length R. If mass B is suddenly given a vertical velocity v perpendicular to the connecting rod, determine the location of the mass center, the velocity of the mass center, the angular momentum, and the angular velocity of the system soon after the motion begins.

## Slide 15: Problem: rigid-body kinetics
What is the angular acceleration, a, of the 60-kg (cylindrical) pulley of radius R = 0.2 m and the tension in the cable if a 30-kg block is attached to the end of the cable?
Analysis of block
  Kinematic constraint (ablock=Ra)
Analysis of pulley

## Slide 16: Energy and work
Work of a force,F, resulting in a change in position from state 1 to state 2:
  Constant force in rectilinear motion, Fx(x2-x1)
  Gravitational force, -W(y2-y1), y>0 upwards
  Spring force, -k(x22-x12)/2, (x2<x1, returning to undeformed state)
Kinetic energy,
Relation between work and kinetic energy:
for conservative forces (such as gravitational and spring forces, but not frictional forces), a potential energy function, V, can be defined such that
  Gravitational force: V = Wy, spring force, V=kx2/2
For conservative forces, an equation for conservation of energy can be expressed as or

## Slide 17: A problem solved using energy principles
A 2-kg block (A) rests on a frictionless plane inclined at an angle q=30°. It is attached by an inextensible cable to a 3-kg block (B) and to a fixed support. Assume pulleys are frictionless and weightless. If initially both blocks are stationary, how far will the 2-kg block travel before its speed is 4 m/s?
Motion constraints: sB=sA/2 (and DyA=-2DyBsinq), and vB=vA/2
Frictionless system  conservative gravitational forces only, only distances and speeds explicitly involved apply energy equation