ME 363

[Lab #7] CNC Machining II

This week's laboratory assignment involves using the CAM software (Mastercam X4) to create a part program for the part shown in Figure 1, post-processing the program and running it on the Emco-Meier CNC milling machine.

- Using the Mastercam manual (if necessary), create a part program for the part shown in Figure 1.  The machine type you need to specify before defining tool paths is MPPC100M.MMD.  There are three features on this part: middle island generation, pocketing, and drilling (use chip break cycle for drilling). The workpiece is Aluminum 7075-T6 and 2 inches by 2 inches in size. Use the following cutting conditions:

- Cutting speed: 1700 rpm

- Feed rate: 10 inches/min.

- Cutting tool: a HSS end mill with a diameter of 0.25 in and 2 flutes (use tool ID T2).

- Coordinates to be used for the tool change: X: -0.5, Y: 0.5, and Z: 1.0

- Stock to be left for finishing pass: 0.01 in.

- Speed to be used for drilling: 2000 rpm

- Feed to be used for drilling: 5 in/min

- Depth increment to be used for drilling: 0.05 in.

- Once the geometry and/or part program is created, you must store it on your network drive space or personal storage media. To save the file, click the File menu and highlight “Save as”. When the submenu is displayed, type in the file name.

- Post process the part program. Post processing will create ISO or EIA codes in an ASCII format for the CNC you specify.  Execute the CNC post processing. After the CNC data is processed, you need to save the .NC file onto a floppy disk for transfer to the Emco mill using a name with the structure: OXXXX (letter O followed by 4 digits—the program number—with no file extension.) If you haven't got any error message, exit from Mastercam X4 and print out the .NC file.

- Take the part program to room 58, load it to the machine (by TA or Mike Sherwood) and perform simulation.  If the program works, make an actual cut.  If not, bring the program back and perform debugging.

Write a report describing the overall procedure used in Mastercam X4, changes made in the part program and your observation.  Also include in the report the printout from Mastercam X4 drawing and the generated part program. Indicate the portion of the program corresponding to each major feature of the part (such as roughing, finishing, pocketing and drilling).

Figure 1: Part dimensions for CNC milling.

NOTE: For the session on milling, the workpiece has to be oriented in Mastercam according to the layout shown in Figure 2 below. In other words, the top left corner of the workpiece will be at the origin of the Mastercam screen with all the Y coordinates being zero or negative.

Figure 2: Coordinates for the CNC milling part.

# Text boxes

Y

X

(0,0)