ME 576  Lab 6  Assignment  	CNC Turning			Name

This week's laboratory assignment involves using the CAM software (Mastercam) to create a part program for the part shown in the attached figure, post-processing the program and running it on the Emco-Meier CNC turning machine.

- Using the Mastercam manual (if necessary), create a part program for the part shown in the attached figure. The machine type you need to specify before defining tool paths is MPLPC120.LMD. The workpiece is Aluminum 7075-T6, 1 inch in diameter and 3 inches in length. Use the following cutting conditions:

Tool:

roughing: number 2, nose radius: 0.032 inch

finishing: number 5, nose radius: 0.015 inch

55 deg. Diamond (inclined angle)

Neutral offset shank, Neg. 3 deg. side cutting (edge angle)

Right handed (cut direction: negative)

Cutting conditions

spindle speed: 2000 rpm (CCW)

max. speed: 4000 rpm

feed rate: 10 inches/min

use 1 for x index and 1.5 for z index

coolant: flood

- Once the geometry and/or part program is created, you must store it on your network drive space or personal storage media. To save the file, click the File menu and highlight “Save as”. When the submenu is displayed, type in the file name.

- For facing, a single pass cutting is sufficient. For roughing and finishing of longitudinal cutting, verify the tool path after tool path is generated. Specify the withdraw angle (other than 45( shown in the tutorial) to avoid the collision of the tool into the workpiece, if necessary. NOTE: The origin for this component has to be set at the point shown in the attached figure. Therefore, all the Z coordinates will be negative and all the X coordinates will be positive.

- Post process the part program. Post processing will create ISO or EIA codes in an ASCII format for the CNC you specify. After the CNC data is processed, you need to save the .NC file onto a floppy disk for transfer to the Emco mill using a name with the structure: OXXXX (letter O followed by 4 digits—the program number—with no file extension.) If you haven't got any error message, exit from Mastercam X4 and print out the .NC file.

- Take the part program, load it to the machine (by TA or Mike Sherwood) and perform simulation.  If the program works, make an actual cut.  If not, bring the program back and perform debugging.

Write a report describing the overall procedure used in Mastercam, changes made in the part program and your observation. Also include in the report the printout of drawing from Mastercam and the generated part program. Indicate what portions of the part program correspond to each machining operation (such as facing, roughing, and finishing).

Figure 1  Geometry of the finished turned part.