Microprocessor (6809)

| X 16 bits |
| --- |
| Y 16 bits |
| U stack pointer |
| H stack pointer |
| PC |
| A (8 bits) | B (8 bits) |
|  |  | N | Z | V | C |  |

# Operations

Arithmetic

- Addition

ADD		ex)  A + M ( A		A + I ( A

ADDB		ex)  B + B ( B		B + I ( B

- Multiplication

MUL 		ex)  A * B ( D

- Subtraction

SUB		ex)  	A - M ( A		A - I ( A

SUBB		ex)	B - M ( B		B - I ( B

Rotation and shift

- Arithmetic shift to the right

ASR

ASRB

- Logic or arithmetic shift to left

LSL, LSLB

- Logic shift to the right

Logic instruction

- Logic AND		AND : Logic AND between A&M or A&I

ANDB :  Logic AND between B&M or B&I

- Logic OR		OR :  Logic OR between A&M or A&I

ORB :  Logic OR between B&M or B&I

- Exclusive OR		XOR : Logic XOR between A&M or A&I

XORB : Logic XOR between B&M or B&I

Incrementing, decrementing, reset

- Incrementing		INC		Incrementing accumulator A or M by 1

INCB		Incrementing accumulator B by 1

- Decrementing		DEC

DECB

- Reset to zero		CLR:		Reset A or M to zero

CLRB: 	Reset B to zero

- Complement to 1	INV:		One's complement A or M

INVB:		Two's complement B

- Complement to 2	NEG:		Two's complement A or M

NEGB:	Two's complement B

Data Transfer

- Loading	LD		I ( A		M ( A

II ( D		MM ( D

LDB		I ( B		M ( B

- Store in memory

ST		A ( M  	D ( MM

STB		B ( M

PLC Processor address field

RAM (8K) $0000 ~ $1FFFF

Inputs / outputs (8K) $2000 ~ $3FFFF

EEPROM

EEPROM

EEPROM

EPROM

Processing cycle: 20 msec

# Input/output Boards

Can be used in bytes and bits

read by byte directly on the input/output modules

read by bits in a working field of the PC memory

RAM STRUCTURE

E.0 ~ E.FF:		256 outside inputs

A.0 ~ A.FF:		256 outside outputs

B.0 ~ B.7F:		128 internal variables/bits (B.0 ~ B.10)

T.0 ~ T.F:		32 bytes for 16 delays

C.0 ~ C.F:		32 bytes for 16 counters

B.100 ~ B.4FF:	1024 internal variables/stored bit

# PC program structure

Operators for Programming

|  |  | Suffix | Operation on |
| --- | --- | --- | --- |
| E. | Input | 0-FF | bit |
| A. | Output | 0-FF | bit |
| S | Sequence | 1-9999 |  |
| EN. | Input | 0-1F | byte |
| AN. | Output | 0-1F | byte |
| B. | Internal variables (Initialization) | 0-7F | bit |
| B. | Internal variables | 80-FF | bit |
| I. | Immediate values (decimal) | 0-255 |  |
| M. | Numerical internal variables | 0-FF | byte |

Reserved variables (do not use)

B.0 to B.F : for intermediate calculations

M.0 to M.F :	for special assignment

##### Examples

- LD Loading of Accumulator A

Operator over bit.

ex.)	LD	E.1: read and loading in accumulator A of status of input 1.

If	E.1 = 0		bit 7 = 0

If	E.1 = 1		bit 7 = 1

ex.)	LD      B.10:	read and loading in accumulator of A of status of memory B.10.

B.F.

B.10

Operation over byte

| ex). | LD | EN.0 | : | Reading of input register 0 and storing in accumulator register |
| --- | --- | --- | --- | --- |
| ex). | LD | I. 128 | : | Loading of immediate value into accumulator A (decimal). |
| ex). | LD | I. $80 | : | Loading of immediate value into accumulator A (hexadecimal). |

2.	ST:  Storage of accumulator A in memory.

| ex). | LD | E.1 |  |
| --- | --- | --- | --- |
|  | ST | A.1 |  |
| ex). | LD | E.2 | E.2 ( (A) |
|  | ST | B.10 | (A) ( B.10 |
| ex). | LD | EN.3 | EN.3 ( (A) |
|  | ST | M.3A | (A) ( M.3A |

3.	AND:	Logic and between memory and accumulator A.

ex).

| LD | E.1 | E.1 ( (A) |
| --- | --- | --- |
| AND | E.2 | (E.1)(E.2) ( (A) |
| ST | B.10 | (A) ( B.10 |

| ex). | LD | EN.2 |
| --- | --- | --- |
|  | AND | EN.3 |
|  | ST | AN.4 |

| EN.2 = $79 | EN.3 = $85 | then | AN.4 = $01 |
| --- | --- | --- | --- |

| 0 1 1 1 | 1 0 0 1 | $79 |
| --- | --- | --- |
| 1 0 0 0 | 0 1 0 1 | $85 |
| 0 0 0 0 | 0 0 0 1 | $01 |

4.	OR	Logic OR between memory and Accumulator A.

EN.0 = $79

EN.1 = $85

AN.0 = (?)

5.	INV	Complement of A or M.

Exercise

EN.0 = $79

EN.1 = $85

AN.0 = (?)

# Text boxes

Index registers

(for indexed addressing modes)

Accumulator

Variable field

Input/output, DAC, ADC, timer, etc.

User program

PLC monitor

transfer if value other than stored value

INPUT/OUPUT board

## Bits working field

transfer of bit

TS0 ( TS0, TS1 ( TS0, TS2 (  TS0, TS3 ( TS0, TS4

TSO:	20 ms scanning

TS1-TS4:  100 ms/each

SP0-61

monitor

TF0

TF15

monitor

TS5

TS4

TS3

TS2

TS1

monitor

TS0

| b7 |  |  |  |  |  | b1 | b0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| operand |

### E.1

B.10

### E.2

(  )

A.1

(    )

### E.2

### E.3

(    )

E.3

E.2

E.1

### E.0

### A.1

(    )

EN.0      EN.1    AN.0