## Slide 1: Assessing the Thermochemical Properties of Organometallics
Andrew Devlin
Purdue University – Johnson Matthey
5/19/2026

## Slide 2: Organometallics
Molecules which contain one or more Carbon-Metal bonds
Unique reactivity and charge properties which allow for use as catalysts
Johnson Matthey (JM) produces many types of organometallics for the agrochemicals and pharmaceuticals industries
Common metal centers include palladium, platinum, iridium, etc.
Palladium allyl chloride dimer, a molecule of interest during this study

## Slide 3: Motivation
It is critical to understand heat of reaction (ΔHrxn ) to ensure safe process scale-up
ΔHrxn is difficult to measure. So, use heat of combustion (ΔHc) instead
Typically, direct testing methods such as bomb calorimetry are used
However, organometallics are very expensive: $1500-2000 per test, ~500 products in JM's Catalog
An accurate theoretical method of estimating ΔHc would be highly valuable to JM
December 7, 2007: An explosion at T2 Laboratories in Jacksonville, FL kills 4 and injures 32 – directly contributable to insufficient process scale-up knowledge

## Slide 4: Previous Work
Where was this project when I inherited it?
Previously, TCIT investigated as a thermochemical estimation tool:
1. DFT
  Used for modeling of metal centers in organometallics
  Not as accurate for ligands (carbon-based surroundings)
2. G4
  More accurate for ligands
  Cannot handle metals due to missing basis sets
  Computationally expensive
TCIT = DFT(Metal) + G4(Organic)
Showcased good accuracy, but process was cumbersome and time consuming
Instead, try using DFT to model the whole molecule!

## Slide 5: Density Functional Theory (DFT)
A quantum computational approach to estimate ΔHc for organometallics
Geometry Optimization
Energy Calculations
Parser Script
Direct Calculation of ΔHc
- Undergone if a crystal structure is unavailable
- Finds XYZ coordinates of all atoms in a molecule
- Computationally expensive
- Input: Crystal Structure
- Utilizes electron density functionals to solve for molecule energy
- Exponentially expensive for large molecules
- Reads energy solution found by previous step
- Outputs a gas-phase ΔHf value in kcal/mol
- Converts ΔHf to ΔHc
(still in gas-phase)
- Elemental composition used to predict combustion products
ΔHc=ΔHf(prod)-ΔHf(react)

## Slide 6: Project Objectives
Explore | Compute | Compare | Evaluate | Apply
-Identify organometallic molecules with experimental data -Explore multiple different metal centers and ligands | Run DFT calculations Obtain theoretical ΔHf & ΔHc | - Compare theoretical & experimental values - Calculate error for ΔHf & ΔHc | Assess DFT accuracy Analyze trends in classes of molecules Examine conservativeness of estimation | Where does DFT work well? Where does it fail? Implications for process safety, industrial use

## Slide 7: Explore
Five organometallic molecules with experimental data
(1,5-COD)PtCl2
Dichloro(1,5-cyclooctadiene)platinum
(MeNH2)2PtCl2
cis-Dichlorobis(methylamine)platinum
Pd Allyl Chloride Dimer
Di-μ-chlorobis(η3-2-propenyl)dipalladium
(MeCN)2PdCl2
Bis(acetonitrile)dichloropalladium (II)
Gen 3 BrettPhos

## Slide 8: Computation- ΔHf Results

## Slide 9: Computation- ΔHc Results

## Slide 10: Gen 3 BrettPhos – Case Study
Molecule is extremely bulky and did not run correctly
1. All cyclohexane rings substituted for methyl groups
2. All isopropyl groups eliminated
2nd Run: 44% error ΔHf, 1.8% error ΔHc
3. Removed an Ipso Carbon Interaction
3rd Run: 14% error ΔHf, 0.5% error ΔHc
The Best Result from this Study

## Slide 11: Analysis- The Effects of Phase-change Enthalpy
ΔHvap contributes very little to the errors observed!
Exactly how much does ΔHvap contribute to error?

## Slide 12: Analysis- Conservativeness of Results
An ideal tool is accurate. A safe tool overestimates.
Of the five molecules with experimental data:
  DFT provided overestimation of ΔHc in three cases
  One example of underestimation
  One example of near-perfect agreement
DFT demonstrates a tendency toward conservative estimation, but is not fully consistent

## Slide 13: Results of other Molecules Studied

## Slide 14: Iridium Errors
All Iridium-containing molecules resulted in output values blown out of proportion
May have resulted from poor basis set assumptions or coding errors in the workflow
Similar errors occurred when molecules were too large, causing computations to time out
Molecule Name and Structure | DFT ΔHf Estimate (kJ/mol)
Ir-92 | 2,741,097
Ir-93 | 4,553,551
Iridium Hexafluoride | 1,821,324 (~105 x the experimental value)

## Slide 15: Where Does DFT Show Promise?
Heat of Combustion ΔHc Predictions
  Showcased better agreement than ΔHf predictions
  Palladium-based molecules- best agreement
Ligand-Dominated Molecules
  Combustion product ΔHf are well-studied
  Gen 3 Brett Phos – 0.57% error
3. Process Safety
  DFT results skewed towards conservative estimation

## Slide 16: Challenges with DFT
Heat of Formation (ΔHf ) Predictions
  Significant deviation from experimental values
  Inconsistent magnitude and sign
Inconsistent Transition Metal Modeling
  Palladium (best) > Platinum > Ruthenium >>> Iridium (worst)
Incomplete Handling of Intermolecular Interactions
  Ex: Ipso-carbon interaction on 3rd Gen BrettPhos
  Solid-state interactions, crystallization energy, vaporization energy

## Slide 17: Key Takeaways
DFT showed mixed accuracy across the molecules studied
ΔHc predictions are generally more reliable than ΔHf
Large deviations in ΔHf highlight limitations in quantum modeling of organometallics
The method produced some conservative estimates, but not consistently
Performance is highly molecule-dependent, with worse results for certain metal centers and ligands

## Slide 18: Future Work
Improve Accuracy for Iridium Molecules
Hybrid Modeling Strategy
Expand Dataset
Improve Practical Relevance
-Test alternative basis sets
-Relativistic corrections
-Validation against experimental data
-Using G4 for ligands, DFT for metal centers
-Reduce cost & improve accuracy
-Target high energy functional groups
(nitro, small carbocycles, adamantane, etc.)
-Find more experimental data
-Implement automatic ΔHvap​ incorporation
-Align DFT output with experimental data
Friendly Cheat Sheet!
Adamantane
Small Carbocycle
Nitro Group
Notes: Pause at cheat sheet to list which molecule is which.

## Slide 19: Global Conclusion
DFT is a useful tool but is not currently a standalone solution for thermochemical prediction in organometallic systems.

## Slide 20: Acknowledgements
-Dr. Robert Higgins, Process Safety Chemist at Johnson Matthey
-Dr. Robert Woodman, Process Safety Leader at Johnson Matthey
-Dr. Ray Mentzer, Research Advisor
-Tyler Pasut, Savoie PhD Student

## Slide 21: Thank You Questions?

## Slide 22
Design Elements
Copy and paste as needed. Delete slide before presenting.