## Slide 1: LOPA and Quantitative Bowtie Analysis Recognizing both Preventive and Mitigative Safeguards

## Slide 2: Presenter
Jim McGlone
Technical Consultant and Chief Marketing Officer
Co-author of Security PHA Review for Consequence-based Cybersecurity
USN nuclear reactor operator and electronic technician on submarines
Nuclear Physics and Computer Technology undergraduate degrees, MBA international business
Rockwell Automation, Tridium (Honeywell), Ultra Electronics

## Slide 3: Risk Analysis Progression
In the beginning, there was HAZOP…
LOPA extended HAZOP through quantification of frequency
  Better resolution and analysis than qualitative only
  Allowed performance-based design processes such as IEC/ISA 61511
“Worksheet” presentation and highly numerical nature loses visual thinkers
Bowtie diagrams separately developed as method for visualizing risk scenarios
  Primarily used for important high-consequence scenarios
  Communicate risk to a variety of stakeholders
Example from Open PHA showing a HAZOP on top and a LOPA on bottom

## Slide 4: Overview
Layer of Protection Analysis (LOPA) is ubiquitous in process hazard analysis (PHA) and safeguard design
LOPA suffers from limitations
  One cause, one consequence
  Multiple causes required to aggregate risk (critical for SIS design)
  Multiple consequences required to design consequence mitigation measures
Unified Hazard Assessment developed to combine disparate risk analysis techniques
Quantitative Bowtie Analysis extends LOPA and addresses shortcomings
Unified Hazard Assessment
  PHA was initially “check the box” – minimum compliance and minimum cost
  Value found in PHA information, expanded to other purposes
    LOPA – for SIS safety integrity levels
    Hazard Registers – tracking and understanding of significant hazard scenarios
    Bowtie diagrams – visualization of hazard scenarios
  Maximizing usefulness of data developed during PHA will require changes in data structure and practices

## Slide 5: Typical Bowtie Diagram
PREVENTIVE
Event
MITIGATIVE
CONSEQUENCE(S)
CAUSE(S)
Example from Kenexis Bowtie

## Slide 6: Extended Bowtie Diagram for Degradation
CAUSE
DEGRADATION
PREVENTATIVE
Example from Kenexis Bowtie

## Slide 7: Early LOPA – One Cause - One Consequence
Example from an early LOPA book published by the AICHE

## Slide 8: Early LOPA in “Spreadsheet” Format
Example from Open PHA showing a LOPA worksheet
CAT = CONSEQUENCE CATEGORY
S = SEVERITY
TMEL = TARGET MAXIMUM EVENT LIKELIHOOD
IPL = INDEPENDENT PROTECTION LAYER
PFD = PROBABILITY OF FAILURE ON DEMAND
MEL = MITIGATED EVENT LIKELIHOOD
RFF = RISK REDUCITON FACTOR

## Slide 9: Mathematical Underpinning of LOPA
Frequencies and Probability are combined based on logic
Logical ‘AND’ – Probability Multiplication
  Relation between initiating event and independent protection layers
Logical ‘OR’ – Probability Addition
  Relation between multiple initiating events
Example from Kenexis Bowtie

## Slide 10: LOPA with Multiple Causes
Example from Open PHA showing LOPA with multiple Causes

## Slide 11: LOPA with Multiple Causes Converted to Quantitative Bowtie
Example from Kenexis Bowtie

## Slide 12: Handling Conditional Modifiers - One Consequence
Example from Kenexis Bowtie

## Slide 13: Multiple Consequences – Conditional Modifiers
Example from Kenexis Bowtie

## Slide 14: Handling Mitigative Safeguards Traditionally
Mitigative safeguards reduce but do not prevent consequence
Options
  Ignore safeguard – no credit taken
  Ignore consequence if safeguard is effective (residual consequence)
    Assumes that mitigative safeguard never fails
  Kludge together multiple LOPA scenarios, one for each consequence

## Slide 15: Quantitative Bowtie of Tank Dike Example
Examples from Kenexis Bowtie

## Slide 16: Analysis of Fire and Gas Detection
Mitigative Safeguard, ineffectiveness can stem from
  Probability of failure on demand of equipment
  Detection Coverage
  Mitigation Effectiveness
Example from ISA TR 84.00.07-2018 Guidance On The Evaluation Of Fire, Combustible Gas, And Toxic Gas System Effectiveness

## Slide 17: Calculation of Fire Detection Coverage
Example from Kenexis Effigy – fire & gas mapping software

## Slide 18: Quantitative Bowtie of Fire Detection/Deluge
Example from Kenexis Bowtie

## Slide 19: Conclusions
LOPA is ubiquitous and will continue to be used
Dump LOPA data to Bowtie using UHA to extend to meet the full range of required applications and use cases
Quantitative bowtie encompasses all current LOPA capabilities and expands to include multiple consequence outcomes
Quantitative bowtie allows for elegant assessment of effectiveness of mitigative safeguards
Quantitative bowtie provides a broader and more visual representation of risk scenarios