## Slide 1: Opportunities to enhance safe chemical manufacturing with electrochemical processes
Brian M. Tackett
Assistant Professor of Chemical Engineering
Purdue University

## Slide 2: About Me
Education & Background
BS Chemical Engineering, University of Pittsburgh (2009 – 2013)
PhD Chemical Engineering, Columbia University (2014 – 2019) Advisor: Jingguang Chen (Electrocatalysis & Sustainability)
NRC Post-Doctoral Fellowship, NIST (2019 – Aug. 2021) Advisor: Tom Moffat (Electrochemistry Fundamentals)
Asst. Prof. Chemical Engineering, Purdue University (Aug. 2021 – )

## Slide 3: Hazards of Industrial Oxidation Processes
Case Study: Ethylene Oxide Synthesis
Route 1: Direct Oxidation
  C2H4 + O2  C2H4O + CO2
  ~10% single pass conversion @ 200 – 260 C
    Higher T, above flammability limit
Route 2: Chlorohydrin Process
  C2H4 + Cl2 + H2O  + Ca(OH)2  C2H4O + CaCl2 + H2O
O
EO is a high-value, high-volume product with large CO2 footprint

## Slide 4: An Electrochemical Alternative
Case Study: Ethylene Oxide Synthesis
Chlorine mediator is generated electrochemically at an electrode by electron transfer from aqueous Cl- salt
Cl2 and H2O transform ethylene to EO in the same manner as chlorohydrin process
Resulting Cl- ions are recycled as mediators (no stoichiometric waste)
Occurs @ 90 C
O
Chung, M., Jin, K., Zeng, J. S., & Manthiram, K. (2020). ACS Catalysis, 10, 14015–14023.
Can we synthesize EO more efficiently without handling toxic chemicals or risking explosions?
Electrochemical reactors provide unique opportunity

## Slide 5: An Electrochemical Alternative
General Advantages of Electron-Driven Reactions
Driving force for chemical reaction = electrochemical potential (i.e. voltage)
  Facilitates ambient T processes
  Enables finer selectivity control
Reaction rate current
  Quantifies rates accurately (10-12 mol/s)
Electrodes are versatile
  Conduct charge to redox mediators
  Catalyze reaction directly (enhance activity/selectivity)
Chung, M., Jin, K., Zeng, J. S., & Manthiram, K. (2020). ACS Catalysis, 10, 14015–14023.
Electrochemical reactors provide unique opportunity
These enable selective oxidations that can potentially mitigate hazards in chemical processing

## Slide 6: Why, What, and How?
Why Now?
Electrochemical process have been around a long time
Rapidly increasing abundance of electrons originating from wind/solar are motivating electrification, broadly
Many great ideas from the past are now more economically/energetically attractive

## Slide 7: Why, What, and How?
What Do We Need to Realize This Vision?
Characterization:
Catalyst/reactor techniques developed over previous decades typically not suitable for gas-liquid-solid interfaces commonly found in electrocatalysis
Need: New/modified characterization techniques specifically designed for electrocatalysts (EC-MS, SEIRAS)
Reactor Configuration:
Electrocatalysts do not stand alone – they are influenced by: conductive current collector supports, gas diffusion layers, ion transport media (ionomer), electrolyte, membrane, etc.
Need: Holistic approach to reactor design/analysis
Education:
Chem/ChemEs are best suited to pursue these problems, but lack of training results in large depth/breadth of electrochem. manufacturing challenges to address
Need: Integrated curriculum that presents electrochemistry along with Chem/ChemE core
reactants
products
catalyst
Spectroscopy
reactants
products
electrocatalyst
Spectroscopy
Liquid electrolyte

## Slide 8: Why, What, and How?
How Am I Approaching These Challenges?
My lab has a unique combination of characterization techniques that enable study of a wide array of electron-driven chemical reactions

## Slide 9: Why, What, and How?
How Am I Approaching These Challenges?
My lab has a unique combination of characterization techniques that enable study of a wide array of electron-driven chemical reactions
Our department has collaborative and complementary faculty that enable multi-scale electrochemical reactor studies
  Electrochemcial alkane dehydrogenation enhances safety  thermodynamic advantages of oxidative dehydrogenation without mixing O2 + alkane.

## Slide 10: Summary and Opportunities
Electrochemical processes enable unique chemical manufacturing routes that could enhance process safety
Rapid influx of solar/wind motivate re-evaluation of electrochemical manufacturing
Realizing safe electrochemical process requires improvements in characterization/reactor configuration/education
My research approach is adaptable to broad range of electron driven chemistries that could improve safety of chemical manufacturing
Replace Cr-based reagents for C-H activation
Electrochemical H2SO4 synthesis
Electrochemical Claus Process to treat industrial gases (H2S  S)
Indirect/mediated halogenations
Potential opportunities to enhance chemical manufacturing with electrochemical processes