## Slide 1: Experimental Vs. Predicted Heats of Reaction for Some Common Reaction types in Pharma Industry
Katherine Young, Joseph Humes, Caitlin Justice & Professor Mentzer

## Slide 2: Agenda
Purpose
Relevant Theory
Reaction Set Results
  Debenzylation
  Bromination
  Boc Deprotection
  Suzuki
  T3P
  Halogenation
Conclusions and Future Work

## Slide 3: Partnership with Industry
Data Collection and Collaboration
Notes: Still work with JM?

## Slide 4: Purpose
Model heats of reaction of various pharmaceutical reaction classes
  Prove efficacy of programs through comparison with experimental data
  Reduce scale-up testing required
Expand TCIT molecular library
  Collaboration with Professor Savoie and Qiyaun Zhao (PhD candidate)
Reveal shortcomings and opportunities in CHETAH’s capability to model complex reactions

## Slide 5: Relevant Theory
CHETAH
Commercially available program widely known and used in industry
Licensed by ASTM since 1974 and marketed as a method to predict reactive/explosive hazards of pure chemicals or mixtures
Calculates heats of formation through Benson’s method of group additivity (BGIT)
  Heat of formation of individual groups summed
  Requires Benson group substitutions for unknown groups
    Largest source of error
Simple user interface that accepts ‘smile’ strings
Benson, S. W.; Buss, J. H. Additivity Rules for the Estimation of Molecular Properties. Thermodynamic Properties. J. Chem. Phys. 1958.

## Slide 6: Relevant Theory
TCIT: TAFFI* Component Increment Theory
Novel program with constantly expanding library
Python based with flexible data inputs
Combines quantum chemistry methods and G4 component contributions
  Corrects for contributions from adjacent atoms as well as two positions away
  Uses consistent rules to generate new components and parameterization data
Requires no substitutions or adjustments to molecules
Accepts variety of inputs (xyz, ‘smile’)
*Topology Automated Force Field Interactions–another method developed by the Savoie group.
Zhao, Q.; Savoie, B. M. Self-Consistent Component Increment Theory for Predicting Enthalpy of Formation. J. Chem. Inf. Model. 2020.

## Slide 7: Modelling Difficulties: Reaction Complexity
CHETAH TCIT
Limited Benson groups available
  Often several component substitutions per molecule
  Cannot work with less common elements (P, S, etc)
  Gas phase Benson groups might be only available
Manual ring corrections required
  Fused rings
  Non-carbon elements in rings
  Placement of cyclic system in more complex structure
Small ionic species library available
Cannot handle radical species
Currently not able to handle charged and free-radical species as well as fused rings (in development)

## Slide 8: Modelling Difficulties: Reaction Complexity - 2
General Reaction Complexities
Unknown side-coupling, side reactions
Gas phase products
Intermolecular forces
Heat of Dosing- reagents combined at various temperatures
Acid-base
  Use highest heat of reaction, not always a reasonable assumption
Heat of dissolution
Intellectual property among collaborators
± 20% from experimental values considered modelled successfully

## Slide 9: Comparison of Complex Reaction Heats
Heat of Reaction of Debenzylation
Reaction | Measured ΔHrxn (-kJ/mol) | CHETAH ΔHrxn (-kJ/mol) | TCIT ΔHrxn (-kJ/mol) | % Diff CHETAH | % Diff TCIT
 | 116.1 | 119.00 | 102.90 | 2.50 | 11.37
 | 114 | 91.00 | 88.93 | 20.18 | 21.99
 | 436 | 244.87 | 266.86 | 43.84 | 38.79
 | 210 | 197.63 | 188.78 | 5.89 | 10.10

## Slide 10: Comparison of Complex Reaction Heats - 2
Heat of Reaction of Bromination
Reaction | Measured ΔHrxn (-kJ/mol) | CHETAH ΔHrxn (-kJ/mol) | TCIT ΔHrxn (-kJ/mol) | % Diff CHETAH | % Diff TCIT
 | 79 | 93.06 | 73.23 | 17.80 | 7.30
 | 106 | 80.77 | 127.90 | 23.80 | 20.66
 | 79 | 88.46 | 73.63 | 11.97 | 6.80
 | 136 | 205.10 | 122.47 | 50.81 | 9.95

## Slide 11: Comparison of Complex Reaction Heats - 3
Heat of Reaction of Boc Deprotection- amine protection
Reaction | Measured ΔHrxn (-kJ/mol) | CHETAH ΔHrxn (-kJ/mol) | TCIT ΔHrxn (-kJ/mol) | % Diff CHETAH | % Diff TCIT
 | 138 | -234.13 | 140.50 | 269.66 | 1.81
 | 52.10 | -50.85 | 55.48 | 197.59 | 6.48
 | 72.8 | -39.65 | 53.60 | 154.46 | 26.37
 | 30.8 | -54.55 | -61.32 | 277.10 | 299.08

## Slide 12: Comparison of Complex Reaction Heats - 4
Heat of Reaction of Suzuki- carbon bond formation
Reaction | Measured ΔHrxn (-kJ/mol) | CHETAH ΔHrxn (-kJ/mol) | TCIT ΔHrxn (-kJ/mol) | % Diff CHETAH | % Diff TCIT
 | 252.4 | 205.90 | 234.48 | 18.42 | 7.10
 | 193 | 174.11 | 356.12 | 9.79 | 59.23
 | 120.1 | 738.42 | 301.42 | 514.83 | 150.97
 | 356 | 266.80 | 309.25 | 25.06 | 13.13

## Slide 13: Comparison of Complex Reaction Heats - 5
Heat of Reaction of T3P- phosphoric reagent, facilitates bond formation
Reaction | Measured ΔHrxn (-kJ/mol) | CHETAH ΔHrxn (-kJ/mol) | TCIT ΔHrxn (-kJ/mol) | % Diff CHETAH | % Diff TCIT
 | 178 | 150.38 | 209.49 | 15.52 | 17.69
 | 189 | 188.00 | 185.66 | 0.53 | 1.77
 | 149.6 | 152.38 | 177.00 | 1.86 | 18.32
 | 197.8 | 185.92 | 184.51 | 6.01 | 6.72

## Slide 14: Comparison of Complex Reaction Heats - 6
Heat of Reaction of Halogenation
Reaction | Measured ΔHrxn (-kJ/mol) | CHETAH ΔHrxn (-kJ/mol) | TCIT ΔHrxn (-kJ/mol) | % Diff CHETAH | % Diff TCIT
 | 122.9 | 166.41 | -49.43 | 35.41 | 140.22
 | 162 | 145.44 | 164.84 | 10.22 | 1.75
 | 196 | 202.98 | 160.79 | 3.56 | 17.97
 | 126 | 84.25 | 131.06 | 33.13 | 4.02

## Slide 15: CHETAH
Chart: Experimental (kJ/mol)
| 116.1 | 114 | 436 | 210
Debenzylation | 119 | 91 | 244.87 | 197.63
Bromination | 93.06 | 80.77 | 88.46 | 205.1
Suzuki | 205.9 | 174.11 | 266.8
T3P | 150.38 | 188 | 152.38 | 185.92
Halogenation | 166.41 | 145.44 | 202.98 | 84.25
line | 0 | 450

## Slide 16: TCIT
Chart: Experimental (kJ/mol)
| 116.1 | 114 | 436 | 210
Debenzylation | 102.9 | 88.93 | 266.86 | 188.78
Bromination | 73.23 | 127.9 | 73.63 | 122.47
DeBoc | 140.5 | 55.48 | 53.6
Suzuki | 234.48 | 356.12 | 301.42 | 309.25
T3P | 209.49 | 185.66 | 177 | 184.51
Halogenation | 164.84 | 160.79 | 131.06
line | 0 | 450
* Removed reaction #1 from halogenation and reaction #4 from DeBoc

## Slide 17: Conclusions
TCIT tended to calculate within 20% with a few key exceptions
  High accuracy with no substitutions required
    Error present can be accounted for in reaction complexity
  Minimal corrections
CHETAH
  Greater experience with the program allows for more accurate group substitutions
  Depending on reaction complexity, able to achieve reasonable first approximation

## Slide 18: Future Work
Finalizing last reaction set: sulfide to sulfone
Summarizing work for potential publication
TCIT
  Continue to expand program with even broader range of chemicals and components
    Adding capability for ionic and free-radical groups
CHETAH
  Continue to experiment with substitutions to find interactions with greatest effect
  Potential for new capabilities

## Slide 19: Thank you Questions?

## Slide 20: References
Benson, S. W.; Buss, J. H. Additivity Rules for the Estimation of Molecular Properties. Thermodynamic Properties. J. Chem. Phys. 1958. https://doi.org/10.1063/1.1744539.
Zhao, Q.; Savoie, B. M. Self-Consistent Component Increment Theory for Predicting Enthalpy of Formation. J. Chem. Inf. Model. 2020. https://doi.org/10.1021/acs.jcim.0c00092.