## Slide 1: When and Why do We Use ADT24 to Assess Thermal Risk?
Shasha Zhang
Process Hazard Evaluation, Chemical Process Development
Bristol-Myers Squibb (BMS)
P2SAC Fall 2022 Conference
Dec 14th -15th 2022

## Slide 2: Brief Introduction of BMS PHE Group
Where we are
Oversight of process safety testing for any production > 20 L
Hazard evaluation and testing for chemical process
Guidance on safety program at partners and support for tech transfer
Process Hazard Evaluation
CPD
Lab & KL
Vendors
Discovery
EHS
CSO
Clinical Supply Operation
EM
External Manufacturing
Dust and other testing associated with chemical hazards
Drug Substance Operations and Supply
CPD
What we do
Who we support
Notes: More content for our group

## Slide 3: Stoessel Criticality
Stoessel Criticality is widely used by many pharmaceutical companies to evaluate thermal risk.
ADT24, also known as TMR24 and Td24, is the temperature at which decomposition reaches its maximum rate in 24 hours under adiabatic condition
Acceptable risk
Stoessel Diagram
Tad: Adiabatic Temperature Rise
MTSR : Maximum Temp Synthesis Reaction – usually Tp + Tad
NOT allowed
Notes: Clear definition of our operation range.
ADT24 -TD24 TMR24
Screening: equation. apply margine
How to calculate MTSR: 0% accumulation;
ADT24: equation – over estimate- report as ADT24 from DSC; AKTS; VSP; catalytical decom- isothermal DSC.
Safety margin: MTSR –heat of reaction 120%

## Slide 4: When is ADT24 needed to address thermal risk?
Tad: Adiabatic Temperature Rise
TMR: Time to Maximum Rate
ADT24/TMR24 is the temperature at which decomposition reaches its maximum rate in 24 hours under adiabatic condition
Risk = Probability x Severity
Severity – Screening will provide some ideas
  High Tad Decomp > 200 oC
  Medium 50 oC < Tad Decomp <200 oC
  Low Tad Decomp < 50 oC
Probability – Based on decomposition kinetics
  Low TMR > 24 hrs
  Medium 8 hr > TMR < 24 hr
  High TMR < 8 hr
ADT24 /TMR24 as a probability indicator is triggered if the severity is medium to high
Notes: TMR represents critical time constant for effectiveness of safety measures.

## Slide 5: When is ADT24 needed to address thermal risk?
Practical procedure
Determine
energy
potential
Energy from DSC?
Process presents
no thermal risks
Assess probability of
triggering
Decomposition (ADT24)
Assess Criticality by
comparing
MTSR and ADT24
< 100J/g
>100J/g
Risk = Probability x Severity
Severity – Screening will provide some ideas
  High Tad Decomp > 200 oC
  Medium 50 oC < Tad Decomp <200 oC
  Low Tad Decomp < 50 oC
Probability – Based on decomposition kinetics
  Low TMR > 24 hrs
  Medium 8 hr > TMR < 24 hr
  High TMR < 8 hr
ADT24 /TMR24 as a probability indicator is triggered if the severity is medium to high
No need to waste resources!
Tad > 50°C
Notes: TMR represents critical time constant for effectiveness of safety measures.
Low risk low severity

## Slide 6: When to Study ADT24 at BMS?
Onset > 200 °C
Onset =< 200 °C
Heat < 100J/g
100 J/g <= Heat <= 200 J/g
Heat > 200 J/g
Kinetics / heat flow?
ADT24
Low risk
Temp <=200 °C, heat > 200 J/g (Tad of 100 °C) ADT24
Temp <=200 °C, heat < 100 J/g (Tad of 50 °C) No need
Energetic /Explosive?
Further study
No
Yes
Slow
Fast
Simple decision tree based on DSC data if no significant gas evolution
Notes: 50 C

## Slide 7: Is the Study of ADT24 Needed?
BMS coupound
Energy: 157 J/g; onset: 64°C
Energy: 107 J/g; Onset 124 °C
Vendor suggested a ADT24 of 40 °C.
No need to study ADT24
20 wt% DBDMH in DMF
ADT24 is determined to be 34°C.
For some marginal cases, thermogram needs to be reviewed to evaluate the necessity

## Slide 8: How to Determine ADT24
Kinetic approaches
  Isoconversion method: DSC/AKTS (Advanced Thermal Analysis Software)
  Adiabatic calorimetry
Run DSCs
Estimate Ea and A
Predict time to maximum rate
Directly measure the kinetic curve
Extrapolate the beginning of the curve
Used by BMS

## Slide 9: How to Determine ADT24
  Estimation approaches
  Traditional ‘safety Margin’ approach - ‘Distance rule’;
    Tsafe = Tonset – X oC
  Equation-based estimation
    Use onset temperature and instrument detection limit assuming Ea= 50 kJ/mol & zero-order kinetics
    Empirical equation for DSC:
Onset temperature as input
Usually overly conservative
Employed by some vendors
Stoessel, F., Thermal Safety of Chemical Processes
NOT BMS preferred approaches
May cause confusion
Used by Legacy Celgene, but labelled as preliminary ADT24
DEKRA/Chilworth
Notes: Tsafe is differently from ADT24.
These are not method BMS is using!!!

## Slide 10: Example 1: Production of an Early Intermediate
A production of 250 kg of intermediate was executed at vendor’s plant.
Desired reaction: RC1 data shows an adiabatic temperature rise of 41 °C.
DSC on distillation stream shows an exotherm of -312J/g from 131 °C. ADT24 is 43 °C based on equation-based estimation by a vendor.
MAT (Maximum Achievable Temperature)
MTSR (Maximum Temperature of Synthetic Reaction)
MAT =MTSR = Tp + Tad
= 67 °C > ADT24 Criticality 5
Tb = 64.7°C
Distillation Temp of 45 °C > ADT24
High risk
Data collected by BMS Partner
Notes: MSTR: worst case scenario

## Slide 11: Example 1: Internal DSC/AKTS Study
A better method is needed to quantify ADT24.
DSC on product shows an exotherm of -410 J/g with an onset of 116 °C.
DSC/AKTS analysis shows ADT24 is 82 °C.
Product is not isolated so ADT24 is considered conservative
MAT =MTSR = 67 °C.
ADT24 is determined as 82 °C
Tb = 64.7°C
Tb< MTSR < ADT24 Criticality 3
Distillation Temp of 45 °C < ADT24
Acceptable risk

## Slide 12: Example 1: Risk Mitigation Overview
MAT =MTSR = 67 °C
ADT24 is estimated to be 43 °C.
MTSR > ADT24 Criticality 5
Distillation Temp of 45 °C > ADT24
High risk
Importance of ADT24 study
MAT =MTSR = 67 °C.
ADT24 is determined as 82 °C
Tb = 64.7°C
Tb< MTSR < ADT24 Criticality 3
Distillation Temp of 45 °C < ADT24
Acceptable risk
An overly conservative estimate of ADT24 may greatly affect assessment on safety.
The ADT24 provided by vendors may lead to confusion – it is highly recommended to contact safety specialist for clarification.
Notes: Green bucket optional

## Slide 13: Example 2: Thermal Stability of Rxn Mixture
An early intermediate was produced on a commercial scale.
The condensation is endothermic with a Tad of -12 °C.
C80 data of reaction mixture shows an exotherm with an enthalpy of -420 J/g and an onset of 135 °C.
Other ARSST and ARC tests confirmed that the exotherm poses a safety concern.
Heating rate: 0.5 K/min
Sample mass: 479mg
Notes: How long does the reaction take?

## Slide 14
 | Sample used | Phi | Onset Temp | ADT8 | ADT24
ARSST | 10 mL | ~1.05 | 140 °C | 124 | 115
C80+AKTS | 2 mL | - | 136 °C | 118 | 104
Phi Tec II | 50 mL | 1.14 | 135 °C | 118 | 109
ARC (BMS) | 5 mL | 1.27 | 123 °C | 117 | 110
ARC (vendor) | 3 mL | 1.91 | 131 °C | 115 | 104
If ’50 K safety margin’ or ‘equation-based estimation’ approach is used, the process temp will probably be set around 76 °C, which is too low for the reaction to run.
Consistent results of ADT24 were obtained from different kinetic methods.
Combining with reaction calorimetry data, the criticality index of the process is rated as “2” in Stoessel system.
The process was safely implemented at commercial scale.
Example 2: Summary of ADT24 study

## Slide 15: Example 3: ADT24 Study of Tetrahydroxydiboron
Tetrahydroxydiboron has been used in many BMS projects.
ADT24 study is important due to its fast decomposition rate and large energy (~1600J/g)
Onset temperature is in the range of 95 -125 ºC depending on experimental condition.
ADT24 is in a narrower range of 70-82 ºC, indicating ADT24 is a more reliable parameter to set the maximum operation temperature limit.
DARC data collected by D. Vanyo
Estimation of ADT24 using onset temperature may introduce larger variability.

## Slide 16: Summary
When to study ADT24?
ADT24 as a probability indicator is triggered if the severity of decomposition is medium to high.
  Simplified answer: an exotherm energy > 100 J/g below 200 °C.
Why to use ADT24?
Using an overly conservative estimate of ADT24 may greatly affect the assessment on safety.
  Simple screening test with distant rule or equation-based estimation may be used by BMS vendors.
A real kinetic study of ADT24 delivers reasonable safety margin.
    Kinetic approaches are preferred by BMS
    Kinetic approaches provide realistic ADT24, and have been demonstrated by many portfolio projects at BMS.
ADT24 is a more reliable parameter to set maximum operation temperature.
  Estimation of ADT24 using onset temperature may introduce larger variability.

## Slide 17: Acknowledgement
Simon Leung, Tao Chen, Douglas Mcleod, Mark Lindrud, Junying Fan, Buck Holloway, Melanie Miller, Paul Fernandez, Nicolas Cuniere, Fransisco Gonzalez Bobes, Chris Sfouggatakis, Dimitri Skliar, Subha Mukherjee, Bahar Inankur, Patrick Sipple, Ketleine Georges, Chris Tickner, Dale Vanyo, Alan Fritz, Steven Chan
BMS partner’s safety group and project team for safety study.