## Slide 1: Protecting Bare-metal Embedded Systems With Privilege Overlays
Abraham A. Clements, Naif Saleh Almakhdhub, Khaled S. Saab,
Prashast Srivastava, Jinkyu Koo, Saurabh Bagchi, and Mathias Payer

## Slide 2: Bare-Metal Systems
Systems without an OS
Constraints
  Small memory sizes
    1 MB Flash, 128 KB’s of RAM
  Tight run-time constraints
  Low power requirements
Single Application
  No kernel/user space seperation
Examples
  Amazon’s Dash button
  Smart door locks
  Engine controllers
  SD card controllers
  WiFi SoC’s
Security left out
Notes: Emphasis
Mention Project Zero WiFi findings

## Slide 3: Default: No Defenses
Security Hardware
Global Data
Stack
Code
Bare-metal Application
Unused or trivially bypassed
Vulnerable to:
Stack smashing
Code injection
Global data corruption
IO
Always accessible
Single (Root)
execution domain
No ROP defenses
Sensitive IO
RAM
Flash
Notes: All have same memory configuration
Can be used to corrupt application/hardware
Any bug is fatal

## Slide 4: Defense Challenges
Single application
  No separation privilege levels (e.g. kernel, user)
Systems lack a MMU
  Defenses are limited to physical memory space
Small memory sizes
Tight run-time constraints
Notes: Small Memory- Little entropy can’t add very much

## Slide 5: EPOXY Embedded Privilege Overlay across X hardware for Y software
LLVM based compiler
Protects against
  Code injection
  Control flow hijacking
  Data corruption
  Direct manipulation of IO
Privilege Overlays
  Creates two privilege levels
  Foundation for other defenses
EPOXY
LLVM-based
compiler
Hardened
Application
Source
Code
Sensitive IO
Notes: Forward Reference that will cover all in detail in presentation

## Slide 6: Threat Model And Requirements
Threat Model
Arbitrary memory corruption
Attacker goals:
  Obtain execution
  Corrupt specific global data
Does not have physical access
Requirements
Hardware support for two execution privilege modes
Memory Protection Unit (MPU)
  Hardware that enforces access permissions on physical memory
Memory usage determined a priori

## Slide 7: Before Epoxy
Code
Global Data
Stack
IO
Application
Security Hardware
Sensitive IO
Privileged Execution

## Slide 8: Privilege Overlay
Creates multiple privilege levels
  Enables developer to assume access to everything
  Restricts privileged operations at run-time
Static analysis identifies privileged operations
  Specific instructions defined by the ISA that require privileges
  Sensitive memory mapped registers (e.g., MPU configuration , sensitive IO)
Created by injecting code to:
  Configure MPU – Enforce DEP and restrict access to sensitive registers
  Reduce privileges of entire application
  Request privileges for restricted operations
  Handle privilege requests

## Slide 9: Privilege Overlay Example
#define UART_RX=0xdeadbeef
char menu_option;
...
menu_option = *(UART_RX)
switch (menu_option):
case ’1’:
handle_case_1;
break;
...
#define UART_RX=0xdeadbeef
char menu_option;
...
request privileges;
menu_option = *(UART_RX)
drop privileges;
switch (menu_option):
case ’1’:
handle_case_1;
break;
...
menu_option = *(UART_RX)
drop privileges;
Unprivileged Execution
Privileged Execution
Default
Privilege Overlay

## Slide 10: Epoxy – After Privilege Overlay
Code
Global Data
Stack
IO
Hardened Application
Security Hardware
Sensitive IO
Enabled enforcing DEP
Access Restricted
Access Restricted
Unprivileged Execution
Privileged Execution
Set to RX
Providing Code Integrity
Set to RW-NX
Stopping Code Injection

## Slide 11: SafeSTack
SafeStack from Code Pointer Integrity *
  Protects against stack smashing
  “Unsafe” variables moved to separate stack
  We adapted to bare-metal systems
* V. Kuznetsov et al., Code Pointer Integrity, OSDI 2014
RAM
Stack
.data
.bss
heap
Stack
UnSafeStack
Guard Region
UnSafeStack
.data
.bss
heap
Notes: Unsafe, used in pointer arthmetic that can’t be proved to be safe, escapes the current bounds. Only functions which have functions which use unsafe variables are use unsafestack frame.

## Slide 12: Diversification
Further protects against ROP attacks
Corruption of specific global data
EPOXY
Source
Code
Seed
Binary 1
Binary 2
Binary 3
Binary 4
Seed 1
Seed 2
Seed 3
Seed 4

## Slide 13: Diversification
Further protects against ROP attacks
Corruption of specific global data
RAM
.data
.bss
heap
Stack
UnSafeStack
A
B
D
A
B
C
D
.data
B
b
d
c
a
a
c
b
d
.bss
C
1
2
4
3
Flash
foo
bar
baz
bar2
foo2
handler
Jumps to handler
Binary 1
invalid execution
E
Padding
Stack
UnSafeStack
heap
handler
foo
foo2
bar2
bar
baz

## Slide 14: Epoxy – All Protections
Code
Global Data
Stack
IO
Hardened Application
Security Hardware
Sensitive IO
Enabled enforcing DEP
Access Restricted
Access Restricted
UnSafeStack
Isolated “Unsafe” Locals
Stack Smashing Protection
ROP Protections
Global Data Protected
ROP Protections
Unprivileged Execution
Privileged Execution
Set to RX
Providing Code Integrity
Set to RW-NX
Stopping Code Injection
Notes: Tie to Desktop

## Slide 15: Performance
 | SS | PO | All
Min | -7.3% | -1.3% | -11.7%
Ave | -3.5% | 0.1% | 1.1%
Max | 4.4% | 2.1% | 14.2%
SS - SafeStack Only, PO - Privilege Overlay Only
IoT Apps Runtime
IoT Apps Energy
BEEBs Runtime
 | SS | PO | All
Min | -4.2% | -10.3% | -10.2%
Ave | 0.2% | -0.2% | 2.5%
Max | 7.3% | 2.8% | 17.9%
BEEBs Power

## Slide 16: ROP Compiler
Used ROPgadget compiler* to identify gadgets across 1000 variants
  Gadget survives if same instructions (ending with a branch) at same address
 |  | # Surviving Across |  |  |  | 
App | Total | 2 | 5 | 25 | 50 | Last
PinLock | 294K | 14K | 8K | 313 | 0 | 48
FatFS-uSD | 1,009K | 39K | 9K | 39 | 0 | 32
TCP-Echo | 676K | 22K | 9K | 985 | 700 | 107
* J. Salwan, ROPgadget, http://shell-storm.org/project/ROPgadget/
Notes: Emphasis max only, get message that attacks do not scale across

## Slide 17: Privileged Instructions Executed
App | Tool | Exe | Priv | Priv %
PinLock | EPOXY | 823K | 1.4K | 0.17%
 | FreeRTOS-MPU | 823K | 813K | 98.78%
FatFS-uSD | EPOXY | 33.3M | 3.9K | 0.01%
 | FreeRTOS-MPU | 34.1M | 33.0M | 96.77%
TCP-Echo | EPOXY | 310M | 1.5K | <0.001%
 | FreeRTOS-MPU | 322M | 307.0M | 95.34%
Notes: FreeRtos – standard embedded, not default

## Slide 18: Conclusion
Fast forwards bare-metal security three decades
Provides state-of-the-art protection for bare-metal systems
    Does not require rewriting application
    Provides strong stack protections, via an adapted SafeStack
    Minimizes number of privileged instructions executed
    Diversifies all memory
Meets requirements for run-time, memory, and energy
Open Sourced: https://github.com/HexHive/EPOXY