## Slide 1: ACES: Automatic Compartments for Embedded Systems
Sandia National Laboratories is a multimission laboratory managed and operated by National Technology & Engineering Solutions of Sandia LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525. SAND2018-8907 C
Abraham A. Clements
clemen19@purdue.edu
Naif Saleh Almakhdhub,
nalmakhd@purdue.edu
Saurabh Bagchi
sbagchi@purdue.edu
Mathias Payer
mathias.payer@nebelwelt.net

## Slide 2: Problem Statement
Bare-metal IoT devices/ SoC’s are vulnerable
  Google P0’s Broadcom SoC
  CVE-2017-6957
Legacy code
  IoT devices, vehicles, etc.
No defenses
  Even DEP is missing
  No separation of privileges
Bare-metal Application
Application Logic
Image
Proc.
TCP
Stack
Camera
HAL
WIFI
HAL
Serial
Coms
Signal
Proc.
UART
HAL
Camera
2.4Ghz Radio
UART
ADC
ADC
HAL
Privileged code
Hardware peripheral
Result: Single vulnerability compromises the entire system

## Slide 3: ACES Overview
ACES creates many compartments
  Applies least privileges
  Creates sub-thread compartments
  Protects integrity of sensitive data and peripherals
Uses static analysis to automatically infer compartments using a policy
Separates compartmentalization from application development
Each compartment has associated data/peripherals
Compartmented Application
Application Logic
Image
Proc.
TCP
Stack
Camera
HAL
WIFI
HAL
Serial
Coms
Signal
Proc.
UART
HAL
Camera
2.4Ghz Radio
UART
ADC
ADC
HAL
Compartmented unprivileged code
Hardware peripheral
Comp.
Switcher
Privileged code

## Slide 4: Related Work
EPOXY – DEP, diversity, and stack protections for bare-metal systems
  Does not address least privileges
  Clements A. A. et al. Oakland 2017 (Our work)
Mbed uVisor – runtime and API to manually create compartments
  Intermixes source and compartmentalization policy
  Requires Mbed OS
  https://www.mbed.com/en/technologies/security/uvisor/
MINION – Creates thread level compartments on micro-controllers
  Fixed algorithm used to determine compartments
  Kim, C. H. et al. NDSS 2018

## Slide 5: Compartments
Set of concurrently accessible memory regions and authorized control-flows between them
Compartments restrict
  Accessible memory
  Control-flow between compartments
Memory Regions
Control-flow
Function
Code
Data
Peripheral
Accessible for compartment
B
A
Comp B
Comp A
Region 2
Region 1
Peripherals
RAM
Code
GPIO
CAMERA
UART
WIFI
Comp A
Comp B
OnBtn
TcpTx
TakeImg
TxImg
Notes: Compartment is collection of memory regions and authorized control flow transfers.
Compartments data and code.

## Slide 6: Creating Compartment
Static analysis identifies code, data, and peripheral dependencies
  ACES ensures compartments can access all required data and peripherals
  Mirco-Emulator used to dynamically identify missed due to dependencies aliasing
Compartments are code centric
  i.e. code belongs to only one compartment
Policy determines how functions, global variables, and peripherals are grouped to create compartments
Different policies possible
  We evaluate: Naïve Filename, Optimize Filename, and Peripheral policies
MPU is used to restrict access to memory regions

## Slide 7: Program Dependency Graph
void OnBtn()
GPIO.led = ON
CAMERA.pwr = ON
g_btn = PUSHED
TakeImg()
TxImg()
void TakeImg()
CAMERA.take_pic = 1
g_image.buf = CAMERA.rx_reg
GPIO.led = OFF
void TxImg()
g_tx_state = ACTIVE
TcpTx(g_image.buf)
g_image.sent = TRUE
void TcpTx(*buf)
GPIO.led_tx = ON
WIFI.tx_reg = buf
g_tcp_stats.tx_count++
g_tx_state = IDLE
OnBtn
TcpTx
TakeImg
TxImg
CAMERA
GPIO
WIFI
g_tx_state
g_btn
g_tcp_stats
g_image
Notes: P1, F1, G1 for variables

## Slide 8: Region Graph
TakeImg
OnBtn
TcpTx
TxImg
PDG mapped to a Region Graph
Functions 1:1
  Control edges not transferred
Data 1:1
  Data edges transferred
Peripherals 1:Many
  Unique region created per dependency edge
WIFI
GPIO
CAMERA
GPIO
CAMERA
GPIO
OnBtn
TcpTx
TakeImg
TxImg
CAMERA
GPIO
WIFI
g_tx_state
g_btn
g_tcp_stats
g_image
g_tx_state
g_tcp_stats
g_image
g_btn

## Slide 9: Compartmentalization Policy
g_image
g_btn
g_btn,
g_image
g_tx_state
g_tcp_stats
Defines what should be grouped to form compartments
Implemented policies
  Naïve Filename
  Optimized Filename
  Peripheral
  Many more are possible
TakeImg
OnBtn
WIFI
GPIO
TcpTx
TxImg
CAMERA
GPIO
CAMERA
GPIO
TxImg,
TcpTx

## Slide 10: Optimize
g_btn,
g_image
Improve security
Improve performance
g_tx_state
g_tcp_stats
WIFI
GPIO
CAMERA
GPIO
CAMERA
GPIO
TakeImg
OnBtn
TxImg,
TcpTx
TakeImg,
OnBtn

## Slide 11: Lowering
Reduces graph to meet HW constraints
  Degree of each code regions must be less than the number of MPU regions
Lowest cost regions merged until constraints are met
Lowing may increases permissions of compartments
Merging peripherals may capture additional peripherals
g_btn,
g_image
CAMERA
GPIO
TxImg,
TcpTx
WIFI
GPIO
TakeImg,
OnBtn
g_tx_state
g_tcp_stats
g_tx_state,
g_tcp_stats
UART,GPIO,
CAMERA,WIFI

## Slide 12: Mapping to Memory
A
B
Comp B
Comp A
Region 2
Region 1
Peripherals
RAM
Code
GPIO
CAMERA
UART
WIFI
Region 1
g_btn,
g_image
CAMERA
GPIO
Comp. B
TxImg,
TcpTx
Comp. A
TakeImg,
OnBtn
Region 2
g_tx_state,
g_tcp_stats
UART,GPIO,
CAMERA,WIFI

## Slide 13: Restricting Control-Flow
Instrument calls and returns crossing compartment boundaries
  Invoke compartment switcher
Compartment switcher authenticates both directions
  Memory permissions only changed for valid transitions
Comp. Switcher
Comp A
Comp B
Call
Return
OnBtn
TcpTx
TakeImg
TxImg
OnBtn
TxImg

## Slide 14: Micro-Emulator
Emulates store instructions in software
  Overcomes limitations of static analysis in generating PDG
  Authenticated writes outside a compartment’s regions
Dynamic profiling run creates white-list of accesses per compartment
Used for stack protection
Previous Stack
RO
RW
New Locals
MPU Permissions
Stack Memory Space

## Slide 15: Evaluation
Evaluated policies for security, runtime, resource usage
  Naïve Filename
  Optimized Filename
  Peripheral
Five applications run on Cortex-M4
  PinLock
  FatFs-uSD
  TCP-Echo
  LCD-uSD
  Animation

## Slide 16: PinLock Case Study
Attacker trying to unlock lock
Assume write-what-where vulnerability in HAL_UART_Receive_IT
 | Overwrite |  | Control Hijack | 
Policy | Global | GPIO | Direct | Deputy
Naïve Filename | ✔ | ✔ | ✔ | ✔
Opt. Filename | ✔ | ✔ | ✔ | ✔
Peripheral | ✘ | ✔ | ✘ | ✘

## Slide 17: Runtime Evaluation
Can have moderate runtime impact
Emulating instructions accounts for largest increase in execution time

## Slide 18: Memory OverhEad
Flash Overhead
RAM Overhead
Notes: Runtime: Compartment Switcher, Micro-Emulator

## Slide 19: Conclusion
Applies least privileges bare-metal IoT devices
  Does not require changes to application logic
  Uses existing hardware
ACES automatically creates and enforces sub-thread
  Decouples security policy from application
  Frees developer from having to manage underlying security hardware
  Enables research in creating compartmentalization policies
Code will be available at:
https://github.com/embedded-sec/ACES