## Slide 1: Combination
Reference: Chapter 9 (3rd Ed.) of Sound Systems: Design and Optimization, by Bob McCarthy (Elsevier, 2010 / 2017)

## Slide 2: Outline
Array building
Role of overlap as a shaping tool
Role of asymmetry as a shaping tool
Basic idea
  Coupled arrays
  Uncoupled arrays
Spectral variance effects
  Coupled line source arrays
  Coupled point source arrays
  Uncoupled line source arrays
  Uncoupled point source arrays
  Uncoupled point destination arrays
Minimum variance coverage shapes

## Slide 3: Array Building
Two principal beamwidth shapes suitable for array building
  2nd-order “plateau” type that flattens out in the high frequencies (“constant directivity”) – provides consistent unity splay angle
  highly sloped 3rd-order elements useful in highly overlapped coupled array configurations (no consistent unity splay angle)
  (1st-order speakers best suited for “standalone” applications rather than array building)

## Slide 4: Review: Beamwidth Shapes

## Slide 5: Array Building
Ability to fill simple symmetrical shape evenly makes 1st-order speaker leader in horizontal coverage applications
Foremost application of 3rd-order speakers is creation of asymmetric arrays, which make it the leader in vertical applications
Middle ground are 2nd-order speakers, which have applications in both H and V planes (but in limited quantities)

## Slide 6: Role of Overlap as a Shaping Tool
If we array two speakers together, what will be the combined coverage angle?
  combined angle can range from half as wide to twice as wide
  decisive factor: percentage overlap
  control of overlap
    angular (point in different directions)
    displacement (moving elements apart)
  low overlap: elements retain much of their individual character (yet merge to make “sculpted shapes” unique to combined arrays)
  high overlap: individual elements disappear and merge into combined shape of a “new and different” single speaker
  overlap is the “shaping tool”

## Slide 7: “Quiz”
Four speaker combination question: What is the combined coverage angle?

## Slide 8: “Quiz”
Four speaker combination question: What is the combined coverage angle?

## Slide 9: Limitations of Combined Shapes
Will use aspect ratio icons in layout form to visualize individual contributors (works well where isolation zone summation is dominant, not so well when coupling or combing zone summation is dominant)
Note that beam concentration and ripple variance aspects of the combined response are not apparent in the simple icon representation

## Slide 10
What asymmetries are available to the array designer?
Why are asymmetries necessary?
Which asymmetries are static (i.e. fixed)?
Which asymmetries are dynamic (i.e. modifiable while in operation or even as a function of program material)?
Takeaway: DSP changes the rules on array beamforming
Role of Asymmetry as a Shaping Tool

## Slide 11: Basic Idea – Coupled Line Source Arrays
Stack the “aspect ratio icons” end-to-end (for side-by-side speakers)
Combined shape of fully-coupled line source can be visualized as a forward extension by means of simple additions of the aspect ratio shapes
Recall: Beamwidth of a single speaker approaches 90 when the transmitted  equals the radiating cone size (blue line in figure). Beamwidth is wider if  > cone size (green line) and narrower if  < cone size (red line).
For a coupled line source, vertical coverage is 72 when the transmitted  equals the line length (e.g. beamwidth for a 2m long array will be 72 at 170 Hz).
Note that equations relating line length to beamwidth assume omnidirectional (“point”) sources.

## Slide 12: Coupled Line Source – FAR Multiplication
Combined coverage angle is found once the array has fully formed at the top of the parallel pyramid.

## Slide 13: Basic Idea – Coupled Point Source Arrays
Arrange the aspect ratio icons side-by-side around a virtual point source (based on unity splay angle)
Combined shape will strongly resemble the radial spread of the individual FAR patterns as long as the amount of combing zone interaction is low

## Slide 14: Coupled Point Source Arrays: Aspect Ratio to Radial Coverage Extension

## Slide 15: Coupled Point Source Arrays: Combined Shapes of Minimum Level Variance
constant speaker order, unity splay angle, constant level
constant speaker order, 60% overlap splay angle, constant level

## Slide 16: Asymmetric Level Scaling
size of icon reduced by 50% for each reduction in level by 6 dB

## Slide 17: Combined Shapes with Asymmetric Level Scaling
technique of partial overlap mixed with level tapering called “layering”

## Slide 18: Combined Shapes with Asymmetric Level Scaling
constant speaker order and splay angle, tapered level
mixed speaker order with splay angle tapered to provide constant overlap ratio, tapered level

## Slide 19: Basic Idea – Uncoupled Arrays
The best way to deal with overly wide coverage shapes is spread multiple sources (uncoupled arrays)
Combined shape can be seen as a lateral extension by means of simple stacking of the aspect ratio shapes
The combined aspect ratio becomes wider (while not becoming longer) and therefore lower in number
FAR is found by dividing the single element FAR by the number of elements

## Slide 20: Uncoupled Line Source Arrays: Combined Shapes

## Slide 21: Uncoupled Line Source Arrays: Combined Shapes
4-element second-order array with 0º splay angle, matched line of origin, constant lateral spacing, and levels
5-element second-order array with 14º splay angle, matched line of origin, constant lateral spacing, and levels

## Slide 22: Compensated Unity Spacing

## Slide 23: Uncoupled Point Destination Arrays

## Slide 24: Spectral Variance of Coupled Arrays
Possible outcomes of beam combinations
  beam concentration (coupling zone overlap)
  beam spreading (isolation zone)
  “passing through each other” (combing zone)

## Slide 25: Spectral Variance of Coupled Line Source Arrays
Representative element
Length effects
Spacing (displacement) effects
Beamwidth shapes
Quantity effects
Pyramid effects
Speaker order effects
Level tapering effects

## Slide 26: Coupled Line Source Element

## Slide 27: Coupled Line Source Length Effects
Line length = 2.76m (one  @ 125 Hz).The coverage angle is about 70 (regardless of quantity) when the line length equals the wavelength. The coverage angle is reduced by half when  equals half the line length.

## Slide 28: Coupled Line Source Element Spacing Effects
Spacing effects for 1/3 , 2/3 , 3/3 , and 4/3 .
Side lobes become strong at element spacing beyond 2/3 .

## Slide 29: Coupled Line Source Beamwidth Shapes

## Slide 30: Coupled Line Source Element Quantity Effects
Coverage pattern narrows as quantity rises
Ratio of spectral variance is unchanged by quantity (as long as line length stays the same)
Beam concentration is the primary driving force in the interactions
Larger quantities give appearance of reduced spectral variance if the range of viewing does not extend far enough for coupling to occur over the full frequency range

## Slide 31: Coupled Line Source Element Quantity Effects

## Slide 32: Coupled Line Source Element Quantity Effects

## Slide 33: Coupled Line Source Element Pyramid Effects
Note high spectral variance vs. distance away from array – “pink shift” as we approach the array (due to “moving axially inside the pyramid”). Moving radially, there is high spectral variance relative to angle off axis.

## Slide 34: Coupled Line Source Speaker Order Effects
Line length is dominant force at lower frequencies (where line length ≥ /2)
Side lobes vary with order but main lobes still matched at mid frequencies
At high frequencies, low-order array coverage degenerates into ripple, while high-order array maintains focus

## Slide 35: Coupled Line Source Level Tapering Effects
(Symmetric) level (i.e. amplitude) tapering effectively reduces the number of elements contributing to the pyramid
Behavior mimics an array of shorter length
Aside – frequency dependent amplitude tapering is not considered in text, nor is delay tapering (accomplished using digital signal processing and delay techniques)

## Slide 36: Coupled Line Source Level Taper Effects
THIS IS NOT HOW YOU WOULD NORMALLY DO LEVEL TAPERING ON A LINE ARRAY

## Slide 37: Spectral Variance of Coupled Point Source Arrays
Beamwidth shapes
Splay angle effects
Level taper effects
Speaker order effects

## Slide 38: Coupled Point Source Beamwidth

## Slide 39: Coupled Point Source Beamwidth

## Slide 40: Splay Angle Effects
Even a small splay angle creates an opportunity for reduced spectral variance (that cannot be found in a coupled line source… unless DSP techniques are used)
Isolation (even in small measure) will counteract pattern narrowing

## Slide 41: Coupled Point Source Splay Angle Effects

## Slide 42: Coupled Point Source Splay Angle Effects

## Slide 43: Asymmetric Coupled Point Source Arrays
Reference points
  center (on axis): angular orientation of the longest distance covered by the array
  top/bottom (off axis): -6 dB points along the target shape, above and below center
  total (TTL): the combined angular spread from top to bottom
Symmetry percentage (“amount of asymmetry”): the ratio of angular coverage above and below center
  level taper
  splay (angle) taper
  mixed loudspeaker orders
  lateral spacing/level offset
  forward spacing/level offsets
  hybrid coupled line/point source arrays

## Slide 44
Level taper bends the minimum variance line and raises the acoustic beam center relative to the geometric center.
Asymmetric Coupled Point Source Arrays

## Slide 45
Asymmetric Coupled Point Source Arrays
Level taper bends the minimum variance line and raises the acoustic beam center relative to the geometric center.

## Slide 46: Splay Angle Effects
16 coupled 3rd order speakers
32 degree overall angle spread, 1 octave,
22 x 120 meters
Hybrid Coupled Line/Point Source Array
Line Source
Point Source
Coverage shapes
Gap
8 kHz
Where would a “gap” in the coverage shape be useful?

## Slide 47: Uncoupled Arrays
Line source
Point source
Point destination

## Slide 48: Lateral Spacing and Level Effects
Symmetric Uncoupled Line Source Array
6 uncoupled 1st order speakers (90) 1/6th octave 12 x 24 meters
Minimum Variance Zone
2 kHz
8 kHz
125 Hz
500 Hz
Notes: Fig 6.38b

## Slide 49: Lateral Spacing and Level Effects
Asymmetric Uncoupled Line Source Array:
Log spacing and level offsets
0 dB
-6 dB
-12 dB
-18 dB
2 kHz
8 kHz
125 Hz
500 Hz
4 x 1st order (90) Spacing is tapered by 50% as level is reduced by 6 dB 1/6th octave 21 x 42 meters
Notes: Fig 6.38b

## Slide 50: Lateral Spacing and Level Effects
Asymmetric Uncoupled Line Source Array:
33% Angular Overlap
5 uncoupled 2nd order speakers @ 2.5m spacing ( 13.5 deg of 40), 1/6th octave 12 x 24 meters
125 Hz
500 Hz
2 kHz
8 kHz
Notes: Fig 6.38b

## Slide 51: Forward Spacing and Level Effects
Asymmetric Uncoupled Point Destination Array:
Offsetting level & distance ratio effects
Single
2:1
4:1
8:1
2nd order speakers Main spkr @ 40m to crossover. Delays @ 20 m (-6 dB), 10m (-12dB) & 5m (-18 dB) respectively 1/6th oct, 6 x 40 m
Notes: Fig 6.38b

## Slide 53: Delay Coverage: 0 degrees
0 degree angle between Main and Delay

## Slide 54: Delay Coverage: 15 degrees
15 degree angle between Main and Delay

## Slide 55: Delay Coverage: 30 degrees
30 degree angle between Main and Delay
30 degree angle between Main and Delay

## Slide 56: Delay Coverage: 60 degrees
60 degree angle between Main and Delay

## Slide 57: Delay Coverage: 90 degrees
90 degree angle between Main and Delay
90 degree angle between Main and Delay

## Slide 58: Conclusions
First-order speakers
  most suitable for single-element applications with a low proximity ratio
  least suitable for angular overlap
  least suitable for combination (power addition)
  beamwidth must not widen as frequency rises (once plateau reached must remain constant)
  should be arrayed at or near unity splay angle based on beamwidth plateau

## Slide 59: Conclusions
Second-order speakers
  most suitable for single-element applications with a medium proximity ratio
  suitable for combination (power addition) on a limited basis
  no beamwidth reversal (widening as frequency increases)
  should be arrayed at or near unity splay angle based on beamwidth plateau

## Slide 60: Conclusions
Third-order speakers
  least suitable for single-element applications
  most suitable for angular overlap
  suitable for combination (power addition)
  constant downward beamwidth slope (with no reversals) as frequency increases
  should be arrayed at an angle greater than 0º (relative)

## Slide 61: Conclusions
Power capability
  coupled arrays can increase concentrated power capability beyond a single element while maintaining minimum variance over long distances
  the coupled point source has the highest ratio of increased power to variance over the widest frequency span and spatial area
  the coupled line source can provided “unlimited” power but is incapable of minimum spectral variance over the space

## Slide 62: Conclusions
Power capability
  asymmetric level tapering will decrease the overall power capability at the geometric center of the array but provide the opportunity for minimum variance over an asymmetric space
  uncoupled arrays can increase distributed power capability beyond a single element while maintaining minimum variance, but only over a very limited distance

## Slide 63: Minimum Variance Coverage Shapes
Rectangle: individual speaker
Arc: symmetric point source
Right triangle: asymmetric coupled point source

## Slide 64: Minimum Variance Principles
Single speakers
  position the speakers with the lowest possible proximity ratio to the audience in at least one plane
  use speakers that have minimum beamwidth ratio over frequency (1st or 2nd order)
  match the properties of symmetry
  match speaker aspect ratio to audience coverage shape
  if speaker coverage pattern overlap on to room surfaces is too strong, use an array instead

## Slide 65: Minimum Variance Principles
Symmetric point source coupled arrays
  fill the arc angle required to fit the shape of the audience area (number of elements required will depend on speaker order)
    low-order speakers must have minimal overlap
    high-order speakers can be overlapped for power addition
  beam spreading will shape (widen) the HF coverage
  beam concentration will shape (narrow) the LF coverage
  apply these principles to make shapes meet in the mid-range

## Slide 66: Minimum Variance Principles
Uncoupled arrays
  achieve isolation by angular offset and/or displacement
  as angular offset falls, the usable depth range falls as well
  uncoupled array depth is initiated by overlap
    before overlap, response is as a single element
    after overlap begins, array behavior and ripple variance begin
  uncoupled array depth is limited by overlap – multiple overlap provides the ending limit for depth
  uncoupled arrays can be scaled by relative level to appropriate depth