## Slide 1: Foundations
of Audio Engineering
Reference: Chapter 1 (3rd Ed.) of Sound Systems: Design and Optimization, by Bob McCarthy (Elsevier, 2017)

## Slide 2: Outline
The acoustic decibel
Good sound
  Context and complications
  Quality factors
Audio transmission
Relationship of time, frequency, and wavelength
How sound propagates
Environmental effects (temperature and humidity)
The waveform
Sound power levels and electrical power requirements
Amplitude and phase response
Coverage angle / beamwidth
Pistonic approximation of cone loudspeaker radiation

## Slide 3: Acoustic Decibel (dB-SPL)
In acoustics, the ratios most commonly encountered are changes in pressure level, measured in dB-SPL:
As distance from a sound source doubles, the dB-SPL decreases 6 dB (this is called the inverse square law)
Adding/subtracting dB levels:
Doubling acoustic power corresponds to a 3 dB increase in SPL
Doubling perceived loudness corresponds to a 10 dB increase in SPL
dB-SPL = 20 log10(p/po) where po = 20 N/m2
SPLa  SPLb = 10 log10 [ 10 db-SPLa/10  10db-SPLb/10]

## Slide 5: Good Sound: Context and Complications
Outdoor concert
  Context:
    portable
    deep/wide/irregular coverage area, necessitating multiple arrays and delay zones
    high power/SPL
  Complications:
    instability of temperature gradient (due to weather and/or daytime vs. nighttime)  affects sound refraction and array aiming, necessitating a dynamic beamsteering mechanism
    overlap areas in array coverage subject to combing  necessitating tight array directivity control
    wind  causes comb filtering effects

## Slide 6: Acoustic Environment Outdoors
SPL decreases 6 dB for every doubling in distance
Sound energy dissipates due to mechanical effects (greater dissipation at higher frequencies)
Relative humidity affects sound absorption (greater at higher frequencies)
Temperature gradient affects sound refraction
Ground surface causes reflection and absorption of sound

## Slide 7: Good Sound: Context and Complications
Indoor concert
  Context:
    fixed installation or portable “touring” (more likely)
    large coverage area, necessitating multiple arrays and delay zones
    high power/SPL
  Complications:
    room geometry and surface treatments may exacerbate unwanted reflections and excessive reverb  intelligibility issues
    temperature gradient more stable (than outdoors), but may shift seasonally (summer vs. winter)  delay compensation
    overlap areas in array coverage causes comb filtering effects  necessitating tight array directivity control and careful aiming
    variable audience fill effects, seat characteristics

## Slide 8: Acoustic Environment Indoors
The sound arriving at a listener’s ears has (at least) three distinct divisions:
  direct sound
  early reflections
  reverberant sound
The direct sound undergoes no reflections and follows inverse-square-law level change (-6 dB per doubling of distance)
The reverberant sound tends to remain at a constant level if the sound source continues to put energy into the room at a regular rate

## Slide 9
Sound paths in a concert hall
Time relationship of direct and reflected sounds
Comparison of direct, early, and reverberant sound fields in an auditorium

## Slide 10: Acoustic Environment Indoors
This gives rise to several basic sound fields:
  near field
  free field
  reverberant field
The near field is typically defined to be within a distance of twice the largest dimension of the sound source
In the (far) free field, inverse-square-law level change prevails
In the reverberant (diffuse) field, sound energy density is nearly uniform
far field
Critical distance (Dc)
Sound fields in an enclosed space

## Slide 11: Good Sound: Context and Complications
Home theater
  Context:
    small room with combination of reflective and absorptive surfaces
    typically surround sound (5.1 or 7.1)
    low/moderate power/SPL
  Complications:
    room geometry and surface treatments can cause LF (subwoofer) room modes
    reflective surfaces can cause HF comb filtering effects
    good directivity control needed for stable “sweet spot” (panoramic angle)
    neighbors

## Slide 12: Good Sound: Quality Factors
frequency range/response, “smoothness”
SPL at (furthest) listening position
headroom (“Crest factor”)
evenness of coverage (spectral and spatial stability)
intelligibility (articulation loss of consonants)
ratio of direct sound field to reverberant sound field
gain before feedback
noise (SNR) and distortion (IM and THD)
transient response and damping factor
group delay (frequency-dependent arrival times)
locality of reference

## Slide 13
Audio Transmission

## Slide 15
= C/F
C is speed of sound at ambient conditions

## Slide 16: How Sound Propagates

## Slide 19
The Waveform
For loudspeakers, + pressure is compression, - pressure is rarefaction

## Slide 20
Relative Phase
Stretching transient response due to frequency-dependent phase shift is also called “time smearing”

## Slide 21
Frequency-Dependent Phase Delay

## Slide 22
Phase Offset (Between 2 Loudspeakers)
Note the difference between phase shift (within single device) vs. phase offset (between devices or systems) – here, LF ranges match but HF range offset by 180

## Slide 23
Time Offset (Between 2 Loudspeakers)
1 ms time offset (signal delay) between two matched speakers

## Slide 27: Sound Power Levels
Sound power levels (dB-PWR) are calculated as:
The standard reference for power in audio work is 0.001 watt (1 milliwatt), called 0 dBm, which corresponds to 0.775 volt across 600  (the “VU meter” reference)
Example: The power in watts corresponding to +30 dBm is:
dB-PWR = 10 log10[ (acoustic power) / 10-12 watt ]
30 dBm = 10 log10[ x / 10-3] = 10 log10[x103]
= 10 log10 [x] + 10 log10 [103]
= 10 log10[x] + 30
0 = 10 log10[x]  x = 1 watt

## Slide 29: Electrical Power Requirement
When SPL goal at a given listening distance known, also need:
  Sensitivity rating of loudspeaker (typically spec as 1m on-axis with input of 1 electrical watt)
  Acoustic level change/attenuation between loudspeaker and farthest listening position
Example: 90 dB program level at listening distance of 32 m outdoors
  Loudspeaker sensitivity measured as 110 dB
  Acoustic level change = 20 log (32)  30 dB
  Add 10 dB for peak (program level) headroom
  SPL required at source is 90 + 30 + 10 = 130 dB
  Need 20 dB above 1 watt, or 10 (20/10) = 100 W

## Slide 33
Coverage Angle / (6 dB) Beamwidth

## Slide 34
Coverage angle C< (H / V) = 6 dB Beamwidth
Polar pattern
Equal level (isobaric) contours (“isobars”)
Directivity factor (Q)
Directivity index (DI) = 10 log Q (also known as “front to back ratio”)
Beamwidth vs. frequency
3D “balloons”
Common Representations of Loudspeaker Coverage

## Slide 36
“CONSTANT DIRECTIVITY”
Loudspeaker Directivity / Beamwidth

## Slide 37
Loudspeaker Beamwidth Light Analogy

## Slide 38
Think of piston as consisting of a large number of very small elements of size S – each one of these elements is observed from distance r
Piston radiation into half-space (e.g., a cone-type loudspeaker mounted in an “infinite” baffle)
Pistonic Approximation of Cone Loudspeaker Radiation
Piston has radius a and is observed from distance r relative to its center at an angle  relative to its central (“Z”) axis
 Observation point

## Slide 40
3.83
In general, want ka  3.83 for a cone radiator, where k = 2f/c
Examples: For 12” woofer, want f  1378 Hz
For 4” midrange, want f  4134 Hz
central lobe only
pair of out-of-phase side lobes
additional pair of in-phase side lobes

## Slide 41
Directivity Pattern of Flat Piston for 3 Different Frequencies
Here, the wavelength  is 4x the diameter of the piston (cone)
Examples: 12” cone loudspeaker operating at 283 Hz or a 4” speaker operating at 848 Hz
Recall that a is the radius of the loudspeaker  its diameter is 2a

## Slide 42
Directivity Pattern of Flat Piston for 3 Different Frequencies
Here, the wavelength  is equal to the diameter of the piston (cone)
Examples: 12” cone loudspeaker operating at 1130 Hz or a 4” speaker operating at 3390 Hz
Recall that a is the radius of the loudspeaker  its diameter is 2a

## Slide 43
Directivity Pattern of Flat Piston for 3 Different Frequencies
Here, the wavelength  is ¼ the diameter of the piston (cone)
Examples: 12” cone loudspeaker operating at 4520 Hz or a 4” speaker operating at 13,560 Hz
Recall that a is the radius of the loudspeaker  its diameter is 2a

## Slide 44: Single 4-inch Loudspeaker

## Slide 45: Single 4-inch Loudspeaker @ 500 Hz

## Slide 46: Single 4-inch Loudspeaker @ 1000 Hz

## Slide 47: Single 4-inch Loudspeaker @ 2000 Hz

## Slide 48: Single 4-inch Loudspeaker @ 4000 Hz

## Slide 49: 32-Element Array of 4-inch Drivers

## Slide 50: 32-Element Array @ 500 Hz

## Slide 51: 32-Element Array @ 1000 Hz

## Slide 52: 32-Element Array @ 2000 Hz

## Slide 53: 32-Element Array @ 4000 Hz

## Slide 54: “Home Stereo” Multi-way System

## Slide 55: “Home Stereo” Multi-way System

## Slide 56: “Home Stereo” Multi-way System

## Slide 57: “Home Stereo” Multi-way System

## Slide 58: “Home Stereo” Multi-way System

## Slide 59: “Home Stereo” Multi-way System

## Slide 60: “Home Stereo” Multi-way System