## Slide 1: Summation
of Audio Signals and Acoustic Waves
Reference: Chapter 4 (3rd Ed.) of Sound Systems: Design and Optimization, by Bob McCarthy (Elsevier, 2017)

## Slide 2: Outline
Properties of Audio Summation
Response Ripple
Acoustical Crossovers
Speaker Arrays
Speaker/Room Summation

## Slide 3
Summation Criteria: Matched Origin
Signal 1
Signal 2
Summed Signal
Signal 1
Signal 2
Summed Signal

## Slide 4
Summation Criteria: Matched Origin
Signal 1
Signal 2
Summed Signal
Signal 1
Signal 2
Summed Signal
?

## Slide 5
Summation Criteria: Multiple Input Signals
Summed Signal
Signal 1
Signal 2
Signal n
Signal 3
Signal 4

## Slide 6
Summation Criteria: Input Signal Direction

## Slide 7
Summation Criteria: Overlap Duration
Summed Signal
S 2
S 1
S 2
S 1
Summed Signal
No addition/subtraction
Addition/subtraction during overlap duration

## Slide 8: Adding dB-SPL
dB-SPLa+b =
20 log10 [sqrt { (10dB-SPLa/20)2 + (10dB-SPLb/20)2
+ 2(10dB-SPLa/20) (10dB-SPLb/20)(cos(a-b))} ]
Two acoustic sources “a” and “b” of relative phase angles a and b

## Slide 9: Adding dB-SPL – “Simplifications”
If both sources are at 0 dB and phase angle a = 0 (i.e., same level, only relative phase angle varies), simplifies to:
dB-SPLa+b = 20 log10 [ sqrt { 2 + 2cos(-b) } ]
If both sources are in phase and only the relative level varies (where source “a” is 0 dB, simplifies to:
dB-SPLa+b = 20 log10 [1 + 10dB-SPLb/20 ]

## Slide 11
Acoustic Addition & Subtraction: Level vs. Phase
two identical signals summed at same level

## Slide 12
Acoustic Addition & Subtraction: The Phase Wheel
two identical signals summed at same level

## Slide 13
Summation: Response Ripple
Time offsets shift all frequencies by the same amount of time
Time offsets shift all frequencies by a different amount of phase
Result of summation with time offset (of signals at same frequency) is response ripple

## Slide 14: Acoustic Addition and Subtraction: Level Offset Effects
Relative Phase=0
Relative Phase=180
Max Ripple

## Slide 15: Summation Zones Defined
Coupling zone
  Sources within ±1/3 wavelength (±120º)
  Amount of addition ranges from 0 to 6 dB depending on phase/level offset
  Ripple is ±3 dB
  Most easily achieved at low frequencies due to large wavelengths

## Slide 16: Summation Zones Defined
Cancellation zone
  Effects only subtractive
  Phase offset ±150º to ±180º
  Ripple ±50 dB

## Slide 17: Summation Zones Defined
Combing Zone
  Phase offset reaches point where subtraction begins (> ±120º)
  Less than 4 dB level difference
  Characterized by addition at some frequencies and dips at others
  Ripple ranges from ±6 dB to ±50 dB
  To be avoided – highest form of variance over frequency

## Slide 18: Summation Zones Defined
Combining Zone
  Level offset ranges from 4 dB to 10 dB
  Semi-isolated state relative to sources, which limits the magnitude of addition/cancellation
  Ripple no more than ±6 dB

## Slide 19: Summation Zones Defined
Isolation Zone
  10 dB or more of level offset
  Relative interactions steadily reduced and eventually become negligible
  At large level offset, relative phase has nominal effect
  Ripple does not exceed 6 dB

## Slide 20: Acoustic Addition and Subtraction: Level Offset Effects
Relative Phase=0 deg
Max + Min = Ripple
Combining Zone
4 to 10 dB Level Offset
Combing Zone
< 4 dB Level Offset
Isolation Zone
> 10 dB Level Offset
Relative Phase=180
Coupling Zone
0 to -10 dB, 0 to -120 phase

## Slide 21: Acoustic Addition and Subtraction: Level Offset Effects
Relative Phase=180 deg
Relative Phase=0 deg
Level Range based on Relative Phase
Combing
Isolated
Combining

## Slide 22: Summation

## Slide 26: Application: Undamped Pipe
loudspeaker mounted in a rigid (undamped) pipe 3 feet in length, open at one end, observed on-axis from “speaker end” (for now will ignore pipe resonance and only consider phase)
3 feet

## Slide 27: Application: Undamped Pipe
how does sound propagate at low frequencies?
3 feet

## Slide 28: Application: Undamped Pipe
how does sound propagate at low frequencies?
3 feet

## Slide 29: Application: Undamped Pipe
if operated at 150 Hz, how much phase shift occurs as the wave traverses the pipe?
3 feet

## Slide 30: Application: Undamped Pipe
if operated at 150 Hz, how much phase shift occurs as the wave traverses the pipe? wavelength = 7.53 feet; phase shift = (360x3)/7.53 = 143 degrees
3 feet

## Slide 31: Application: Undamped Pipe
what will be level of “combined” signal at source?
3 feet

## Slide 32: Application: Undamped Pipe
what will be level of “combined” signal at source?
total “round trip” phase shift = 180+143+143=466
(106 degrees net); combined level will be +1.7 dB
3 feet

## Slide 33: Application: Undamped Pipe
if frequency changed to 100 Hz, what will be combined level at source?
3 feet

## Slide 34: Application: Undamped Pipe
if frequency changed to 100 Hz, what will be combined level at source? wavelength is 11.3 feet; phase shift traversing pipe 96 degrees; round trip phase shift is 371 (nearly “in phase”); combined level is +5.95 dB
3 feet

## Slide 35
Application: Flanging vs. Phasing
Flanging is a delay effect used in recording studios since the 1960s
Effect obtained by summing outputs of two reel-to-reel tape machines playing copies of the same recording
Touching the flange on one of the supply reels slows it down (relative to the other machine), creating a time delay (phase offset) between the two machines
Subsequently touching the flange on the supply reel of the other machine (and releasing the first one) will cause the delay to gradually disappear, then grow in the other direction

## Slide 36
Application: Flanging vs. Phasing
Echo is not perceived because the delays are relatively short (typically 1-10 ms)
Flangers provide uniformly spaced filter notches, which may cause a discernable pitch to the effect and/or a periodic tone to disappear  therefore provide best effect with inharmonic (non-periodic) sounds
Flanging creates a rapidly varying high-frequency sound by adding a signal to an image of itself that is delayed by a short, variable amount of time (typically 0 to 10 ms)
Demo: https://www.youtube.com/watch?v=r7jhRoZ4NgQ

## Slide 37
Application: Flanging vs. Phasing
A phaser (or phase shifter) is a close cousin of a flanger, where the spacing between filter notches is non-uniform
The phaser effect is obtained by replacing the delay line of the flanger with a string of all-pass filters
Unlike a comb filter, all-pass filters do not change the amplitudes of the individual frequency components, but does have a substantial effect on the phase of individual frequency components (“frequency dispersion”)
The phaser effect is most audible on the transient response (attack or decay of a sound)
Demo: https://www.youtube.com/watch?v=Ici_YOVDl_0

## Slide 38
Response Ripple: Spatial Distribution
Time offsets between two sources vary over the space
Relationship between the sources and summation destination is triangular
Different types of triangles reveal the variation tendencies

## Slide 39
Factors Affecting Response at Summation Point
Level offset due to distance offset (inverse square law)
Level offset due to polar response (frequency and angular dependent)
Phase offset due to path length difference

## Slide 41: Pythagorean Problem: Level Offset is a Ratio, Time Offset is a Difference
4
5
3
Relative Level: 8/10 = 0.8 (-2dB)
Relative Time: 10-8 = 2.0 (2 ms)
C
A
B
8
10
6
Relative Level: 4/5 = 0.8 (-2dB)
Relative Time: 5-4 = 1.0 (1 ms)

## Slide 44
Summation Example Key Features
Maximum addition over all frequencies at center of isosceles triangle (coupling zone)
1 KHz and 10 KHz show deep cancellations around the right triangle point (combing)
10 KHz is first to show reduced combing as move into obtuse triangle (isolation zone)
Area inside isosceles triangle (acute) has highest degree of variation over position/frequency (combing)
Isolation increases as obtuse angle increases
100 Hz pattern does not show cancellation at the right angle position (displacement between sources is less than a wavelength)

## Slide 46
The Acoustic Crossover
Meeting point of two (or more) correlated input signals at comparable levels
Separated by frequency in the same (or separate) enclosure
Separated over a matched range in separate enclosure
Separated by a physical boundary (The Room)

## Slide 47
Divider/Crossover Terminology
Spectral divider: electronic device that separates the response into multiple frequency bands for transmission through distinct loudspeakers
Spectral acoustic crossover: frequency range where equal acoustic levels are found from each of the electronically/physically separated elements that converge there
Spatial divider: electronic or acoustic device that separates response into multiple channels of common frequency range for transmission through distinct loudspeakers
Spatial acoustic divider: location where equal acoustic levels are found from the multiple electronically/physically separated elements that converge there

## Slide 49
The Acoustic Crossover: Quantified
Crossover class
Crossover slope (order)
Degree of symmetry
Number of elements
Combined response

## Slide 50
Gap
Unity
Overlap
Crossover Classes
Combined Shapes
Individual Shapes
Coupling Zone
Crossover Point

## Slide 51: Crossover Slope Order
3rd
(18 dB)
2nd
(12 dB)
1st
(6 dB)
Combined Shapes
Individual Shapes
Coupling Zone
Crossover Point

## Slide 52: Asymmetric Crossover Levels
- 6 dB
- 3 dB
0 dB
Combined Shapes
Individual Shapes
Coupling Zone
Crossover Point
1st Order Slopes

## Slide 53: Asymmetric Crossover Slopes
1st / 3rd Order
1st / 2nd Order
1st / 1st Order
Combined Shapes
Individual Shapes
Coupling Zone
Crossover Point

## Slide 55: The Spectral Crossover

## Slide 56: The Spectral Crossover

## Slide 58
Spectral vs. Spatial Crossovers
Common ground:
Both interactions governed by properties of acoustic summation
Strategies for achieving optimal summation rooted in same concept: the phase-aligned crossover
Differences:
Spatial crossover can run through the full audio range – much more difficult to isolate with cancellation
Relative phase in a spatial divider affects all frequencies, while phase change in spectral divider only affects frequency range of crossover

## Slide 59
Spectral vs. Spatial Crossovers
Analogous functions (“duality”):
Position in room where two speakers share equal level is analogous to spectral divider crossover frequency (coupling zone)
Directional control capability of speaker analogous to spectral divider slope – highly directional speaker is like a steep spectral crossover

## Slide 60
Spectral vs. Spatial Crossovers
Analogous functions (“duality”):
Change in relative level between speakers becomes a change in position of the spatial crossover point – analogous to crossover frequency shift in spectral divider that results from changing the relative driver level
Power addition capability that comes from H or V overlap in the spatial crossover analogous to useable overlap in the crossover frequency of spectral divider

## Slide 64
Spatial Crossover Classes
Crossover class varies with distance:
Gap: A+B < 0 dB
Unity: A+B = 0 dB
Overlap: A+B > 0 dB

## Slide 65
Gap
Unity
Overlap
Crossover Classes
Combined Shapes
Individual Shapes
Coupling Zone
Crossover Point

## Slide 66: Spatial Crossover Classes
Gap
(X+X=<0dB)
Unity
-6 + -6 =0dB
Overlap
(X+X=>0dB)
Combined Shapes
Individual Shapes
Coupling Zone
Crossover Point

## Slide 67: Spatial Crossover Classes vs. Frequency
Gap
Unity
Overlap
Combined Shapes
Individual Shapes
Coupling Zone
Crossover Point
3rd Order Speakers
10 kHz
1 kHz
100 Hz
10 kHz
1 kHz
100 Hz

## Slide 68
Combined Shapes
Individual Shapes
Coupling Zone
Crossover Point
3rd Order (18 dB)
2nd Order
(12 dB)
1st Order (6 dB)
Spatial Crossover Shapes vs. Speaker Order
Notes: Fig 2.46

## Slide 69
Combined Shapes
Individual Shapes
Coupling Zone
Crossover Point
6 dB
3 dB
0 dB
Asymmetric Spatial Crossover: Level Offset
10 kHz
Notes: Fig 2.46

## Slide 77: Coupled Line Source Array

## Slide 78
1/24th octave
2x 1st order (90)
@ 0 deg
12 x 12 meters
Coupled
Line Source
Speaker order effect
1st order spkrs @ 0 deg
10 kHz
1 kHz
100 Hz

## Slide 79: Coupled Line source 2nd Order
1/24th octave
2x 2nd order (40)
@ 0 deg
12 x 12 meters
Coupled
Line Source
Speaker order effect
2nd order spkrs @ 0 deg
10 kHz
1 kHz
100 Hz

## Slide 80: Coupled Line source 3rd Order
1/24th octave
2x 3rd order (08)
@ 0 deg
12 x 12 meters
Coupled
Line Source
Speaker order effect
3rd order spkrs @ 0 deg
10 kHz
1 kHz
100 Hz

## Slide 81: Coupled Line Source – 3rd Order X 3

## Slide 82: Parallel Pyramid for 3 Elements

## Slide 83: Parallel Pyramid for 8 Elements

## Slide 84: Parallel Pyramid Overlap Effects

## Slide 85: Coupled Point Source Array

## Slide 86
Coupled Point Source Array
Unique feature: it can maintain a unity class crossover over distance
  not “automatic”
  variable over frequency
  done by creating a splay angle that is equal to the element coverage angle (the “unity splay angle”)
  if coverage angle remains constant over frequency, so will the unity class crossover

## Slide 87: Coupled Line source 3rd Order
1/24th octave
2x 1st order (90)
@ 90 deg
12 x 12 meters
Coupled
Point Source
Speaker order effect
1st order spkrs @ 90 deg
10 kHz
1 kHz
100 Hz

## Slide 88: Coupled Line source 3rd Order
1/24th octave
2x 2nd order (40)
@ 40 deg
12 x 12 meters
Coupled
Point Source
Speaker order effect
2nd order spkrs @ 40 deg
10 kHz
1 kHz
100 Hz

## Slide 89: Coupled Line source 3rd Order
1/24th octave
2x 3rd order (08)
@ 08 deg
12 x 12 meters
Coupled
Point Source
Speaker order effect
3rd order spkrs @ 8 deg
10 kHz
1 kHz
100 Hz

## Slide 90: Coupled Line source 3rd Order
1/24th octave
2x 1st order (90)
@ 90 deg
12 x 12 meters
Coupled
Point Source
Overlap effects
0 %
1st order spkrs @ 90 deg
10 kHz
90 Deg
0%

## Slide 91: Coupled Line source 3rd Order
1/24th octave
2x 1st order (90)
@ 45 deg
12 x 12 meters
Coupled
Point Source
Overlap effects
50%
1st order spkrs @ 45 deg
10 kHz
22 Deg
75%
45 Deg
50%
45 Deg
50%

## Slide 92: Coupled Line source 3rd Order
1/24th octave
2x 1st order (90)
@ 22 deg
12 x 12 meters
Coupled
Point Source
Overlap effects
75%
1st order spkrs @ 22 deg
22 Deg
75%
10 kHz
22 Deg
75%

## Slide 93: Coupled Point Source, Level Offset

## Slide 94: Coupled Point Source – Level, Splay, Delay

## Slide 96: Uncoupled Line Source Array

## Slide 103: Uncoupled Point Source

## Slide 113: Coupled Line source 3rd Order
1/24th octave
2 x 1st order (90)
@ 0 deg
12 x 12 meters
Uncoupled Pt. Destination
Angle and level effects
-9 dB with delay
0 deg
-9 dB, 17.45 ms
10 kHz
1 kHz
100 Hz

## Slide 115
Speaker/Room Summation
Room reflections are inherently copies of the original signal, and therefore correlated to the source signal
Reflections can continue for extended periods of time as they move from surface to surface around the room
Most surfaces do not reflect all frequencies at the same relative level, phase, and angle of incidence
The room/speaker crossover is “self-aligning” (in time) and matched in level at the room boundary surface

## Slide 116
Speaker/Room Summation
Distance between speaker and surface analogous to half the source displacement distance between two speaker array elements
Relative angle of speaker and surface is analogous to half the splay angle between two speaker array elements
Coverage angle of the reflected “virtual” speaker is same as coverage angle of source speaker
Room surface is a physical spatial divider, and therefore the spatial crossover (coupling zone)

## Slide 118
Speaker/Room Summation
Absorption in wall surface analogous to level reduction of the secondary speaker – analogous to asymmetrical crossover
Power addition capability that comes from H or V overlap in the surface spatial crossover analogous to coupling zone addition in speaker/speaker interactions