## Slide 1: System Components for the EASE Focus 3 Design Project Loudspeakers
Reference: Chapter 11 (3rd Ed.) of Sound Systems: Design and Optimization, by Bob McCarthy (Elsevier, 2017)

## Slide 2: Outline
Specific questions and answers
Reception goals and challenges
Channel/system types
  mono
  stereo
  surround
  fills
  monitor
Balcony battles
EASE Focus 3 project loudspeaker component selection
  main arrays
  fills / distributed delay
  subwoofer arrays
Summary / conclusions

## Slide 3: Specific Questions
How many channels?
Location of each channel’s desired sound image?
What are the specific practical limitations?
  landmark status concerns (no drilling in plaster fascia)
  invisibility (all speakers must be hidden)
  sight lines (no speakers allowed below proscenium)
  scenic elements (speaker locations must dodge set pieces and structural members)
  must use “Brand X” speakers
  must be portable
  must fit in a truck (touring companies)
  must be easily rigged
  must be dummy-proof
  must be a line array (even if a line array isn’t the best choice)

## Slide 4: Specific Questions
Where are open microphones in a given channel’s coverage area?
What is the channel’s program material? (must be evaluated on a channel-by-channel basis)
What is the desired power scale? (loud, stupid loud, insanely loud)
What is the channel’s range of coverage? (“reach”)
What is the channel’s coverage area shape?
What areas need to be covered by fills?
What are the acoustic properties of the channel’s coverage area (absorption coefficients)?
What are the restrictions on choice of mix position? (prime house seats consumed by tech crew vs. “cheap seats”)
What is the budget?

## Slide 5: Specific Answers
Speaker locations
Speaker array types
  long and narrow space – coupled arrays
  wide and shallow space – uncoupled arrays
Speaker models (required power and coverage angle)
Speaker quantities (power needs and coverage)
Speaker angles/orientation
Acoustic treatment (esp. on-axis surfaces)
Signal-processing channels
Cost

## Slide 6: Reception Goals
Spatial separation as desired by artist (stereo, surround, multi-channel)
Credible tonal and spatial relationship to the source
Appropriate frequency bandwidth
Sufficient loudness
Desirable acoustics – tonal balance (appropriately scaled diffuse reverberation field, freedom from discrete echoes/resonances)
Clarity (sufficient direct-to-reverberant level ratio)

## Slide 7: Challenges
Unfavorable architectural acoustics for amplified sound
Acoustic path obstructions (set pieces, lighting)
Poor speaker positions and focus angles
Insufficient coverage (gaps due to lack of resources, poor positions/focus angles)
Excessive coverage (too many loudspeakers, overlap due to poor positions/focus angles → combing)
Insufficient system subdivision (signal processing and power amplifiers) – independent channels needed to minimize spectral variance (EQ) and ripple variance (level + delay)

## Slide 8: Channel/System Types - Mono
Central cluster (coupled point source) is the standard; alternative is “dual mono” system on left and right of the stage (uncoupled point destination array – note: lots of opportunity for combing!)
Related subsystems should preserve forward locality of reference, and be scaled as appropriate for their relative throw distances (fills, under balcony)
Subdivide when appropriate in order to level compensate for different distances, to minimize reflections, improve sonic image, or deal with obstructions

## Slide 9: Loudspeaker Choice and Placement Options
central cluster (typically single-channel)
  excellent coverage
  high intelligibility
  high gain before feedback
  smooth frequency response
  good locality of reference
  cluster needs to be large for long, narrow room
  potential for interference in driver overlap regions
  hard to hide architecturally
  “ugly hanging mess”

## Slide 10: Central Vertical Line Array Example

## Slide 11: Loudspeaker Choice and Placement Options
split (uncoupled point) source
  best if multi-channel
  high intelligibility
  potential solution for challenging room geometries
  generally more aesthetically pleasing (but not always)
  potential for creating large interference (combining) zone
  potential for loss of locality of reference
  potential for limited frequency range over which directional control is possible

## Slide 12: Split (Uncoupled Point) Source

## Slide 13: Channel/System Types - Stereo
Horizontal overlap required in center seating area
Be mindful of non-scalable time offset considerations regarding stereo imagining (keep offset within 10 ms)
Stereo “aux” systems rarely worth effort/expense (e.g., stereo under-balcony delays)
If the stereo spacing is too narrow, it is not worth the trouble (e.g., central cluster split into stereo)

## Slide 14: Channel/System Types - Stereo

## Slide 15: Channel/System Types - Surround
Surround speakers typically spaced along side and rear walls as an uncoupled line source array in the horizontal plane (1st order standard) – use aspect ratio method to space them
Want to mount these as high as they practically can in order to reduce proximity effect (distortion of horizontal localization)
Surround speakers will provide the most uniform experience if they are aimed far across the space (left aimed at right, rear aimed at front)
Subdivide coverage for different seating levels (first floor, second floor)
Delay generally not required except in special cases

## Slide 16: Channel/System Types - Surround

## Slide 17: Channel/System Types - Fills
Sidefill – provides horizontal radial extension to main system (semi-isolated from mains)
Infill – also provides horizontal radial extension to main system (differ from sidefills in that they are oriented toward the center rather than the outside)
Downfill – provides a vertical radial extension of main array (typically an asymmetric component of the coupled point source)
Frontfill – coverage of seats very near to stage (usually located on stage lip, very limited in forward coverage depth)
Delays – forward extensions of mains, inherently uncoupled

## Slide 18: Channel/System Types - Fills

## Slide 19: Loudspeaker Choice and Placement Options
distributed / delayed (uncoupled point destination)
  good solution for large, absorptive rooms with low ceilings
  potential solution for challenging room geometries
  potential solution for reinforcing “distant” zones
  requires digital delays / multiple amplifiers (expensive)
  potential for loss of locality of reference
  generally not well suited for rooms with high ceilings (or that are highly reverberant)

## Slide 20: Distributed / Delayed

## Slide 21: Balcony Battles
Shape is “W” turned on its side – suggests need for uncoupled pair of asymmetric point source arrays
Problem is midrange and below (can do the HF steering)
Tradeoffs
  single main: best for minimum ripple variance, worst for level and spectral variance
  multiple main: worst for ripple variance, best for minimum level and spectral variance
Return ratio – number of dB closer we find the front of the balcony to the farthest area angularly adjacent to it (where sound goes when skims just above or below the balcony front); affects decision whether or not to split mains

## Slide 22: Balcony Battles

## Slide 23: Balcony Battles

## Slide 24: Balcony Battles

## Slide 25: Balcony Battles

## Slide 26: Balcony Battles
Introducing “shock” into splay angle increment to induce “separation” of main beam

## Slide 27: Monitor Systems
Two choices
  stage monitor loudspeakers
    powered
    unpowered
  personal (earbud) monitors
    wired
    wireless
Monitor mixes
  main (FOH) mixing console
  personal monitor mixers

## Slide 28: Stage Monitors
Can be PASSIVE or ACTIVE

## Slide 29: Personal Monitor Mixers

## Slide 30: Wireless Earbud Monitors

## Slide 31
Main Loudspeaker Arrays for the EASE Focus 3 Design Project

## Slide 33
HK CADIS CAD 208 (Cadis-V11.gll)

## Slide 36
EV X-LINE X2-212/120 (X-Line Advance X1, X2, X12-125F v2.1.gll)

## Slide 38
Fills / Distributed Delay Loudspeakers for the EASE Focus 3 Design Project

## Slide 40
HK VR 10810 (HK-VR10810-V10.gll)

## Slide 42
Subwoofer Arrays for the EASE Focus 3 Design Project

## Slide 43
EV X12-128 4 Element FFRF (X12-128 4-Element Cardioid Stack (Front-Front-Rear-Front) v2.2.gll)

## Slide 44
EV X12-128 4 Element FFRF (X12-128 4-Element Cardioid Stack (Front-Front-Rear-Front) v2.2.gll)

## Slide 46: Loudspeaker Selection: Summary / Conclusions
There is no universal, “one size fits all” solution to loudspeaker selection
When selecting loudspeakers for the EASE Focus 3 sound reinforcement design project, compare and contrast offerings from multiple manufacturers – be prepared to defend your choices