## Slide 1: ECE 477 Digital Systems Senior Design Project
Module 10
Now What??? (Systematic Debugging)
© 2014 by D. G. Meyer

## Slide 2: Outline
“Avoid Really Stupid Tricks (RST) when debugging”
“My power supply doesn’t work. What do I do now???”
“My microcontroller doesn’t work. What do I do now???”
“My microcontroller kinda works, but ‘strange things’ are happening. What do I do now???

## Slide 3: “Avoid Really Stupid Tricks (RST)” - 1
Do NOT solder parts, attach wires, connect probes, etc. while your board is powered up
  Temporary short circuits can totally fry numerous components on your board
  Remember that the soldering iron tip is GROUNDED, and that random points tied to ground on your board while it is in operation could be a very bad thing!

## Slide 4: “Avoid Really Stupid Tricks (RST)” - 2
Do NOT attempt to “probe” the pads of surface mount parts
  Few have been known to do this successfully
  Shorts between/among microcontroller pins, regardless of how temporary, can be disastrous
  This is why you put headers on your board!

## Slide 5: “Avoid Really Stupid Tricks (RST)” - 3
Do NOT connect port pins directly to power supply rails to obtain a “1” or “0” when debugging (or, in general)
  Pin might be programmed as an output, at which point its pad driver will be instant toast
  If pin programmed as an input, might be over-biased and destroy buffer
  ALWAYS use a resistor (10K is a good value) as a pull-up or pull-down – ALWAYS
  To test ADC (analog) inputs, ALWAYS use a potentiometer (10K is a good value) – ALWAYS

## Slide 6: “Avoid Really Stupid Tricks (RST)” - 4
Do NOT attempt to power different parts of your circuit with different (external) power supplies
  Think about what will happen to your board/parts if two essentially infinite current sources are trying to drive (even slightly) different voltages on the same net/trace…
  Then, look for “burn marks” on ECE 362 students who tried this on their Mini-Project

## Slide 7: “My power supply doesn’t work” - 1
Quantify symptoms
  no voltage output whatsoever
  voltages over/under specifications
  voltage drops significantly when connected to the rest of your circuit
  excessive heat generated by components
  excessive ripple/noise on regulated output

## Slide 8: “My power supply doesn’t work” - 2
Consider possible causes of each symptom
  no voltage output whatsoever – check input voltage; if that’s OK, check output impedance; if that’s OK, replace regulator IC
  voltages over/under specifications – check to make sure regulator GND pin is hooked up (also look for cold solder joint); otherwise, replace regulator IC
  voltage drops significantly when connected to the rest of your circuit – may be bad regulator, but also could be load impedance too low (partial short/malfunction)
  excessive heat generated by components – unregulated input voltage may be too high, load may be partially shorted, or insufficient heat sink used
  excessive ripple/noise on regulated output – check size of filter caps and/or amount of input ripple

## Slide 9: “My microcontroller doesn’t work” - 1
Perform basic checks
  what’s the first basic thing you should check?
  look at power/ground pins under microscope
  what’s the second basic thing you should check?
  oscillator circuit (but be careful, since connecting scope probes to oscillator circuit pins can detune it enough to disable it)
  what’s the third basic thing you should check?
  reset circuit – is reset being held low “long
  enough” (and not stuck low)?
  what’s the fourth basic thing you should check?
  silicon errata sheet for your microcontroller

## Slide 10: “My microcontroller doesn’t work” - 2
More advanced checks
  “heartbeat” program – just toggle a port pin and look at on scope (make sure heartbeat works on your Eval Board)
  utility routines to exercise ports and on-chip peripherals
    Digital I/O – distinctive pattern (Johnson counter)
    ADC – connect potentiometer to inputs / vary
    PWM – increment duty cycle in loop
    Timers – generate periodic interrupts
    SPI – transmit/receive distinctive patterns
    SCI – transmit/receive distinctive patterns

## Slide 11: “My microcontroller kinda works” - 1
Possible “random” behaviors
  digital input values read from a port are “random” – check pull-up (internal/external), most likely inputs are floating (also check for cold solder joints)
  digital input values read from a port have a consistent (wrong) pattern – check programming of port pins – make sure they are configured as inputs – input may be damaged due to ESD/over-voltage
  the same value is read from adjacent port pins – check for solder bridges, cold solder joints, or floating adjacent pins

## Slide 12: “My microcontroller kinda works” - 2
Possible “random” behaviors…
  digital values sent to an output port don’t appear on the pins (port pins are not driven) – check to make sure port pins are programmed to be outputs, and that the “drive” register (if present) is set correctly (some pins can be configured to be open-drain)
  some output pins are always driven high or always driven low – this is most likely due to a “stuck at” fault resulting from a failure in the pad driver circuit (if there are spare port pins available, fly wire around the problem: otherwise, it’s time to replace the microcontroller)
  the same value is output on adjacent port pins – check for solder bridges (and possible damage to C)

## Slide 13: “My microcontroller kinda works” - 3
Possible “random” behaviors…
  analog input values read from the ADC are always zero (or, always the same value) – check reference voltage, ADC programming/device driver (make sure you are waiting for the “conversion complete” flag to be set)
  analog input values read from the ADC are “random” (or, are inconsistent) – check ADC reference voltages and input pin solder joints (cold joint can act like a capacitor); also, check driver routine to make sure it is handshaking on the “conversion complete” flag
  the lower two bits (or so) of values read from the ADC are “random” – this is “normal” (typically all the lower two bits are good for is rounding the result!)

## Slide 14: “My microcontroller kinda works” - 4
Possible “random” behaviors…
  the SCI/SPI is not receiving or transmitting data – most likely a configuration/driver problem (look at Tx line on logic analyzer; when Tx works, loop back to Rx line and check to make sure the same characters your driver is transmitting are being received)
  the SCI is “alive” (can see waveforms on oscilloscope), but board will not communicate with a PC “com” port or a serial LCD – check baud rate and character frame format of sending/receiving end; check to make sure RS232 level translators generating correct polarity and voltage swing (nominally  9 V); check to make sure side “A” Tx connected to side “B” Rx, and vice-versa

## Slide 15: “My microcontroller kinda works” - 5
Possible “random” behaviors…
  processor “crashes” when board is moved or “flexed” – bad (“cold”) solder joint somewhere (retouch all power/ground solder joints)
  processor runs for a few milliseconds and resets…processor runs for a few milliseconds and resets… – make sure WDT (watchdog timer) is disabled; also, check reset circuit

## Slide 16: “My microcontroller kinda works” - 6
Possible “random” behaviors…
  applications run on the processor for a few seconds, and then “crash” – may have random interrupts that are not implemented or handled correctly, stack may be overflowing (“creep” due to software error)
  microcontroller gets too warm for comfort – pins programmed as outputs are “fighting”, input signals not at supply rail potential (weak 1’s), or may be drawing too much current from port pin (source/sink)