## Slide 1: Embedded Hardware Interfacing George Hadley ©2014, Images Property of their Respective Owners.
Notes: George Hadley ©2014
Cover image source: http://hd.wallpaperswide.com/thumbs/motherboard-t2.jpg

## Slide 2: Outline
Microcontroller Selection
General Interfaces
User I/O Interfaces
Sensors
Actuators and How to Control Them
Memory
Wired Interfaces
Wireless Interfaces

## Slide 3: Microcontroller Selection
Many different types and manufacturers w/ variety of metrics and capabilities
Many selection considerations also apply to microprocessors, CPLDs, FPGAs, etc.
2 “phases” of microcontroller selection:
Importance and Guidance
Initial Prototyping/Proof of Concept: Choose an appropriate device family (parts within should be pin compatible) for the final product, then pick the most powerful device in that family
Mature Prototype/Production: Based on your requirements from phase 1 (memory, etc.), refine your choice to a more cost-efficient part
Notes: Microcontroller image source: http://upload.wikimedia.org/wikipedia/commons/1/18/PIC18F8720.jpg

## Slide 4: Microcontroller Selection
Speed (a.k.a. frequency) – How fast can your device run? (Generally measured in MHz)
Power – How much power does your device consume? (Generally measured by current consumption in mA or µA)
Memory – How much onboard memory does your device have? (Measured in kB, typically)
Voltage – What voltage range can your device operate at? (Lower voltages use less power for a given frequency)
Performance Considerations

## Slide 5: Microcontroller Selection
What onboard computational features does your device possess?
DSP operations (integrated multiply- accumulate, etc.)
Floating-point support?
Types of memory:
EEPROM – byte-addressable, nonvolatile
Flash – page-addressable, nonvolatile
RAM – byte addressable, volatile
Capability Considerations

## Slide 6: Microcontroller Selection
What peripherals does your device possess?
General µC interfaces (recall from ECE362): I2C, SPI, UART, GPIO, ADC, PWM, etc.
DAC (Digital-to-Analog) – Improved performance over PWM w/ lowpass filter
Computing interfaces: USB, Ethernet, Bluetooth, etc.
Other specialty interfaces: 1-Wire, I2S, DMA, CAN, OBD-II, etc.
Interfaces can be implemented in software (referred to as “bit-banging”)
Interface Considerations

## Slide 7: Microcontroller Selection
Variety of device packages available
Some packages are impossible to solder by hand (BGA, LGA, most QFN)
Some packages contain under-chip pads used for heat dissipation and/or mechanical stability
Recommendation: choose the most dense package variant for your desired part that you can solder by hand (for initial prototyping phase, at least)
Packaging Considerations
Notes: DIP Image Source: http://media.digikey.com/photos/Microchip%20Tech%20Photos/RE46C122E16F.JPG
SOIC Image Source: http://estore.digxtech.com/image/cache/data/ProductImages/ICs_General/8Pin_SOIC_IC_1-600x600.jpg
SSOP Image Source: http://media.digikey.com/Photos/FTDI%20(Future%20Tech%20Devices)/28-SSOP.jpg
QFP Image Source: https://dlnmh9ip6v2uc.cloudfront.net/assets/8/3/6/3/b/51dc6e21ce395f0807000000.png
QFN Image Source: http://icanbuild.it/wp-content/uploads/2011/11/28-QFN-package.jpg
BGA Image Source: http://anysilicon.com/wp-content/uploads/2012/07/bga1-anysilicon.jpg
LGA Image Source: http://media.digikey.com/Photos/Linear%20Tech%20Photos/LTM4613.jpg

## Slide 8: Microcontroller Selection
Availability/cost of programming and debugging tools
Availability/cost/usability of software development tools
Age/status of the product. (Near end-of-life (EOL)? In production? Future product?)
Ease of acquiring device samples.
Ease of acquiring the microcontroller itself. Is it in stock? Can you get spares (2-3 spares)?
Silicon-level bugs in the manufactured devices (IC manufacturers generally publish known bugs in “Silicon Errata” documents which are available online)
Other Considerations

## Slide 9: Microcontroller Selection
Various device manufacturers exist to research potential parts (use parametric selection tools to narrow offerings):
Microchip – http://www.microchip.com
Atmel – http://www.atmel.com
Texas Instruments – http://www.ti.com
Freescale Semiconductor – http://www.freescale.com
STMicroelectronics – http://www.st.com
Analog Devices – http://www/analog.com
NXP Semiconductors – http://www.nxp.com
Cypress Semiconductor - http://www.cypress.com/
Parts can be purchased or sampled (in some cases)
Manufacturers and Availability

## Slide 10: General Interfacing
Various logic families (5V, 3.3V, 2.5V, 1.8V, etc.)
Often necessary to convert from one voltage domain to another (e.g. a 3.3V microcontroller communicating with a 5V sensor)
Different level translation techniques available depending on:
Duplex (one-way communication or bidirectional?)
Number of lines (1 line? Several?)
Speed of communications
Dedicated ICs available, as well as analog methods (app notes available online)
Level Translation

## Slide 11: General Interfacing
Amplifier used to boost the strength of analog/digital signals
Typically used to drive signals over extended lengths of cable
Often used in telecommunications, audio, and certain digital computing applications (RS-232, USB, etc.)
ICs available from various manufacturers to perform line-driving functions
Line Driving
Notes: Line Driver Schematic Image Source: http://www.ti.com/lit/ds/symlink/ua9638.pdf

## Slide 12: General Interfacing
µC/FPGA/etc. device pins are often incapable of sinking/sourcing sufficient current for a DC load
BJTs and MOSFETS can be used as switches in these situations, allowing a load to be switched on or off
Switching DC Loads – Transistors
Notes: BJT, MOSFET Image Source: Self created.

## Slide 13: General Interfacing
Tradeoffs: BJTs: May require substantial base current to achieve saturation (Darlington pairs often used to obtain high hFE at high IC) MOSFETs: Require minimal gate current and less susceptible to thermal runaway; more expensive
Inductive loads (relays, motors, etc.) may require an arc suppression diode (Energy stored in an inductive load must be dissipated; otherwise the “inductive kickback” can damage the switching device)
Switching DC Loads – Transistors 2
Notes: Transistor Inductive Load Image Source: self created

## Slide 14: General Interfacing
Some devices (LEDs, etc.) are sensitive to the current passed through them
Even small changes in the forward voltage of the LED can lead to significant changes in the current flowing through the device (potential to cause damage)
For these applications, constant current drivers may be desirable
Drivers can be created using discrete parts or purchased as ICs
Switching DC Loads – Constant Current Drivers
Notes: Constant Current Driver Image Source: http://www.pcbheaven.com/userpages/images/LED_driving_and_controlling_methods_14.png
LED I-V Curve Image Source: http://www.electronics-tutorials.ws/diode/diode12.gif

## Slide 15: General Interfacing
Modulation technique in which the duty cycle of a pulsed signal is varied based on the transmitted data
Can be implemented in software
Major uses:
  Reducing power consumption by devices (LEDs)
  Motor speed control
  Simple audio
  Sensors
Pulse Width Modulation (PWM)
Notes: PWM Image Source: http://www.ni.com/cms/images/devzone/tut/a/dadc74b4230.jpg

## Slide 16: General Interfacing
Sometimes needed for control of home appliances and devices (lamps, fans, etc.)
Generally use relays or semiconductors:
Relay: Mechanical device triggered using an electromagnet
Semiconductors: Cheaper, higher reliability, less noisy, special control requirements
Heat sinking and isolation usually required
Switching AC Loads
Notes: Relay Image Source: http://m4.sourcingmap.com/photo_new/20080229/g/ux_a08022900ux0021_ux_g03.jpg
SCR Image Source: http://img.alibaba.com/img/pb/183/259/239/1269679937279_hz_myalibaba_web13_4178.JPG

## Slide 17: General Interfacing
Isolation: The act of preventing current flow between 2 circuits by providing no direct conductive path between the elements of one circuit and those of another; often used in safety and reliability situations
Isolation is often ideal when an electrical failure in one circuit (such as a high-power DC load) could cascade to and destroy another circuit (such as a microcontroller)
IMPORTANT: Isolated circuits CANNOT have a shared ground connection; a shared ground connection defeats any efforts to isolate the circuits
Isolation
Notes: Isolated, Non-Isolated Image Source: Self created

## Slide 18: General Interfacing
Numerous methods exist to provide isolation between circuits:
Transformers: Provide isolation via magnetic flux between coils
Opto-isolators/Optocouplers: Provide isolation via light transmitted over an air gap
Capacitors: Provide isolation via electric fields over an air gap (pass AC signals but not DC signals)
Hall-Effect Sensors: Use an inductor to transmit information across an air gap magnetically
Relays/Solenoids: Allow flow of electricity when closed, air gap when open
Isolation 2

## Slide 19: General Interfacing
Places where isolation is often used:
Safety situations: An electrical failure could cause injury or death to a living thing
Mission-critical situations: An electrical failure could cause catastrophic damage or destruction of an expensive piece of equipment
High-power loads: (E.g. high-power LEDs, motors, etc.) An electrical failure could cascade and cause damage or destruction of critical circuitry such as a microcontroller or FPGA
At point-of-entry for offboard cables: A long offboard cable can act like a large antenna, allowing to pick up large, unexpected, and potentially damaging induced voltages and currents
Isolation 3

## Slide 20: User I/O Interfacing
Projects may call for a matrix of switches or switch-like elements (magnetic sensors, light sensors, etc.)
Standard approach is to assert individual rows of the matrix and listen for signals on the columns of the matrix. (Repeatedly scan through each row of switch matrix). Can be performed by Keypad Encoder IC (or similar)
Without proper care, “ghosting” or “masking” can occur on a keypad matrix when attempting to detect multiple key presses
An excellent writeup on switch matrices can be found here: http://www.dribin.org/dave/keyboard/one_html/
Keypads and Switch Matrices
Notes: Keypad Image Source: http://www.zen22142.zen.co.uk/Circuits/Switching/12keypad.jpg
Switch Matrix Image Source: http://www.dribin.org/dave/keyboard/one_html/switch_open.gif

## Slide 21: User I/O Interfacing
Convert the angular position or motion of a shaft into an analog or digital code
Often used on user interfaces as knobs, particularly in instances when unlimited rotation is desirable
Rotary Encoders
Notes: Rotary Encoder Image Source: http://media.digikey.com/photos/Panasonic%20Photos/EVE-GA1F2012B,%20EVE-GA1F2024B.jpg
Timing Graphs and Logic Table: Borrowed from previous iteration of hardware interfacing lecture by Prof. David Meyer; original source unknown

## Slide 22: User I/O Interfacing
Sliders and knobs are generally available as potentiometers
Linear scales and logarithmic scales available (log scale potentiometers often used in audio and video applications)
Reading slider value is as simple as performing A/D conversion on the potentiometer value
Knobs and Sliders
Notes: Rotary Potentiometer Image Source: http://amprepairparts.com/dshaft16.jpg
Slide Potentiometer Image Source: https://cdn.sparkfun.com//assets/parts/2/5/2/4/09119-03-L.jpg

## Slide 23: User I/O Interfacing
Many types: Discrete, 7-segment display, LED strip, LED meter, etc.
Variety of colors: single color, bicolor, RGB, etc. (color of LED influences forward voltage of LED)
LEDS
Notes: Discrete LED Image Source: http://th00.deviantart.net/fs70/PRE/f/2013/234/d/6/led_rainbow_by_steeph_k-d6jb8az.jpg
7-Segment Display Image Source: http://www.adafruit.com/images/1200x900/878-00.jpg
LED Strip Image Source: http://www.hitlights.com/blog/wp-content/uploads/2012/12/Illusion-LED-Strip-RRFT1000-40RGBD-1.jpg
LED Meter Image source: https://lh3.ggpht.com/amItC01K_Rlh7jlJCXB-2DVzu4czrZFz90776i46Z51rIvtFWLEPBw1cAawOopnUAQ=h900

## Slide 24: User I/O Interfacing
Used to display dot-matrix characters
Available in various colors, backlight colors, widths, heights, and operating voltages
Various interfaces available; most character LCDs are ultimately based on the Hitachi HD44780 LCD controller
It is possible to store a limited number of custom characters onto LCD displays for custom graphics. One writeup on the subject is available here: http://www.pyroelectro.com/tutorials/16x2_lcd_custom_character/index.html
Character LCDs
Notes: Character LCD Image Source: http://www.blazedisplay.com/UploadFile/16X2_Character_LCD_Module_STN_Yellow_Green_L.jpg

## Slide 25: User I/O Interfacing
Provide more flexible and sophisticated options than character LCDs
Variety of colors, screen sizes (measured in pixels), interfaces, voltages, etc.
Generally necessitate the use of libraries such as graphics libraries, fonts, drawing APIs, etc. in order to use effectively
Graphical LCDs
Notes: Graphical LCD 1 Image Source: http://www.voti.nl/common/LCD_21_test2.jpg
Graphical LCD 2 Image Source: http://www.picbasic.co.uk/forum/attachment.php?attachmentid=1671&stc=1&d=1179960607

## Slide 26: User I/O Interfacing
Adds user interface layer to existing graphical display
2 major touch technologies: resistive and capacitive
Generally necessitate the use of libraries such as graphics libraries, fonts, drawing APIs, etc. in order to use effectively
Generally necessitate the use of dedicated display driver hardware (µC offloads graphics commands to display driver)
Touchscreen LCDs
Notes: Touchscreen LCD 1 Image Source: http://www.thaieasyelec.net/images/uploads/Product-Image/ARM/ETEE009-Bluescreen.jpg
Touchscreen LCD 2 Image Source: http://img-europe.electrocomponents.com/images/R7502581-01.jpg

## Slide 27: User I/O Interfacing
Nixie Tubes: Numbers displayed using gas tubes (similar in function to a neon sign)
Electromagnetic Dot Display: Uses magnets to flip dots into on or off position
Esoteric Display Options
Notes: Nixie Tubes Image Source: http://badnixie.com/Web_Files/DSC_10014.JPG
Flip Dot Display Image Source: http://www.decadecounter.com/vta/pict13/flipdot1.jpg

## Slide 28: User I/O Interfacing
Electronic Paper:
Reflects light, rather than emitting it (saving power)
Flexible
Capable of retaining static text and images indefinitely without application of power
Emerging Display Options
Notes: Electronic Paper Image Source 1: http://images.gizmag.com/hero/3949_170405115752.jpg
Electronic Paper Image Source 2: http://cdr.cz/sites/default/files/images/7029/03_e-ink_display_technologie.jpg

## Slide 29: Sensors
Light-sensing techniques:
Photodiode/Phototransistor: Conductivity is determined by level of light exposure (tuned to various wavelengths of light)
Solar Cell: Supplies current proportional to incident light on the solar cell surface
Light, Color, and Imaging
Notes: Sensitivity Graph Image Source: http://www.aliexpress.com/item/9mm-cds-ldr-photocell-sensor-GM9516/500733516.html
Photodiode Image Source: http://img.directindustry.com/images_di/photo-g/photodiode-silicon-33535-2583809.jpg
Photocell Image Source: https://cdn.sparkfun.com//assets/parts/2/4/6/2/09088-02-L.jpg

## Slide 30: Sensors
Color sensing techniques:
Dedicated color sensors: Finely tuned photocells to detect RGB color wavelengths
LEDs: Can reverse-bias and use as a color-sensing device
Cameras: Can use cameras in conjunction with image processing software (OpenCV, etc.) to detect colored objects
Light, Color, and Imaging
Notes: LED Color Sensor Schematic Image Source: http://www.robotroom.com/ReversedLED/PhotodiodeAmplifierSchematic.gif
LED Color Sensor Image Source: http://www.georgegardner.info/wp-content/uploads/2012/02/IMGP4235.jpg

## Slide 31: Sensors
CMOS/Cellular Cameras readily available
Computational considerations: speed, resolution, frame rate, processing latency, memory/buffering considerations
Generally require additional hardware considerations (motherboards, embedded drivers, dedicated hardware, etc.)
Video/Photo Imaging
Notes: CMOS Camera Image Source: https://cdn.sparkfun.com//assets/parts/9/6/4/5/12804-04.jpg

## Slide 32: Sensors
Gyroscopes: Measures orientation based on angular momentum principles
Compass: Senses orientation relative to magnetic fields
GPS: Senses position by measuring received signals in satellite constellation and calculating satellite delays
IMU: Inertial measurement unit; uses gyros, compasses, and accelerometers to accurately determine position and velocity of objects
Motion, Position, and Orientation
Notes: Digital Compass image Source: https://developer.mbed.org/media/uploads/aberk/hmc6352.jpg
GPS Module Image Source: http://www.laptopgpsworld.com/images/uploads/4784542567_1ac29afa37.jpg
IMU Image Source: http://www.cumatix.com/wp-content/uploads/2012/05/AU7428N200_s.jpg

## Slide 33: Sensors
Accelerometers: Use MEMS and piezoelectric materials to measure force applied to a known mass (F = ma)
Altimeters/Barometers: Determine the height/altitude of an object by measuring atmospheric pressure
Shaft Encoders: Measure rotations of an axle, then use known properties of the wheel to determine distance traveled
Motion, Position, and Orientation
Notes: Accelerometer Image Source: http://farm2.static.flickr.com/1118/1193147290_d2069c9c08_m.jpg
Barometric Pressure Sensor Image Source: https://cdn.sparkfun.com//assets/parts/6/9/2/08161-03-L.jpg
Shaft Encoder Image Source: http://www.labbookpages.co.uk/circuits/files/wheelEncoder/sensor.jpg

## Slide 34: Sensors
Hall Effect Sensor: Measure presence of (nearby) magnetic fields
Rangefinder: Measure distance to an object through various methods
Sonar/Ultrasonic: Sound waves
Radar: Radio waves
Lidar: Light waves
Infrared: IR light
Proximity and Rangefinding
Notes: IR Rangefinder Image Source: https://cdn.sparkfun.com//assets/parts/2/2/6/0/08958-03-L.jpg
Ultrasonic Rangefinder Image Source: https://cdn.sparkfun.com//assets/parts/1/0/5/2/EZ1_img.jpg

## Slide 35: Sensors
Thermocouple: Measures the voltage induced by the temperature gradient between dissimilar metals
Thermistor: Resistor whose resistance changes significantly as a function of temperature
Infrared: Measure heat by measuring the emitted infrared radiation
Heat and Temperature
Notes: IR Thermometer Image Source: http://www.medicaldevice-network.com/contractor_images/melexis/3-temperature-sensor.jpg
Thermistor Image Source: https://ultimachine.com/sites/default/files/imagecache/product_full/Thermistor_1_0.jpg

## Slide 36: Sensors
Microphone: (Electret type most common) – Uses dielectric material and diaphragm to detect sound
Piezoelectric: Materials which convert mechanical vibrations into electrical charge. Used in microphones and other sensors (such as flex sensors)
Sound and Vibration
Notes: Piezoelectric Sensor Image Source: http://www.meas-spec.com/uploadedImages/Sensor_Types/Piezo/Products/IMG_PiezoSensor_LDTI_028.jpg
Electret Microphone Image Source: https://cdn.sparkfun.com//assets/parts/1/7/6/9/08635-03-L.jpg

## Slide 37: Sensors
Fingerprint Scanners: User authentication and security applications
Gas Sensors: Used to detect the presence of methane, CO, CO2, O2, H2, and other gases
Electrokardiogram (EKG): Used in heartbeat detection
Electroencephelogram (EEG): Used in brainwave detection
Chemical and Biological
Notes: Fingerprint Scanner Image Source: http://www.elabpeers.com/media/catalog/product/cache/1/image/800x800/9df78eab33525d08d6e5fb8d27136e95/i/m/img_9428.jpg Gas Sensor Image Source: http://img-europe.electrocomponents.com/images/R538992-01.jpg
EKG Image Source: http://static.flavors.me/dynamic_images/background/e5bc2bf327504d14a2e9a37f0e0cf3e4

## Slide 38: Actuators and Control
Light Bulbs: Create light through use of a heated filament (or ionized channel, in case of fluorescent bulbs)
LEDs: Create light using semiconductor properties
Laser Diodes: Similar to LEDs, but generate lasers
Bright light sources and lasers require special safety considerations (eye protection)
Light
Notes: Fluorescent Light Bulb Image Source: http://www.elightbulbs.com/catpics/ge/97609lg.jpg
RGB Power LED Image Source: http://www.conrad.com/medias/global/ce/1000_1999/1800/1820/1827/182711_BB_00_FB.EPS_1000.jpg Laser Diode Image Source: http://www.armlaser.com/images/armlaser.com%20450nm%20blue%20laser%20diode.jpg

## Slide 39: Actuators and Control
LEDs:
High-power LEDs: Require DC switching techniques, may require constant current drivers
Many LEDs: May require dedicated driver chip
Multiplexing: Switch groups of LEDs on and off quickly (reduces power consumption)
Charlieplexing: Technique for driving large numbers of LEDs from few device pins
Light bulbs: Require AC switching techniques (relays, triacs, etc.)
Laser diodes: Require DC switching techniques
Light Control
Notes: Multiplexing description: http://en.wikipedia.org/wiki/Multiplexed_display
Charlieplexing description: http://en.wikipedia.org/wiki/Charlieplexing

## Slide 40: Actuators and Control
Buzzer: Converts electricity to frequency tones
Speaker: Converts electricity to sound
Dynamic Loudspeaker: Uses magnetic coil to vibrate diaphragm; good frequency response
Piezoelectric Speaker: Uses piezoelectric materials; poor frequency response but compact and durable
Audio
Notes: Multiplexing description: http://en.wikipedia.org/wiki/Multiplexed_display
Charlieplexing description: http://en.wikipedia.org/wiki/Charlieplexing Speaker Cutaway Image Source: http://upload.wikimedia.org/wikipedia/commons/7/79/Loudspeaker-bass.png
Piezoelectric Speaker Image Source: http://media.digikey.com/Photos/PUI%20Audio/APS2509S-T-R.JPG

## Slide 41: Actuators and Control
Filtering needed to condition input and remove noise
Amplification generally needed (control sound volume):
“Class A” Amplifier: Simple, great performance, horrible efficiency (25-50% max depending on techniques)
“Class B” Amplifier: Improved efficiency (~78.5% max), distortion and performance issues
“Class AB” Amplifier: Compromise between A and B approaches; medium efficiency and performance
“Class C” Amplifier: Exists, but not recommended for audio applications
Amplifier techniques can be used for other applications (driving radio signals, motor control, etc.)
Audio Control

## Slide 42: Actuators and Control
“Class D” Amplifier:
Uses transistors as switches rather than linear amplifiers
Output signal is modulated (PWM, delta-sigma, etc.), then fed to the amplifier
Pros: extremely power efficient with good performance
Cons: complexity
ICs available to perform this functionality and reduce complexity requirements
Audio Control 2
Notes: Class-D Amplifier Image Source: http://dangerousprototypes.com/wp-content/media/2011/05/5731723841_7732b06cd2-W490.jpg

## Slide 43: Actuators and Control
Wire Heaters: Highly resistive wire which generates heat when current is passed through (similar to filaments in a toaster – Nichrome and Tungsten popular options)
Peltier Cooler: Uses electricity to generate a temperature differential (Used in some cooling applications)
Thermal
Notes: Peltier image source: http://www.reuk.co.uk/OtherImages/schematic-diagram-of-peltier-module.jpg
Nichrome wire image source: http://ak.picdn.net/shutterstock/videos/5437880/preview/stock-footage-tungsten-filament-burner-heats-up-and-turns-red.jpg

## Slide 44: Actuators and Control
DC Motors: Use oscillating electromagnetic fields to produce continuous rotation
Brushed DC: Uses an internal commutator and conductive brushes to mechanically switch the magnetic field (low cost, simple control, lower life span)
Brushless DC (BDC): Utilizes permanent magnet for switching of magnetic field, external commutation (higher cost, more complicated control, higher reliability)
Motion: Motors
Notes: Brushed DC motor image source: http://hades.mech.northwestern.edu/images/d/d0/Motor_cutaway.png

## Slide 45: Actuators and Control
Stepper Motors: Similar to brushless DC, but produce motion in discretized steps rather than smooth motion. Sophisticated control schemes generally used; partial step motion is possible under certain control schemes
Servos: Designed to travel to a specific rotational angle based on a provided digital value. Motion limited to ~270º without modification.
Motion: Motors 2
Notes: Stepper motor image source: http://upload.wikimedia.org/wikipedia/commons/8/83/Nema_17_Stepper_Motor.jpg
Servo motor image source: http://jeroendoggen.files.wordpress.com/2012/01/parallax-standard-servo.jpg

## Slide 46: Actuators and Control
Linear Actuators: Convert electricity into linear motion (solenoids, mechanical conversion of rotational to linear motion)
Muscle Wire/Shape memory alloy: Material changes shape when electric current applied; used to imitate biological muscles
Motion: Other
Notes: Linear actuator image source: http://images10.newegg.com/NeweggImage/productimage/A2C5_1302387647915556233GSmEgnSns.jpg
Muscle wire image source: http://a.tgcdn.net/images/products/zoom/ef2f_muscle_wire_moving_hand_kit_anim.gif

## Slide 47: Actuators and Control
Pumps: Used to transport fluids throughout a system
Important: some pumps must have fluids in them to work while others can be run dry.
Pneumatics: Air used to control motion of system parts
Hydraulics: Water, oil, or other liquid used for motion
Motion: Other 2
Notes: Pump image source: http://www.adafruit.com/blog/wp-content/uploads/2012/12/window-397.jpg
Pneumatics image source: http://www.chiefdelphi.com/pics/bin/1043974483pneumaticsboard.jpg

## Slide 48: Actuators and Control
H-Bridge: Transistor circuit commonly used to control the direction of a DC motor (PWM input waveforms commonly used for speed control)
Transistors used as switches; arranged in “H” pattern
Motion: DC Motor Control
Notes: H-Bridge image and table source: self-created

## Slide 49: Actuators and Control
Stepper motor stator and rotor consist of wound coils
Stepping through rotation in a given direction is a matter of activating the coils in a specific sequence (partial stepping control options available)
Motion: Stepper Motor Control
Notes: Stepper Motor Drawing Image Source: http://www.ustudy.in/sites/default/files/images/VR%20Motor.JPG
Stepper Motor Control Schematic Source: Based on previous hardware interfacing slides by Professor David Meyer; original source unknown

## Slide 50: Memory
2 categories of memory:
Volatile: State lost when power is removed
Nonvolatile: State retained when power is removed
Types of memory:
EEPROM: Byte addressable, nonvolatile, smaller sizes (~8MB), fast access times
Flash: Page addressable (256-512B/page), nonvolatile, large sizes available (32GB+), slow access times
SRAM (Static RAM): Volatile, low power, dual-port options available
DRAM (Dynamic RAM): Dense, volatile, requires periodic refreshing
Notes: SD Card Image Source: http://blog.frankvh.com/wp-content/uploads/2009/07/sd-card.jpeg
DRAM Image Source: http://www.blogcdn.com/www.engadget.com/media/2009/01/samsung_dram-chips_1.29.09.jpg

## Slide 51: Wired Interfacing
Universal System Bus (USB)
Multiple data rate classes available:
  Low-Bandwidth: 1.5 Mbps (USB v1.1)
  Full-Bandwidth: 12 Mbps (USB v1.1)
  Hi-Speed: 480 Mbps (USB v2.0)
  SuperSpeed: 5.0 Gbps (USB v3.0)
  SuperSpeed+: 10 Gbps (USB v3.1)
Some common protocol implementations:
Host: Device acts as the master for other USB devices (requires implementation of 1+ host controllers)
Client: Device acts as a slave device (various profiles available)
USB On-The-Go (OTG): Devices take turns acting as host and slave
Computing Interfaces
Notes: USB Logo Image Source: http://upload.wikimedia.org/wikipedia/en/f/f4/USB.png
USB Cable Image Source: http://www.publicdomainpictures.net/pictures/10000/nahled/1-1211026487gA6W.jpg

## Slide 52: Wired Interfacing
USB cont.
USB connector options:
  Standard: larger connectors used on laptops, desktops, tablets, etc.
  Mini: Used in cameras, camcorders, and other small devices
  Micro: Supercedes mini on most smartphones, etc.
  USB Power Limits:
  USB v1.1: 150mA@5V from port, 2A@5V from external
  USB v2.0: 500mA@5V from port, 2A@5V from external
  USB v3.0: 900mA@5V from port, 2A@5V from external
  All USB devices start in low power mode; must request additional power
Computing Interfaces 2
Notes: USB Cable Chart Image Source: http://img528.imageshack.us/img528/8805/usbtypes.jpg

## Slide 53: Wired Interfacing
Ethernet (IEEE 802.3):
Specification involved in networking devices (for more on networking devices, read up on the OSI and TCP/IP networking models)
Consists of the physical layer and link layer for connecting devices
Ethernet development generally requires external support hardware:
  PHY Chip: Implements the physical layer functions of an Ethernet interface
  MAC Chip: Implements data link layer functions of an Ethernet interface
  A useful reference design for microcontroller Ethernet can be found here
Computing Interfaces 4
Notes: OSI Model Reference: http://en.wikipedia.org/wiki/OSI_model
TCP/IP Model Reference: http://en.wikipedia.org/wiki/Internet_protocol_suite
Microcontroller Ethernet Example: http://dangerousprototypes.com/docs/Web_Platform
Ethernet Cable Image Source: http://deltautomation.files.wordpress.com/2011/10/ethernet-cable-utp-mold-type-kb-aa06.jpg
Microcontroller Ethernet Board Source: http://dangerousprototypes.com/docs/images/4/41/Webplatformv11-overview.jpg

## Slide 54: Wired Interfacing
Powerline Communication (PLC) / X-10:
  Modulate signals over existing AC power lines to send data
  Example applications: home automation, Christmas tree light controllers
Musical Instrument Digital Interface (MIDI):
Standard specifying a protocol and connectors
MIDI over USB is permitted
On-Board Diagnostic System (OBD-II):
Required on all US motor vehicles manufactured after 1995
Facilitates communication with onboard vehicle computers
Many manufacturers implement proprietary codes (use of licensed OBD-II protocol ICs can overcome this)
Other Interfaces
Notes: MIDI Connector Image Source: http://www.adafruit.com/blog/wp-content/uploads/2012/12/1134_LRG.jpg

## Slide 55: WireLESS Interfacing
WiFi (IEEE 802.11x):
At the embedded hobbyist level, WiFi is generally implemented using dedicated chips and/or modules
NOTE: PAL2.0/3.0 has challenges with individual embedded WiFi (use of personal routers recommended)
Revisions of the WiFi protocol:
IEEE 802.11a: 54Mbps@5GHz (OFDM)
IEEE 802.11b: 11Mbps@2.4GHz (OFDM)
IEEE 802.11g: 54Mbps@2.4GHz (OFDM)
IEEE 802.11n: 54-600Mbps@2.4GHz or 5GHz (OFDM), Support for multiple antennae (MIMO)
Future Revisions: More channels, millimeter wave band support (30+ GHz), etc.
General Computing Interfaces
Notes: WiFi Module Image Source: http://media02.hongkiat.com/electronic-circuits-modules/spark-core.jpg

## Slide 56: WireLESS Interfacing
Bluetooth:
Common wireless option for interfacing to computers and mobile devices (~100 yard/m max range)
2.4GHz operation (interference from WiFi, microwaves, and other 2.4GHz devices)
As of Bluetooth v4.0, a second Bluetooth Low-energy spec (Bluetooth LE) was introduced. Bluetooth LE is not backwards compatible with existing Bluetooth hardware
General Computing Interfaces 2
Notes: Bluetooth Logo Image Source: http://fontmeme.com/images/Bluetooth-Logo.jpg
Bluetooth Module Image Source: http://www.seeedstudio.com/depot/images/newblue_LRG.jpg

## Slide 57: WireLESS Interfacing
GSM/GPRS:
2nd Gen cell network protocols (900MHz, 1800MHz)
3G:
3rd Gen cell networks (various standards; CDMA, TDMA, FDMA common protocols)
4G:
4th Gen cellular networks (various standards; WiMax and LTE common protocols)
Mobile/Cellular Interfaces
Notes: GSM/GPRS Module Image Source: https://cdn.sparkfun.com//assets/parts/3/2/8/7/09533-01.jpg
4G Cell Module Image Source: http://linkwave.co.uk/sites/default/files/styles/zoom/public/mc7710_1.JPG?itok=Fb_IdeDB

## Slide 58: WireLESS Interfacing
Zigbee:
2.4GHz operation (incompatible w/ Bluetooth and WiFi)
Support for mesh networking (network nodes can be added/dropped ad hoc)
RF:
Various RF modules exist at different frequencies
Power, and supported modes at various frequencies governed by the FCC (in USA)
Embedded Interfaces
Notes: Zigbee Module Image Source: http://www.newark.com/productimages/standard/en_US/4573287.jpg
RF Module Image Source: http://www.rf-module-china.com/admin/uploadfile/200905/2009052518390692.jpg

## Slide 59: WireLESS Interfacing
Radio Frequency Identification (RFID):
Cheap, passive tags (used to ID objects)
Near Field Communication (NFC):
Communicates using electrical or magnetic fields (but not radio waves)
Capable of communicating through conductors
Secure, private (more difficult to intercept than RF)
Wireless Power Transmission:
Used in some charging applications
Other Interfaces
Notes: RFID Module Image Source: http://www.robotshop.com/Images/big/en/rfid-reader-module-id-2.jpg
NFC Module Image Source: http://www.elecfreaks.com/store/images/NFC-Module.jpg