## Slide 1: Professional Considerations in Digital System Design Case Study: NEST LEARNING Thermostat
David G Meyer ©2020, Images Property of their Respective Owners

## Slide 2: Outline – Professional Considerations in Digital System Design
Case Study: The NEST Learning Thermostat
  Company History
  How NEST Learns
  Common Thermostat Circuits
  IP Protected by Patents
  What’s Inside
  Block Diagram
  Key Functions
  Schematic Details
Professional Considerations: Case Study Applications
  Reliability & Safety
  Legal
  Environmental & Regulatory
  Ethical & Public Policy

## Slide 3: Clicker Quiz
Indicate your “highest level” of experience with household thermostats:
  I know that 4 wires are required for the basic interface, and that the control signals operate at 24 VAC
  I have installed an electronic/smart thermostat
  I have installed a conventional/mechanical thermostat
  I understand that temperature control requires hysteresis, but have never installed a thermostat
  I only know if it’s too hot or cold, and how to adjust the thermostat accordingly
Question 1

## Slide 4: Background
Nest Labs Company History
Headquartered in Palo Alto, California
Designs and manufactures sensor-driven, Wi-Fi enabled, self-learning (programmable) thermostats and smoke detectors
Co-founded by former Apple engineers Tony Fadell and Matt Rogers in 2010
First product was Nest Learning Thermostat (2011), inspired by Fadell’s motivation to build a better “electronic” thermostat than those currently available
Google acquired Nest Labs for $3.2B early in 2014
Nest purchased Dropcam for $555M later in 2014
Latest products include Nest Protect (Smoke and Carbon Monoxide detector with voice alerts), Doorbell, and Lock

## Slide 5: Background
How Nest Learns

## Slide 6: Background
Nest Learning Thermostat Energy Savings Claims

## Slide 7: BACKGROUND
Basic 4-Wire Circuit Thermostat Circuit
Questions:
What is unknown?
What signal is (generally) not available at the thermostat?
What are implications of the need to switch 24VAC at up to 1 A?
What are implications of the unknown load impedance?
What are the implied restrictions on how an electronic thermostat can be powered?
common

## Slide 8: PATENTS
US Patent 8,523,083 (filed Jun. 2012, issued Sep. 2013)
THERMOSTAT WITH SELF-CONFIGURING CONNECTIONS TO FACILITATE DO-IT-YOURSELF INSTALLATION
Ease of Installation
ABSTRACT A thermostat is configured for automated compatibility with HVAC systems that are either single-HVAC-transformer systems or dual-HVAC-transformer systems. The compatibility is automated in that a manual jumper installation is not required for adaptation to either single-HVAC-transformer systems or dual-HVAC-transformer systems. The thermostat has a plurality of HVAC wire connectors including a first call relay wire connector, a first power return wire connector, a second call relay wire connector, and a second power return wire connector. The thermostat is configured such that if the first and second external wires have been inserted into the first and second power return wire connectors, respectively, then the first and second power return wire connectors are electrically isolated from each other. Otherwise, the first and second power return wire connectors are electrically shorted together.

## Slide 9: Clicker Quiz
Contrary to the illustration from the Nest website reproduced here, the following wire connection (color) is typically not included in standard 4-wire household thermostat circuits:
  Red (RH / RC)
  Yellow (Y)
  White (W)
  Blue (C)
  none of the above
Question 2
Notes: D – blue (there is no “common wire”)

## Slide 10: Clicker Quiz
Contrary to the illustration from the Nest website reproduced here, the following wire connection (color) is typically not included in standard 4-wire household thermostat circuits:
  Red (RH / RC)
  Yellow (Y)
  White (W)
  Blue (C)
  none of the above
Question 2 - Answer
Notes: D – blue (there is no “common wire”)

## Slide 11: Clicker Quiz
For the thermostat wiring shown, the following HVAC function cannot be controlled from the thermostat:
  fan (air circulation) only
  dehumidification
  heating
  cooling
  none of the above
Question 3
Notes: D – blue (there is no “common wire”)

## Slide 12: Clicker Quiz
For the thermostat wiring shown, the following HVAC function cannot be controlled from the thermostat:
  fan (air circulation) only
  dehumidification
  heating
  cooling
  none of the above
Question 3 - Answer
Notes: D – blue (there is no “common wire”)

## Slide 13: PATENTS
US Patent 8,620,841 (filed Aug. 2012, issued Dec. 2013)
Dynamic distributed-sensor thermostat network for forecasting external events
Event Forecasting System
ABSTRACT Systems and methods for forecasting events can be provided. A measurement database can store sensor measurements, each having been provided by a non-portable electronic device with a primary purpose unrelated to collecting measurements from a type of sensor that collected the measurement. A measurement set identifier can select a set of measurements. The electronic devices associated with the set of measurements can be in close geographical proximity relative to their geographical proximity to other devices. An inter-device correlator can access the set and collectively analyze the measurements. An event detector can determine whether an event occurred. An event forecaster can forecast a future event property. An alert engine can identify one or more entities to be alerted of the future event property, generate at least one alert identifying the future event property, and transmit at least one alert to the identified one or more entities.

## Slide 14: Patents
Event Forecasting System is Key Patent Claim

## Slide 15: PATENTS
US Patent 8,511,577 (filed Aug. 2012, issued Aug. 2013)
Thermostat with power stealing delay interval at transitions between power stealing states
Advanced Energy Harvesting (“Power Stealing”) Strategy
ABSTRACT A thermostat includes a plurality of HVAC (heating, ventilation, and air conditioning) wire connectors including a connection to at least one call relay wire. The thermostat may also include a powering circuit, including a rechargeable battery, which is configured to provide electrical power to the thermostat by power stealing from a selected call relay wire. The power stealing may include an active power stealing mode, in which power is taken from the same selected call relay wire that is used to call for an HVAC function, and an inactive power stealing mode in which, in which no active call is being made. The powering circuit may be configured to substantially suspend (or at least reduce the level of) power stealing for at least a first time period following each transition of the thermostat from between operating states.

## Slide 16: Overview
What’s Inside

## Slide 17: Overview
What’s Inside

## Slide 18: Overview
Conceptual Block Diagram

## Slide 19: Introduction
Block Diagram

## Slide 20: Key Functions
Mechanical Causation of Insertion Sensing Signals
ARM Cortex-A8

## Slide 21: Key Functions
Accommodation of Single and Dual Transformer Installations

## Slide 22: Schematic Details
Connection Sensing Mechanism
Use of auto-switching connectors for automatically selecting a source for power harvesting

## Slide 23: Schematic Details
Power Supply - 1
“high voltage” buck converter

## Slide 24: Schematic Details
Power Supply - 2
Bootstrap LDO

## Slide 25: Schematic Details
Power Supply - 3
Battery LDO and charging circuitry

## Slide 26: Schematic Details
Output Drive for Connection Between RC and W (or Y / G)
Most electronic thermostats accomplish this function (switching 24 VAC signals) using a latching relay or an (optically isolated) thyristor (triac or SCR) – why is such a complicated circuit used by the Nest Thermostat to perform essentially the same task?
Why is a transformer required?
Why is PWM used?

## Slide 27: Clicker Quiz
Based on the preferred embodiment published in the patents, a fairly complicated circuit is used to provide essentially a “contact closure” between two terminals (like RC and W1 to control cooling). The reason given in the patent disclosure for using this circuit in place of a much simpler device (like a relay or SCR) is:
  to increase reliability
  to enable energy harvesting while the control contact is “closed”
  to enable energy harvesting while the control contact is “open”
  to eliminate the annoying “click” associated with relays
  none of the above
Question 4
Notes: D – blue (there is no “common wire”)

## Slide 28: Clicker Quiz
Based on the preferred embodiment published in the patents, a fairly complicated circuit is used to provide essentially a “contact closure” between two terminals (like RC and W1 to control cooling). The reason given in the patent disclosure for using this circuit in place of a much simpler device (like a relay or SCR) is:
  to increase reliability
  to enable energy harvesting while the control contact is “closed”
  to enable energy harvesting while the control contact is “open”
  to eliminate the annoying “click” associated with relays
  none of the above
Question 4 - Answer
Notes: D – blue (there is no “common wire”)

## Slide 29: PATENTS
US Patent 8,511,577 (filed Aug. 2012, issued Aug. 2013)
Thermostat with power stealing delay interval at transitions between power stealing states
Advanced Energy Harvesting (“Power Stealing”) Strategy
ABSTRACT A thermostat includes a plurality of HVAC (heating, ventilation, and air conditioning) wire connectors including a connection to at least one call relay wire. The thermostat may also include a powering circuit, including a rechargeable battery, which is configured to provide electrical power to the thermostat by power stealing from a selected call relay wire. The power stealing may include an active power stealing mode, in which power is taken from the same selected call relay wire that is used to call for an HVAC function, and an inactive power stealing mode in which, in which no active call is being made. The powering circuit may be configured to substantially suspend (or at least reduce the level of) power stealing for at least a first time period following each transition of the thermostat from between operating states.

## Slide 30: Outline – Professional Considerations in Digital System Design
Case Study: The NEST Learning Thermostat
  Company History
  How NEST Learns
  Common Thermostat Circuits
  IP Protected by Patents
  What’s Inside
  Block Diagram
  Key Functions
  Schematic Details
Professional Considerations: Case Study Applications
  Reliability & Safety
  Legal
  Environmental & Regulatory
  Ethics & Public Policy

## Slide 31: RELIABILITY & safety
FEMCA* of Power MOSFETs
Questions:
What happens if the MOSFETs heat up (even just a few degrees above ambient)?
What is the most likely cause of power MOSFET failure?
What happens if either or both MOSFETs fail open?
What happens if either or both MOSFETs fail shorted?
What is the criticality level of either of these failure modes?
*failure effects mode and criticality analysis

## Slide 32: LEGAL
Patent Infringement
February 2012 - Honeywell filed a lawsuit claiming that some of its patents had been infringed by Nest (e.g., US 7,476,988 “Power Stealing Control Devices”)
May 2013 – Allure Energy filed lawsuit against Nest for newly issued patent US 8,442,695 “Auto-Adaptable Energy Management Apparatus” (filed November 2011)
Kevin Imes, president and CEO of Allure Energy, first began developing a smart thermostat in 2009, filing its patent application in 2010, to manage home temperature and energy usage. Allure Energy also developed and patented “Proximity Control Technology” that instantly adapts to a user’s daily schedule to provide automatic comfort and energy savings at home based on the distance a user may be from a residence.
“With our own capital, we created a smart and original thermostat control that also syncs music, reports local weather and offers energy tips, and filed all the required patent documentation well before Nest Labs launched its products.”

## Slide 33: Environmental & Regulatory
Nest Learning Thermostat Energy Savings Claims
Homes using Vectren natural gas or Vectren electric as the primary heat source are eligible for this rebate. Dual fuel systems are not eligible.
Rebate available for existing homes only; new construction is not eligible.
"Smart" thermostat: Must be Wi-Fi capable and connected to the home. Must be ENERGY STAR certified as "Smart." Limit of two thermostats per home ("Wi-Fi" and/or "Smart").
Wi-Fi enabled thermostat: The product must be Wi-Fi capable and connected to the internet for programming and adjusting remotely. Limit of two Wi-Fi enabled thermostats per home ("Wi-Fi" and/or "Smart").

## Slide 34: ETHICS & Public Policy
Security of Personal Data
Energy use profiles could be collected by devices like Nest and sold by data mining companies such as Google
No “consent clause” on use of this personal data is currently included with purchase agreement
Potential for abuse?