## Slide 1: ECE 477 Digital Systems Senior Design Project
Module 12
Designing for Reliability, Maintainability, and Safety
Spring 2014 Edition

## Slide 2: Outline
Introduction
Component Failures and Wear
Mean Time To/Before Failure (MTTF/MTBF)
Heat Controller Example
Failure Rate Calculation
Improving System Availability
Failure Mode & Effects Analysis (FMEA)
Criticality Analysis (FMECA)
Fault Tree Analysis (FTA)
Software and Watchdogs
Maintainability
Standards and Compliance
Reference: “Designing for Reliability, Maintainability, and Safety – Parts 1, 2, and 3”, Circuit Cellar, December 2000, January 2001, April 2001.

## Slide 3: Introduction
Reliability, maintainability, and safety integral to product development
Tradeoffs between requirements and cost
Reducing probability of failure is expensive
Given little potential for personal injury, the primary consideration is manufacturing cost vs. potential customer unhappiness
There are UL, IEC, FCC standards (possibly others) to be met

## Slide 4: Component Failures
Electronic components can most often be modeled by constant failure rate ()
Leads to exponential failure distribution
Same probability of failure in the next hour regardless of whether it is new or used
but…see May 2011 IEEE Spectrum feature article on “Transistor Aging”

## Slide 5: Component Failures
Components do not “age” or “degrade” with use – constant failure rate unrelated to hours of use (under certain conditions)
Equivalent information is gained testing10 units for 10,000 hours vs. testing 1000 units for 100 hours
“Impossible” 10-9 failure as likely to happen in the first 5 minutes of operation as 114,000 years from now
Infant mortality reduced by robust designs, manufacturing process control, and “shake and bake”

## Slide 6: Definition of Failure Rate
Units: usually given in terms of unit failures per million hours, i.e., [10-6 units/hr) (given just one unit is involved)
Not really a probability, but rather an “expected value”
More intuitive way to describe: “unit failures per million hours per unit”, i.e., [fails/(106 hour  unit)]
Equivalent to:
  number of failures per unit per million hours
  number of failures/hour given 1 million units in field (assuming failed units are replaced)

## Slide 7: Definition of Failure Rate
Given p  10-6 [fails/(hr  unit)], N [units] in the field and T [hours]
  expected number of failures in T hours
    F (no. of failures) = p  10-6 fails/(hr  unit)  N units  T hours
    F = p  10-6  N  T failures (all other units cancel out)
  example: given 1000 units in the field (at all times), and p = 2  10-6, how many failures would you expect in one year?
    F = 2  10-6 fails/(hr  unit)  1000 units  (365  24) hours = 17.52

## Slide 8: Definition of Failure Rate
Given p  10-6 [fails/(hr  unit)], N [units] in the field and T [hours]
  expected number of failures in T hours
    F (no. of failures) = p  10-6 fails/(hr  unit)  N units  T hours
    F = p  10-6  N  T failures (all other units cancel out)
  suppose you are aiming for no more than one unit failure per week with 10,000 units in the field – what is an acceptable failure rate?
    F = p  10-6  N  T failures
    p  10-6 = F/(N  T) = 1 failure / (10,000  7  24 hrs) = 0.59510-6 failures per unit per hour

## Slide 9: Clicker Quiz

## Slide 10
How long is 106 hours?
  41,667 days
  1370 months
  114 years
  all of the above
  none of the above
Notes: 1-D

## Slide 11
Given a failure rate of 1 x 10-6 units/hr, should you be “happy” if a if a typical single unit only fails once in 114 years on average ?
  yes
  no
Notes: 2-A

## Slide 12
How long between unit failures will it be if you have 1 million units in use?
  0.1 hour (6 minutes)
  1 hour
  10 hours
  1,000 hours
  1,000,000 hours
Notes: 3-B

## Slide 13
Is this rate acceptable if this failure causes serious injury?
  yes
  no
Notes: 4-B

## Slide 14: Component Wear*
If, based on observation, failure rate does depend on time used, it may be due to wear caused by improper derating
Well-derated electronic systems seldom reach the point of wear-out failure
Well-derated = working at < 30-40% of specified ratings
Heat is the main reliability killer – even a small reduction will have a significant effect
*See also “An Odometer for CPUs,” IEEE Spectrum, May 2011

## Slide 15: Reliability Models for Components
Calculated value is p, the predicted number of failures per 106 hours of operation
Examples (Mil-Hdbk 217F):
Microelectronic Circuits
Diodes

## Slide 16
Microelectronic Circuits (see 5.1 p.23ff of Mil-Hdbk 217F)
(based on # of gates or transistors or on type of micro, e.g., 8bit, 16bit, etc)
Notes: C1 - based on # of gates or # of transistors

## Slide 17: Expectations for Homework
Choose hottest and/or most complex components
  Which are your hottest/most complex components?
Choose most closely related MIL-HDBK-217F model
List assumptions and rationale for parameter values used
Present information as table or bullet list

## Slide 18: MTTF/MTBF
For irreparable parts, use mean time to failure (MTTF) = 1/ for components with an exponential life distribution
For assemblies with repairable parts, mean time between failure (MTBF) is appropriate
Field returns are always a more powerful statement of performance than statistical predictions
Reliability models are conservative
  equipment generally outperforms the statistics (well designed equipment)

## Slide 19: Heat Controller Example
Gas-fired burner to maintain hot-tub water temperature within a specified tolerance
Possibility of personal injury if controller malfunctions
Performing hazard analysis and modifying the design based on results obtained
  important for showing “reasonable care” in court (reduction of liability)

## Slide 20: Heat Controller Example
Simple hazard analysis
10-9 generally accepted as “never” (50% chance of failure after 79,000 years of continuous operation)
BTW: with 1M units in field, never occurs once every 6 weeks

## Slide 21: Initial Circuit Design
What is the purpose of R3, Q1, and D5?

## Slide 22: Preliminary Failure Rate Calculation

## Slide 23: Improving System Availability
Components with greater failure rates than the rest (Q1, U1, U2, D5, T1, X1)
Q1, U1, U2 work at conservatively estimated junction temperature of 100°C
  efficient heat sinking can reduce junction temperature to 50ºC (∆T = Pdiss x Rth) T = Tambient + ∆T
Transzorb D5 & diodes D2, D3 conduct during infrequent transients only
  reduce their contribution by applying a duty cycle
Design T1 to run at a lower temperature to improve its reliability

## Slide 24: Improving System Availability
Implementing these steps
  Increase MTBF from 280,000 hours to 714,000 hr.
  p = 1.4 [failures/106 hours]
For the remaining analysis (Part 2), the results of these calculations will be used to evaluate and improve product safety

## Slide 25: The Rest of the Story…
Designing a functional product represents about 30% of the design effort
Making sure a product always fails in a safe, predictable manner takes the remaining 70%
Law of diminishing returns: exercise good judgment in adding safety features
Keep in balance: safety features and possibility of “nuisance alarms” (failures resulting from added complexity)
Utilize built-in self-test (BIST)

## Slide 26: FMEA
Bottom-up review of a system
Examine components for failure modes
Note how failures propagate through system
Study effects on system behavior
Leads to design review and possibly changes to eliminate weaknesses

## Slide 27: FMECA
Addition of criticality analysis
Not necessary to examine every component
  Multiple components may have same failure effect
Rearrange design into functional blocks
  consider component failures within those blocks that may be critical
Create chart listing possible failures
  block, failure mode, possible cause, failure effects, method of detection, criticality, and probability*
* probability calculation not required for homework

## Slide 28
Original Circuit
What would be the effect of a failure of R3, Q1, or D5?
(what if they fail open? shorted?)

## Slide 29
Power supply
*
Note: some causes of 0 V could be overheat, fire, or chemical
hazard, could then be a critical failure.

## Slide 30: Failure Cause/Mode/Effect/Criticality (use Circuit Cellar article for examples, but these are the course definitions)
Cause – failure of a device
  open circuit, short circuit, or change in device behavior
  for complex devices, could be failure of a particular feature (e.g., caused by “stuck at” fault of microcontroller port pin)
  list all components that could produce this failure mode
Mode – related to method of diagnosis
  observable or measurable behavior of component or sub-circuit resulting from a device failure.
  something you might observe when probing internals of the system with a multi-meter, scope, or logic analyzer.
Effect – external behavior of entire system
  for hot tub, it either overheats or under-heats the water
  for most systems – possibility of fire or damage to other components, external or internal
Criticality – how serious are the consequences
  High: _involves potential injury, requires rate ≤ 10-9_
  Medium (optional): _renders system unrepairable_____________
  Low: _inconvenience to user, required rate typically > 10-6______

## Slide 31
Original Circuit

## Slide 32
micro
temp. sense

## Slide 33
Original Circuit

## Slide 34
solenoid drive
D2

## Slide 35: High Criticality Failures
A2 – power supply over-voltage
A3 – power supply out of tolerance (too high or too low)
B2 – micro failure or software malfunction
C2 – temperature sensor
D2 – solenoid drive

## Slide 36: In Class Team Exercise
Part 1: Define criticality levels for your project
low
medium
high
Part 2: Identify one potential high criticality failure mode
descriptive name
potential cause
effect

## Slide 37: Fault Tree Analysis (FTA)
Purpose: estimate probability of a particular failure mode or set of failure modes
Top-down graphical analysis
Starts with top event of interest
Builds fault tree using Boolean logic and symbols
Incorporating known failure probabilities (same as used in FMECA) yields probability of event of interest
  OR probabilities added (accurate only for small probabilities)
  AND probabilities multiplied

## Slide 39: Probability of Failure
PF = 1 - e-t
For PF = 0.5 (50% chance of uncontrolled heating), it takes 22 years of operation given  = 3.5424 X 10-6
NOT GOOD ENOUGH FOR A SYSTEM THAT CAN POTENTIALLY CAUSE INJURY – NEED  = 10-9
(78,767 years for PF = 50%)
note: for small t, PF  λ

## Slide 40
Adding Hardware Monitors
(and monitors for the hardware monitors)
check thermistor voltage
monitor C5 voltage as a heartbeat check on PIC
wired OR of
comparators
bad notation
power-on-reset device monitors supply voltage, resets micro
Monitor L1/Q1/Q2 current
Allow micro to insert fault as a self-test

## Slide 41
Adding Hardware Monitor

## Slide 42: Added Redundancy
Microcontroller – performs sanity check on thermistor output
  short/open would cause voltage to move out of plausible range
  abrupt change in temperature would indicate fault
Comparators (monitor circuit)
  turn off Q2 if temperature exceeds upper limit
  provide window for plausibility testing of temperature sensor
Difficult part: eliminating dormant failures (all faults must be detected)

## Slide 43
Final Design
software monitors, built-in-test

## Slide 44
* assumes the analog circuitry can tolerate higher voltages
*

## Slide 45
IMPORTANT RESULT: All high criticality failures are monitored

## Slide 46
Final Design
-7

## Slide 47: Software and Watchdogs
Role of watchdog timer is to reset processor if “strobe timeout” occurs
Problem: watchdogs integral to microcontroller are no more reliable than microcontroller itself
External watchdogs “better”, but have to make sure that it is prevented from being strobed in the event of failures/bugs
Possible solution: make watchdog respond to a “key” (that would be difficult for failed software/bug to generate)

## Slide 48: Maintainability
Reliability predication indicates that after 10,000 units shipped, will need to service two problems per day
Keep customers happy with quick repair turn-around time (TAT)
Repair will most likely be by replacement (“line replaceable units” – LRU)
Maintainability analysis generates data showing the time needed to identify the faulty LRU, the time to replace it, and the time to re-test the system
Mean-time-to-repair (MTTR)

## Slide 49: Standards & Compliance
Many categories in consumer electronics:
Arcade, Amusement and Gaming Machines -- Bowling and Billiard Equipment -- Cable and Satellite Communication Equipment -- Circuit Components for Use in Audio/Video Equipment -- Commercial Audio and Radio Equipment, Systems and Accessories -- Low Voltage Portable Electronics; Household Audio and Video Equipment -- Musical Instruments -- Professional, Commercial and Household Use Equipment.
Example of a category relevant to ECE 477
  IEC 62368-1 Audio/Video, Information and Communication Technology Equipment – Safety Requirements. Published Jan. 2010, UL & CSA versions, Feb. 2011

## Slide 50: From electronicdesign.com
The ABCs of IEC 62368-1, An Emerging Safety Standard
Date Posted: October 22, 2010
Hazard Based Safety Engineering
Energy sources: electrical, thermal, kinetic, and radiated
To prevent pain or injury, either the energy source can be designed to levels incapable of causing pain or injury, or safeguards such as insulation can be designed into the product to prevent the energy transfer to the body part.