## Slide 1: Power supply
Design considerations

## Slide 2: Outline
DC-DC conversion and voltage regulation
    Buck: Regulating wall-wart/battery output to desired voltage
    Boost: Size constrained systems (Run off single AAA, for example)
Sources
  Plugged-in
    AC-DC conversion
      Short answer: use third party supplies
    DC-DC conversion
  Battery-based
    High current draw vs. Low current draw
    Rechargeable vs. non-rechargeable

## Slide 3: Voltage regulation – Why?
Variable voltage drop based on current draw
  Internal resistance, wire resistance
Spurious resets on current spikes
Signals are typically in supply range
  Rail-to-rail  Ground to VCC
    Narrower range is common
  Supply noise  Noisy signals

## Slide 4: Imaginary perfect regulator
Efficiency = 100%
  Input power = output power
Vin * Iin = Vout * Iload
  Vout is constant; no ripple
What do we have to give up in practice?
  Efficiency, High quality (low ripple), low cost/footprint
  Pick any two.
Efficiency
Low ripple/
quality of regulation
Cost/
footprint

## Slide 5: Linear regulators (including LDOs)
Two major categories
  Linear regulators (including LDOs)
  Switching regulators (aka switchers)
Linear regulators
  Wasteful (thermal waste of energy)
  Power dissipation = Vin * Iload
  Useful work = Vout * Iload
Small voltage buck and/or low load current
  5V  3.3V,
Efficiency
Low ripple/
quality of regulation
Cost/
footprint
Linear regulators

## Slide 6: Switching regulators
High efficiency
  85%-96%
Noisy
  Average voltage is well-regulated
  A/C noise component
Efficiency
Low ripple/
quality of regulation
Cost/
footprint
Switching regulator ($)
Switching regulator
($$$)

## Slide 7: Tips
For fixed voltage with very low dropout, look for custom regulator
  E.g. MCP 1700 with < 180mV dropout, up to 250mA
    Can get 3.3V regulation on LiPo batteries (3.7V)
Good old 78xx (fixed and variable regulators in family)
  2V dropout
Switching regulators
  Pre-packaged drop-in regulator (e.g., OKR-T/3-W12-C)
  7805 drop-in replacement (e.g., Murata 78xxSR)
Using discrete regulator ICs
  Delicate designs. Use passives and layout recommended in datasheet

## Slide 8: Heat Sink
Pay attention to heat thermal issues
  More important in Linear regulators
  Follow datasheet recommendations
    Will need understanding of current demands of your project

## Slide 9: Boost DC/DC conversion
Common case: Buck (step-down) regulation
Extreme low power:
  Operate on 1 AA battery or button cell
  Boost to more reasonable supply.
Typically low-current draw
  Maybe a sensor or low-duty cycle application
  Lots of boost converter ICs
  Attiny43U (Microcontroller with built-in boost converter)
    Operates down to 0.7V

## Slide 10: Battery power: Terminology
“Cell” single chamber of electrochemical reaction
Battery: array of cells
    Array size possibly 1
Primary: irreversible chemical reaction
  Chemical energy  electrical energy
  Non rechargeable
Secondary: chemical energy  electrical energy  chemical energy
  Rechargeable

## Slide 11: Characteristics of interest
Form factor : AA, AAA, 18500, 2032 etc
Voltage
Current draw
Capacity
  Not simple; depends on current draw
Leakage/Self-discharge
  Energy loss on the shelf
Energy density, power density

## Slide 12: Chemistry
Primary
Alkaline
  Cell voltage 1.5V
Button cell
  1.35-1.55V (Silver/Zinc/Mercury)
Lithium – Family of chemistries
  1.5-3.7V
Secondary
Lithum-ion (totally different from Lithium) 3.6-3.7V
NiCad 1.2V
NiMH 1.2V
Lithium-ion polymer (LiPo) 4.2-2.7V (Nom: 3.7V)
LiFePO4 3.2-3.3 V

## Slide 13: Capacity
500 mAH @ 3.7V
  50 mA for 10 hours
  25 mA for 20 hours
  500 mA for 1 hour
  5A for 6 minutes
  No!
Depends on discharge profile

## Slide 14: Non-rechargeable
Alkaline : Good old stuff
  AA, AAA, C, D : 1.5V
Lithium : Typically sold as ultra long-life
Do not ignore
Useful when:
  Relatively long useful life
  Relatively low current draw OR Relatively rare unplugged operation

## Slide 15: Other advanced issues:
Wireless charging:
  Inductive coupling
    Qi – broadly used in mobile industry
  Solar charging
In-circuit recharging
  Careful - charging profiles
  Serious safety issue (High energy density in personal devices)
Microcontroller-driven power management
Battery monitoring issues
Thermoelectric

## Slide 16: Backup battery
Very common use-case
  Normal use and battery recharge when plugged in
  Battery operation when not plugged in
    Seamless transition
Two assumptions
  Rechargeable battery
  Safe charging
What if non-rechargeable? (E.g., smoke alarms)
What if trickle charging is inadequate?

## Slide 17: Simple backup battery

## Slide 18: Power Management ICs
E.g. TI BQ24072 (For Li+)
Charging + Dynamic power-path
for battery backup
Other similar ICs for other
Chemistry
Note: Thermistor input

## Slide 19: Inductive coupling
Air core coupling
  High losses
  Fairly widespread standard : Qi
    Not available in small quantities
  Some hobby parts available
Magnetic material core
  Equivalent to transformer, but with separable coils
  Secondary coil in toothbrush; Primary coil and core in charging base

## Slide 20: Solar charging
Always use to drive battery charger
  Use battery to provide stable power supply
Size capacity to ensure statistical guarantees of availability
  Assume panel sized to fully-charge battery in 4 hours
  Probability of 4 hours of direct sunlight each day = 0.7 (say)
  Probability of 4 hours of direct sunlight in two days = 0.91 = 1 - (1-0.7) (1-0.7)
  Probability ...... 3 days > 0.97
  If battery sized for three days of operation, 97% probability of never running out.
  Similar process for more sophisticated weather/climate models

## Slide 21: Power management
Sleep/low-power states
  Important for battery-powered systems
Selective
  Some peripherals/sub-blocks in low-power states when not used
Whole chip
Questions to ask?
  Programmed wakeup? Via interrupts? Need physical wakeup?
  Is duty cycle low enough?

## Slide 22: Voltage Regulator (Selected data)
LM 117
  Adjustable voltage regulator
  Vout to Adj = 1.25V (Invariant)
  Negligible current through Adj
  Everything else follows
    Reason about voltage Vout

## Slide 23: Other Linear regulators
7805 : Very similar
  Simpler for fixed output
  Vout-Adj voltage = 5V
  Very similar reasoning
    Can be used to design adjustable regulators
    Can be used as current regulators
      Constant current source (LED drivers)

## Slide 24: Drop-in Replacement Switching regulator (DC-DC)
Pin compatible
Examples
  ReCom R-78Cxx-1.0
  Equivalent parts from Murata

## Slide 25: Step-Down Switching Converter: LM 2675
(fixed) 3.3, 5, 12 VDC and (adjustable) 1.21 – 37 V versions
Up to 1 amp
Up to 96% efficient
Five external components

## Slide 26: Battery monitoring
Simple voltage-based approach
Plateaus in discharge curve
Possibly depends on chemistry
Fuel gauge ICs
Source: Energizer.com

## Slide 27: Heat sink
Idea of THERMAL RESISTANCE
  Measured in ºC/W (temperature rise per watt dissipated)
  Lower thermal resistance is better
Thermal resistance is ~ inversely proportional to price
1W dissipation
Design goal: heat sink/junction temperature not to exceed 10º C above ambient temperature
Need a thermal resistance of approx 10º C/ 1 W  10
Airflow reduces thermal resistance