## Slide 1: ECE 477 Digital Systems Senior Design Project
Module 9
Board Assembly and Soldering Techniques
© 2014 by D. G. Meyer

## Slide 2: Outline
“I’ve got my board, now what?”
“Which end of this thing gets hot?”
“Flux is your friend.”
“Static is your enemy.”
“Do unto your iron, as you would have it do unto you.”
“Everything is awesome, everything is cool when we’re part of a team.”

## Slide 3: “I’ve got my board, now what?” - 1
Visually inspect board against printout of top/bottom copper
  Confirm footprint and drill size of all parts
    Minimum trace: 0.0049”
    Minimum space: 0.0045”
    Minimum finished hole size: 0.010”
  If necessary, use drill press in lab to drill out any holes that need to be enlarged (e.g., headers)
    Problem: your vias will already be plated!
  Look for shorted traces and traces that got etched away (will be limited need to do this)
    Using a sharp hobby knife, carefully scrape away copper that did not get etched between traces
    “Fly wire” any traces that got etched away
    If “major” problems – contact fab house for replacement

## Slide 4: “I’ve got my board, now what?” - 2
“Ohm out” traces, especially those with vias
  probably not essential if you used traces > 8mil
Install power supply components (diodes, voltage regulators, filter capacitors, etc.)
  never ever attempt to solder a “live circuit”
  test and “burn in” your power supply
  measure all supply voltages and look at them on an oscilloscope to determine how “quiet” they are
  make sure correct supply voltage appears at correct pins of each IC and that, under load (a resistor), are within tolerance
  note that some SMPS circuits will not function without a load – use an appropriately sized resistor

## Slide 5: “I’ve got my board, now what?” - 3
Install all bulk and bypass capacitors and test all supply rails again to make sure nothing got “shorted” in the process
Install microcontroller, reset circuit, crystal (or oscillator) circuit, flash programming header, and any other test points/headers
  power up the board and “smoke test” (hint: if the microcontroller starts to get warm real fast, something is wrong!)
  load a simple “heartbeat” program that toggles a port pin – verify basic functionality

## Slide 6: “I’ve got my board, now what?” - 4
Install RS232 level translator chip (where applicable) and associated components (9-pin D connector, capacitors, etc.)
  power up and “smoke test”
  load a simple program that “echoes” data to/from a virtual terminal – verify basic functionality “HELLO WORLD”
Add each interface circuit to your board block-by-block and “smoke test” each one as well as test/verify functionality

## Slide 7: “I’ve got my board, now what?” - 5
It is very important that each interface circuit be constructed and tested block-by-block!
Don’t add “new” circuitry until all the “existing” circuitry is fully functional!!
NOTE: If you need to “fly wire” any signal traces, use 30 gauge “wire-wrap” wire (use thicker wire, e.g., solid 24 gauge, for power and ground connections)

## Slide 8: “Which end of this thing gets hot?” - 1
Heat transfer: solder will flow from the colder region to the warmer region if it can
Secret
  choose the right iron tip (and temperature) so the warm region will be effective
  position the iron correctly so the solder flows in a path that makes sense
  provide an environment for the solder to flow – need flux and clean, smooth metal surface
  never ever attempt to solder a “live circuit”

## Slide 9: “Which end of this thing gets hot?” - 2
Tip selection
  different types: point, blade, chisel
  bottom line: want to “match” geometry of surface area warmed by tip with geometry of surface area to be soldered
    conical (point) tip  circular area
    screwdriver (blade) tip  rectangular area
    chisel tip  triangular region
  if the tip is too small, it is difficult to get enough heat transfer for the solder to flow
  if the tip is too large, the flow of solder cannot be contained in a small area

## Slide 10: Name That Tip
chisel (bevel)
screwdriver (blade)
conical (point)
bent chisel

## Slide 11: “Which end of this thing gets hot?” - 3
Tip selection
  note that chisel (bevel) and screwdriver tips can be very useful for:
    soldering groups of pins “at once” on surface-mount devices
    removing “solder bridges” among several pins at once
Basic soldering technique
  if needed, apply flux with pen/brush (e.g., for fine-pitch surface-mount components)
  heat area with iron tip (2-3 seconds)
  apply solder and allow to flow
  remove heat and allow to cool

## Slide 12: Using the Right Amount of Solder
Minimal b) Optimal c) Excessive
see http://www.elexp.com/t_solder.htm

## Slide 13: What’s Wrong With These Pictures?
see http://www.elexp.com/t_solder.htm

## Slide 14: What’s Wrong With These Pictures?
see http://www.elexp.com/t_solder.htm
Bad soldering of terminal wire

## Slide 15: What’s Wrong With These Pictures?
see http://www.elexp.com/t_solder.htm
Bad soldering of terminal wire
Bad soldering of PCB pad

## Slide 16: What’s Wrong With These Pictures?
see http://www.elexp.com/t_solder.htm
Bad soldering of terminal wire
Bad soldering of PCB pad
Bad soldering of both (solder did not flow properly)

## Slide 17: “Which end of this thing gets hot?” - 4
Solder removal (de-soldering)
  apply flux (if necessary)
  heat area to be de-soldered (surface-mount parts require a special heat gun to do this)
  use solder wick (copper braid) or “solder sucker” to remove solder
Cautions
  “cold” solder joints (solder did not flow)
  too much heat (components will be damaged and/or traces will peel off board)
  access (be careful about assembly order!)
  examine solder joints of surface mount components using microscope

## Slide 18: “Flux is your friend.”
Flux is a liquid in which solder can flow
Most “electronic” solder contains some flux
Without flux, solder will be pasty and sticky (refuse to flow)
The secret to soldering is using flux to make solder flow, and then controlling the heat so it flows under control

## Slide 19: “Static is your enemy.”
Many of the parts you will be using are static sensitive (can be damaged by ESD)
To avoid damaging your components, do all of your board construction on the anti-static (gray or blue) mats in lab
When soldering, use an anti-static wrist band and make sure it is connected to ground

## Slide 20: “Do unto your iron, as you would have it do unto you.”
Wet the sponge with distilled water before you begin
Choose the iron with the appropriate tip for the job and set the temperature accordingly (bent chisel is a good place to start)
Tin and clean the tip before starting
Clean the tip frequently during use
Tin the tip when you are finished and TURN OFF the iron
Use soldering irons only for soldering!

## Slide 21
conical (point) tip

## Slide 22
screwdriver (blade) tip

## Slide 23
chisel (bevel) tip

## Slide 25: “Everything is awesome, everything is cool when we’re part of a team.”
Professional SMT Soldering Demo
Fine Pitch Drag Soldering
Leaded vs. Lead-Free Solder
Circuit Board Manufacturing
SMD Removal Using a Chip Quik Kit
Everything is Awesome!