## Slide 1: Practical Software Design Topics

## Slide 2: Oscillators and Clocks
Arguably the most important configuration for an embedded system
All systems depend on clock configuration
Should be the second block initialized
  The first is the watchdog timer
Higher clock speed means more computations per second and more power use
What does a typical oscillator block look like? (next slide)

## Slide 3
32 kHz Crystal
FLL/PLL
Hi Freq. Crystal
Main Clock
Peripheral Clock
CLOCK BUS

## Slide 4: Simple Pseudocode
// 32 kHz watch crystal input on XT1
OSC_1_CONFIG_REG = CHOOSE_XT1;
// 32 kHz watch crystal = 32,768 Hz
// 32,768 Hz * 64 = 2,097,152 Hz (~2 MHz)
PLL_CONFIG_REG = CHOOSE_OSC_1 + MULTIPLY_BY_64;
// Main clock ~2 MHz
MAIN_CLK_CONFIG_REG = CHOOSE_PLL + DIVIDE_BY_0;
#define MAIN_CLOCK_FREQ 2097152 // in Hz
// Peripheral clock ~500 kHz ( 2097152 / 4 = 524288 )
PERIPH_CLK_CONFIG_REG = CHOOSE_PLL + DIVIDE_BY_4;
#define PERIPH_CLOCK_FREQ 524288 // in Hz

## Slide 5: What’s with the #define???
// Set up the system timer interrupt at 1048 Hz
unsigned short divider = PERIPH_CLOCK_FREQ / 1048;
// 500.27 in this example -> 500 after integer truncation
TIMER_1_CONFIG_REG = CHOOSE_PERIPH_CLOCK + divider;
If peripheral clock changes later, this code will NOT need to be modified
Creates a robust software design
These ideas aren’t just limited to clocks and timers (external component values, etc.)

## Slide 6: More #define Tricks
Get input from GPIO
#define BUTTON_1_MASK 0x04
#define BUTTON_1_PRESSED ( PORT1_IN & BUTTON_1_MASK )
Drive output pins
#define LED_1_MASK 0x20
#define LED_1_ON ( PORT1_OUT |= LED_1_MASK )
#define LED_1_OFF ( PORT1_OUT &= ~(LED_1_MASK) )
if( BUTTON_1_PRESSED ) {
LED_1_ON;
} else {
LED_1_OFF;
}

## Slide 7: More #define Tricks
Use macros to inline simple functions
// Utilize truncation to round a number
#define MAX( x , y ) ( (x) > (y) ? X : y )
if( MAX( adc_val_1 , adc_val_2 ) > 255 ) { ... }
Create settings
#define __DEBUG_MODE__
#ifdef __DEBUG_MODE__
printf( “Debug mode ON\n” );
#endif
Error messages during compile time
#error Useful to use with different settings options.