## Slide 1: ECE 477 Digital Systems Senior Design Project
Module 3
Microcontrollers for Embedded Applications
© 2013 by D. G. Meyer

## Slide 2: Outline
General C Selection Guidelines
  Memory Requirements / Types
  Development Environment
  Interfacing / Bus Expansion
PIC Microcontrollers
Atmel Microcontrollers
Freescale Microcontrollers
Analog Devices DSPs
ATOM Boards
ARM Modules

## Slide 3: General C Selection Guidelines
Memory requirements/types
  Beware of hidden liabilities
    Data acquisition (ADC) buffers
    Large file storage (mp3)
    Library routines (floating point emulation, printf)
  Nonvolatile memory
    Flash (code, static data)
      in-circuit programmable?
      programming “dongle” availability?
      programming connector requirements?
    EEPROM (storage of calibration or configuration parameters, history data, control panel settings)
      granularity of erase/write?
      software driver availability?

## Slide 4: General C Selection Guidelines
  Volatile memory (SRAM)
    stack
    heap
    I/O buffers
    run-time variables
    (generally no executable code except for “specialty functions” like erasing and reprogramming a sector in Flash)
    note initialization requirements when system boots

## Slide 5: General C Selection Guidelines
Interfacing/Bus Expansion
  Number of general purpose I/O pins
    programmable data direction?
    programmable pull device?
  Bus expansion capability
    multiplexed or simplex external bus?
    “glue logic” requirements?
Number/types of integrated peripherals (objective: want to “match” project requirements to C capabilities)

## Slide 6: General C Selection Guidelines
Development environment
  Useful to have an asynchronous serial port dedicated to debugging
  Useful to have spare I/O pins dedicated to debugging (e.g., “heartbeat” LED)
  In-circuit programmable Flash available for quickly downloading and testing code revs (but typically require a “programming dongle” so be sure to include a header/connector on your PCB)
  BDM (background debug mode) VERY helpful be sure to include a 6-pin BDM header on your PCB if using a Freescale microcontroller
  Assembler/Compiler/Linker/Loader/(Simulator)?

## Slide 7: General C Selection Guidelines
Carefully note package options available
  QFP, SOIC, and SSOP types generally preferable
  QFN type “doable” (but avoid if possible)
  watch out for “tabs” on bottom of chip
  DIP types OK (good for prototyping) but compromise PCB density
  avoid PGA and BGA
Price/availability
  get at least two more than you need of every IC
  now (sooner rather than later)

## Slide 8: Package Options (Sample)

## Slide 9
http://www.microchip.com

## Slide 12
www.atmel.com

## Slide 14
Parametric Product Table

## Slide 15
Parametric Product Table…

## Slide 16
www.freescale.com

## Slide 18
Freescale 16-bit Parametric Product Table

## Slide 19
www.analog.com

## Slide 21
http://www.intel.com/products/processor/atom/index.htm

## Slide 22
http://www.keil.com/mcb2300/mcb2370.asp