## Slide 1: ECE 477 Digital Systems Senior Design Project
Module 4
Power Supply Design
© 2014 by D. G. Meyer

## Slide 2: Outline
Switch mode power supply theory
  forward converter
  flyback converter
Switching regulators
  step-down switching converter
  step-up switching capacitor charge pump
DC-DC converters
Battery management
Taking the heat

## Slide 3: Switch Mode Power Supply (SMPS)
Switching approach based on high-frequency voltage  A.C. input (line voltage) immediately rectified to produce high-voltage D.C.
Chopper FET creates a high-frequency signal fed to transformer
High frequency  smaller transformer (less metal, less weight, lower cost)…but, more components
Adjusting chopper’s duty cycle provides regulation
input rectifier
chopper
isolation
output rectifier
output filter
isolation
control

## Slide 4: Basic Forward (Buck) Converter
Forward (“buck”) converter transfers energy while the chopper is conducting
Transformer provides secondary charging circuit during conduction phase (chopper on)
When chopper turns off, choke releases its magnetic energy and current continues to flow into output capacitor
+

## Slide 5: Basic Flyback Converter
Note phase of isolation transformer – while the chopper is conducting current in the primary, current is not allowed to flow in the secondary
Primary becomes storage device opposing current flow by creating a magnetic field
When chopper turns off, stored magnetic field collapses and energy is transferred to the secondary
+

## Slide 6: Switching Regulator – Basic Idea
Regulation achieved by changing pulse width and/or pulse frequency
Done “automatically” by switching regulator IC
Typically over 90% efficient
TRADEOFF: lower current output than typical linear regulator circuit, and more external components; also, higher noise
Vout
feedback
+

## Slide 7: Step-Down Switching Converter: LM 2675
(fixed) 3.3, 5, 12 VDC and (adjustable) 1.21 – 37 V versions
Up to 1 amp
Up to 96% efficient
Five external components

## Slide 8: Step-Down Switching Converter: LM 2675

## Slide 9: Step-Down Switching Converter: LM 2675

## Slide 10: Step-Down Switching Converter: LM 2675

## Slide 11: PCB Tutorial Exercise

## Slide 12: PCB Tutorial Exercise

## Slide 13: PCB Tutorial Exercise

## Slide 14: PCB Tutorial Exercise
Standard 1206 type surface mount ceramic capacitor

## Slide 16: Switched Capacitor Charge Pump Step-Up Converter
Based on LTC1263 www.linear-tech.com
Produces 12 VDC @ 60 mA from VCC as low as 4.75 V
Four external components

## Slide 18: Important Notes About DC-DC Converters
While chip size and heat dissipation are reduced, component properties and physical layout become more critical…
  Inductors and output capacitors typically need to be “low ESR” type – pay close attention to component data sheets
  “Analog” ground for DC-DC must be separate from all other grounds on PCB
  Certain nodes in layout are critical to keep traces short and wide to reduce parasitic inductance and capacitance
  Failure to follow manufacturer’s recommended layout and component selection criteria will (most likely) result in non-operation of the circuit and many hours spent in debugging and fly-wiring

## Slide 23: Taking the Heat
Sometimes a properly sized HEAT SINK is required to help a discrete device dissipate heat
Idea of THERMAL RESISTANCE  measured in ºC/W (temperature rise per watt dissipated)  “lower thermal resistance is better”
Thermal resistance is ~ inversely proportional to price.

## Slide 24
Source: http://www.mouser.com

## Slide 25: More Thought Question Analysis
Need to pick properly sized HEAT SINK to help device dissipate heat
Idea of THERMAL RESISTANCE  measured in ºC/W (temperature rise per watt dissipated)  “lower thermal resistance is better”
Example: For first case analyzed (6 VAC secondary), let’s say we don’t want heat sink/junction temperature to rise more than 10º C above ambient temperature  need a thermal resistance of approx 10º C/ 3.5 W  3
Thermalloy choice “B” comes close (3.4) – see chart

## Slide 27
3.4

## Slide 28: More Thought Question Analysis
Need to pick properly sized HEAT SINK to help device dissipate heat
Idea of THERMAL RESISTANCE  measured in ºC/W (temperature rise per watt dissipated)  “lower thermal resistance is better”
Example: For first case analyzed (6 VAC secondary), let’s say we don’t want heat sink/junction temperature to rise more than 10º C above ambient temperature  need a thermal resistance of approx 10º C/ 3.5 W  3
Thermalloy choice “B” comes close (3.4) – see chart
What if we’re “cheap” (only want to spend $0.43 for the heat sink instead of $1.66)? – choice “R” has a thermal resistance of 24  will experience 24 x 3.5 = 84º C temperature rise – ouch!!
P.S. Don’t forget to use HEAT SINK COMPOUND

## Slide 30
24