## Slide 1: Rear Axle Module
EV Kart Manual
EPICS

## Slide 2
Table of Contents
Topic | Page
Overview | 3
Tools | 4
Parts | 5
Understanding Tools Nomenclature | 8
Step 1: Bearings | 9
Step 2: Cassettes | 11
Step 3: Axle | 20
Step 4: Wheel Hub | 27
Appendix and References | 32

## Slide 3
Overview
1
2
3
4
This module will be divided into four steps:
  Bearings
  Cassettes
  Axle
  Wheel Hub

## Slide 4: Tools
Required Tools for Module
1.
3.
2.
4.
5mm and 6mm Allen Wrench
Tape measurer
13/17mm wrench
10,13,17mm socket wrench set
(Optional) Rubber Mallet for adjusting axle height

## Slide 5: Parts
Required Parts for Module
50mm Aluminum Bearing Cassette
Economy Caliper Bracket
Brake Caliper Spacer
M8x1.5x25mm Cassette Bolts
D.30 Brake Caliper
Economy Caliper Bolt M10 x 110
50mm PKT Axle

## Slide 6: Parts
Required Parts for Module
Brake/Sprocket Hub Pinch Bolt M6 x 30
50mm Complete Brake Disc
M6 x 10 Set Screws
50mm Rear Wheel Hub Aluminum
30mm Sprocket Carrier
Engine Stop Bolt
M8 Flat Washer
50mm (ID) Axle Bearing

## Slide 7: Parts
Required Parts for Module
2 Peg Key
Brembo Brake Hub
M10 Nylon Nut
M8 Nylon Nut
M10x45 Cap Bolt
Economy Bracket Caliper Spacer

## Slide 8
Understanding Tool Nomenclature
Metric Terminology:
Example:
*all measurements in this guide will exclude pitch and fit classification

## Slide 9: Step 1: Bearings (0:36-1:24)
Rear Axle Assembly
Note: if bearings come pre-installed, skip this step.

## Slide 10
1.1
Brake / Sprocket Hub Pinch Bolt M6 x 30
50mm Aluminum Bearing Cassette
Check that the M6x30 pinch bolt is loosened.
Use a 5mm Hex key if needed.
5mm Hex Key
Pinch Bolt

## Slide 11: Step 2: Cassettes (1:25-3:16)
Rear Axle Assembly

## Slide 12
2.1
Bolt Washer Prep
Prep a washer and M8x25mm bolt by placing the washer onto the bolt shank, such that the washer sits directly behind the bolt head. Repeat this for 12 washer-bolt pairings.
M8 Washer
Shank
M8x25mm Cassette Bolts (12)
Bolt with washer:

## Slide 13
2.2
Cassette Installation
Place the cassette into the frame hanger so that the set screws section of the bearing is facing inwards.
Cassette with Bearing
Set screw section
Cassette in frame hanger oriented correctly

## Slide 14: Cassette Bolts
2.3
M10 Flat Washer (18)
Insert cassette bolt with washer into the right-most bottom hole.
Screw in by hand until it remains firmly in hole without additional support.
Repeat for remaining 5 holes, starting with the bottom row and working upwards by row.
Note that the top row of holes should remain open.
*start with the motor side and repeat for brake side
4
2
3
1
M8x1.5x25mm Cassette Bolts (12)
Numbers indicate order of insertion of bolts​
13mm Wrench

## Slide 15: Cassette Bolts (pt2)
2.3
M10 Flat Washer (18)
4. Go back and tighten all bolts by hand until the washer is snuggly pressed between the cassette and the bolt head.
5. Finish tightening all bolts with a 13mm wrench.
6. Repeat exactly for brake side.
*start with the motor side and repeat for brake side
4
2
3
1
M10x1.5x25mm Cassette Bolts (12)
Numbers indicate order of insertion of bolts​
13mm Wrench

## Slide 16: D.30 Caliper Bracket Prep
Economy Bracket Caliper Spacer
Economy Caliper Bracket
M8x45 Cap Bolt
2.4
Prep a spacer and caliper bracket by inserting a M10x45 bolt through the middle hole of the caliper bracket so that the bolt head is pressed against the caliper bracket.
Then put the spacer on the threads of the bolt so that the caliper bracket is sandwiched between the spacer and the bolt head.
16

## Slide 17: Economy Caliper Bracket Instillation
On the inside of the brake side cassette, attach the caliper bracket to the top holes by inserting the prepped caliper with spacer and bolt into the top right hole and tightening by hand until the spacer is firmly held between the caliper bracket and the cassette.
50mm Aluminum Bearing Cassette
Prepped Economy Bracket
2.5a
17

## Slide 18: Economy Caliper Bracket Instillation
For the second bolt of the caliper bracket, first hold a spacer in front of the left hole so that it is sandwiched between the caliper and cassette. Then insert the bolt through the caliper, spacer, and cassette.
Place an M8 Nylon nut on the backside of each bolt and tighten by hand as much as possible.
50mm Aluminum Bearing Cassette
Prepped Economy Bracket
2.5b
18

## Slide 19: Brake Caliper Installation
Insert an M10x110 bolt with M10 washer into the front hole of the economy caliper bracket. Then push it through the entire brake caliper. Repeat for bottom hole of economy caliper bracket.
Place an M10 nut on the backside of each bolt and tighten with 17 mm Allen Wrench.
2.6
1
2
Brake Caliper
M10x110 bolt
M10 Washer
19

## Slide 20: Step 3: Axle (3:18-6:25)
Rear Axle Assembly

## Slide 21: Axle Alignment
1.Stand behind the kart on the brake side.
2. Insert the axle into the brake-side bearing and push it through until it is directly in front of (but not through) the motor-side bearing.
3. The axle should be directly aligned with the opening of the opposing bearing. If it is not aligned, then adjust the axle by hitting it in the direction opposite of misalignment.
4. Remove axle from bearings and repeat exactly on the motor side.
5. After aligning the axle on both sides, insert the axle through both bearings, starting from the motor-side bearing. Make sure that the axle is still moving easily through the bearings.
6. Tighten both cassette pinch bolts with a 5mm hex key.
3.1
21

## Slide 22: Brake Disc Installation
50mm Complete Brake Disc
3.2a
Stand behind the kart with the brake disc in your left hand. With your right hand, slide the brake pad side of the axle out of its bearing.
Position the brake disc between the brake caliper and the axle, with the pinch bolts of the brake hub facing right (towards the chassis).
Keyway Under Brake Disk
22

## Slide 23: Brake Disc Installation
50mm Complete Brake Disc
3.2b
Keyway Under Brake Disk
Then slide the axle through the disc so that the keyway is on the axle. Once the disc is held in place, insert key into the designated spots on the axle. Continue sliding the axle back through the brake caliper and bearing until the key is inserted fully into the keyway.
2 Peg Key
23

## Slide 24: Centering Axle
30mm PKT Axles
Tape Measurer
3.3
Center the axle. Use a tape measure to determine the length of the axle extending past the bearing on each side of the kart. Shift the axle so that the length is the same on both sides.
Measure distance between axle end and bearing
24

## Slide 25: Secure Axle Position
50mm PKT Axles
4mm Allen Wrench
3.4
Tighten the set screw of each bearing using a 4mm Allen Wrench. Tighten until you feel the set screw contact the axle, then tighten another half a turn.
Bearing Set Screw
25

## Slide 26: Secure Brake Disc
5mm Allen Wrench
3.5
Center the brake disc over the brake pads. After centering, tighten the brake disc hub's two pinch bolts with a 5mm Allen wrench.
M6x30
Brake Disk Pinch Bolt
Brake Disk Centered Between Brake Pads
26

## Slide 27: Step 4: Wheel Hub (6:26-7:35)
Rear Axle Assembly

## Slide 28: Wheel Hub Keyway Installation
4.1a
Place the key onto the end of the axle and push the 50mm rear wheel hub onto the end of the axle until it stops.
*start with the brake side and then repeat for motor side as instructed in next steps.
Key under wheel hub
2 Peg Key
28

## Slide 29: Brake Side Wheel Hub Installation
4.1b
Tighten the two M6x30 pinch bolts with an 6mm Allen wrench.
*start with the brake side and then repeat for motor side as instructed in next steps.
Pinch Bolt
Brake/Sprocket Hub Pinch Bolt M6 x 30
6 mm Allen Wrench
29

## Slide 30: Sprocket Installation
50mm Sprocket Carrier
4.2
1. For the motor side, place the axle keyway closest to the bearing and slide the sprocket over it.
2. Repeat keyway and wheel hub installation on the motor side as instructed in 4A and 4B.
Key under sprocket hub
2 Peg Keyway
Installed sprocket
30

## Slide 31: Motor Mount Stop Bolt
4.3
Place an M10 nut on the threads of the motor mount stop bolt.
Insert the bolt with nut into the side of the frame hanger, as instructed in the image to the right.
M10 Motor Stop Bolt x 30
6 mm Allen Wrench
Bolt Goes Here
31

## Slide 32: Appendix and References
Rear Axle Assembly

## Slide 33: Top Kart Video Demonstration
33