## Slide 1: Generation of Empirical Tight Binding Parameters from ab-initio simulations
Yaohua Tan, Michael Povolotskyi, Tillmann Kubis, Timothy B. Boykin* and Gerhard Klimeck
Network for Computational Nanotechnology, Purdue University
*Department of Electrical and computer Engineering, University of Alabama in Huntsville

## Slide 2: Motivation
Nano electronic devices
complicated 2D/3D geometries;
10000 ~ 10 million atoms in the active domain;
many materials are used.
Candidate methods for device-level simulations
Ab-initio methods
Empirical methods
 efficiency should be considered

## Slide 3: simulation time and accuracy
Simulation time
Error
(compared with Experiment)
LDA /GGA
GW/BSE
sp3s* TB
sp3d5s* TB
Device-level calculations are possible
Depend on
parameters
Empirical TB
ab-initio methods
Empirical Tight Binding
can be fast and accurate enough
 Easier for device level calculations

## Slide 4: Brief summary: empirical TB vs ab-initio methods
 | Empirical TB | Ab-initio methods
Computation load | light | heavy
Application to quantum transport | Widely used | demonstrated by some works.
Parameterization | Empirical | Non-empirical
Explicit basis functions | No | Yes
Issue: How to get TB parameters for new materials?
TB parameters of commonly used semiconductors are obtained.
J. Jancu, et al., PRB 57 6493
T. Boykin, et al., PRB 66 125207

## Slide 5: How to get TB parameters for new materials?
By fitting to experimental band structures.
Demonstrated working for many situations
Ab-initio calculations
+ TB parameters construction
Disadvantage: (for exotic materials)
insufficient experimental data;
TB basis remains unknown.
Advantage:
less empirical;
can get TB Basis functions.
Disadvantage:
Dependent on ab-initio calculations.
Require reliable ab-initio calculations;
GW / hybrid functional / bandgap correction;
J. Jancu, etc, PRB 57 6493
T. Boykin, etc, PRB 66 125207
Traditional way:
This work:

## Slide 6: Method
Step: ab-initio calculation  Ei(k), φi,k(r), Hab-initio
2. Step: Define analytical formula for TB basis functions n,l,m (r,,) = Rn,l(r)Yl,m(,) Yl,m(,) is Tesseral function, Rn,l(r) is to be parametrized
Ab-initio band structure Ei(k)
Wave functions φi,k(r)
Yl,m(,)

## Slide 7: Method (continue)
Step: Parameterize Rn,l(r)
get transform matrix U: ab-initio basis  TB basisn,l,m
4. Step:
basis transformation (low rank approximation):
Hab-initio  HTB
Approximate HTB by two center integrals;
Step:
Compare the TB results (band structure, wave functions) to ab-initio results; Measure the overlaps of basis functions;
J. Slater & G.Koster PR. 94,1498(1964)
A. Podolskiy & P. Vogl PRB 69, 233101 (2004)
Iteratively optimize the TB results

## Slide 8: Band structure of Silicon
The Silicon is parameterized using 1st nearest neighbor sp3d5s* model.
ABINIT is used to perform the DFT calculations
Band gap is corrected by applying scissor operator
Most of the important bands agree with the DFT result!

## Slide 9: Basis functions and wave functions of Silicon
Real space WFs of top most valence bands
Si
Si
Si
Radial parts of TB Basis functions
TB Basis functions are obtained;
Selected TB eigen states are fitted to the corresponding DFT eigen states.
Properties beyond traditional Empirical TB
High probability  Si-Si bond

## Slide 10: band structure of bulk MgO
sp3d5s* model with 2nd NNs coupling is used
Application to new material MgO.
(No existing reasonable parameters.)
Most of the important bands agree with the DFT result!

## Slide 11: Strained Silicon
biaxial strain ( )
Strain dependent basis functions
Energy of conduction bands under Biaxial strain
Energy of valence bands under Biaxial strain
The behavior of strained Silicon are accurately reproduced!

## Slide 12: conclusion
We develop a method Generating TB Parameters from ab-initio simulations
Works for typical semiconductors like Si;
Provides basis functions and TB eigen functions.
Works for new materials like MgO;
Works for more complicated materials like Strained Si.

## Slide 13
Thanks!

## Slide 14: Si TB Parameters
Parameters | Value | Parameters | Value
Es | 3.3219 | Vsdσ | -2.1014
Ep | 11.4168 | Vs*dσ | -0.3168
Es* | 24.1262 | Vppσ | 3.7130
Ed | 24.1313 | Vppπ | -1.4575
∆SO | 0.0183 | Vpdσ | -1.9827
Vssσ | -2.0060 | Vpdπ | 2.2269
Vs* s*σ | -1.9115 | Vddσ | -3.2916
Vss*σ | -0.2093 | Vddπ | 4.0617
Vspσ | 2.4967 | Vddδ | -2.2975
Vs*pσ | 1.9978 |  | 

## Slide 15: Appendix
Basis functions definition:
transform matrix U:
TB Bloch functions:
basis transformation: