## Slide 1: Theoretical and Experimental Study on Graphene Nanoribbon Tunneling Transistor
  SungGeun Kim
  Advisor: Prof. Gerhard Klimeck
    Electrical and Computer Engineering
    Purdue University
1
Please do not distribute.

## Slide 2: Outline
Challenges for conventional transistor
  Size scaling
  Supply voltage scaling
TFET as a solution for low power operation
Why GNR TFET?
Challenges to GNR TFET
  Doping
  ON/OFF current
  Edge-roughness
Summary/Conclusion
LG
Vdd
Credit: Mehdi Salmani
i
Metal
p+
n+
G
Oxide
D
S
log10DOS
Therm.
Therm.
Tunn.
Edge roughness effects
S
D
Vd
Id
C
H
98% tunneling current
→SS degradation
Electrostatic Doping
Notes: geometrical scaling

## Slide 3: Transistor Scaling
Transistor is driving the size and power scaling of electronic devices.
Size Scaling
Power Scaling
Voltage scaling 240V→1.6V
Size scaling ~cm→~nm
Transistor
www.goldstardsimulations.com
2013
Vacuum tube (Eniac)
computermuseum.li
1946
www.nokiainnovation.com
intel.com
microsoftstore.com
CPU
intel.com

## Slide 4: Future Projection for Transistor Scaling
ITRS projects that size/supply voltage scales significantly in the future.
LG
Vdd
chipworks
ITRS 2012
DIBL increase
S-to-D tunneling
Short channel effects
75%↓
25%↓
Vth shift
SS degradation
ON-current reduction
Notes: conduction band edge profile

## Slide 5: Transistor Performance Projection of ITRS
ITRS2012
ON-current increase as LG↓
ITRS 2012 (MASTAR)
Analytical model based on drift-diffusion
No 2D electrostatic
No realistic quantum effects
Mobility/vsat fitting
Ion as a target
Channel
Oxide
Drain
D
S
Gate
Source
Bulk
SOI
DG
IOFF=0.1 μA/μm

## Slide 6: Analytical Modeling vs. Quantum Transport
ITRS2012
DD/QT Simulation Results-ITRS2014
SOI/DG Data: Mehdi Salmani
Reducing channel length of Bulk/SOI/DGFET degrades ON-current.
ON-current increase as LG↓
ON-current decrease as LG↓
Ballistic
+Scattering
QCDD
IOFF=0.1 μA/μm
IOFF=0.1 μA/μm
Drift diffusion with quantum corrections (IEEE, TED, submitted)
confinement (calibrated with 1D Schroe.-Poisson)
ballistic mobility (good match with exp.)
quasi-ballistic transport (calibrated with M.C.)
Calibrated with exp. (Samsung 20 nm/Intel 32 nm)
Ballistic+Scattering
Quantum transport: ballistic
: mean free path calculated from experimental mobility
Series Resistance: ION reduction by 33% (same as previous ITRS)
Notes: Ioff=0.1uA/um

## Slide 7: Short Channel Effects/S-D tunneling
Significant short channel effects (DIBL, S-to-D tunneling effects)
SOI/DG Data: Mehdi Salmani
Barrier Controlled Device has NO Barrier??
@OFF
(%)
We may need a fundamentally different device structure
that can utilize tunneling!
98% tunneling current
→SS degradation
Notes: Itunneling/Ioff
Put arrows correctly

## Slide 8: Slow Supply Voltage Scaling
Much slow supply voltage scaling? Why?
Obstacle: short channel effects
ITRS 2012
75%↓
25%↓
Notes: put the arrows opposite direction

## Slide 9: Fundamental Limit of Conventional Transistor
Vg↑
log f(E)
Hot injection
Reducing supply voltage has big impacts on on-current
because of SS>60 mV/dec limit.
SS≥60 mV/dec
Vg
Vdd
log Id
0
Hot injection limits the SS of conventional transistors.
p
Metal
n+
n+
Oxide
D
S
Vg
Id
x
E
Ef
Need completely different structure/material

## Slide 10: Tunneling Transistor for Low Power
Cold injection is necessary for sub-60mV/dec operation.
Vdd can be scaled more aggresively
Vg
Vdd
log Id
0
log f(E)
Ef
Cold injection
SS=60 mV/dec
Conv.
TFET
i
Metal
p+
n+
G
Oxide
D
S
Solve the power problem!
10
Structure
P=fCVdd2
T(E)

## Slide 11: Choice of Material/Structure for Good TFET
Low bandgap
Low effective mass
better gate control (1D)→ small screening length
i
Metal
p+
n+
G
Oxide
log f(E)
Ef
Cold injection
Good TFET
11
Material
Graphene nanoribbon
T(E)
Eg
A. Seabaugh, Proceedings of the IEEE, 2010
λ

## Slide 12: GNRTFET Experiment
Many theoretical studies have been presented, but no actual experimental realization of GNRTFET before.
Collaboration with University of NotreDame
  Challenges in doping GNR
  Challenges in creating p-n junction
Dr. Wansik Hwang, Dr. Susan Fullerton
GNRTFET experiment
Notes: before

## Slide 13: Challenge in Doping GNRs
i
Metal
p+
n+
Gate
Oxide

## Slide 14: Challenge in Doping GNRs
Chemical doping: D. B. Farmer et al., APL, 2009
Metallization: B. Huard, et al., PRB, 2008
Substrate doping: H. E. Romero, ACS Nano, 2008
Difficult in controlling at nano-scale
Not easy to reproduce
Metal
Gate
Oxide

## Slide 15: GNRTFET Structure with Electro-static doping
Electrostatic doping with PEO: easy to control in nanoscale
Very efficient doping method: high charge density (Philip Kim, 2007)
W. Hwang, et al., ND
PEO: Polymer Electrolyte
n/p>1014cm-2

## Slide 16: ID-VBG Characteristics
W=10 nm
VG1
VG2
P
N
Efficiency of doping in GNR with side gates
GNR is originally p-type.

## Slide 17: ID-VBG Characteristics
P
N
Efficiency of doping in GNR with side gates
GNR is originally p-type (on SiO2).
Double dips in Id-Vg shows p-n junction characteristics.
EfS
EfD

## Slide 18: Experiment vs. Drift-diffusion (NotreDame)
First experimental data that shows NDR in GNRTFET.
NDR tells that there is a p-n junction with very high doping concentrations.
Drift-diffusion simulation gives a qualitative picture, but not quantitative one: quantum transport simulation needed.
Experiment
Drift-diffusion (ND)

## Slide 19: ID-VD at VBG=0 V
Experiment
EfS
EfD
VDS=0 V
P++++
N
VBG=0 V
EfS
EfD
VDS=1 V
VBG=0 V
Tunneling branch
GNR on SiO2 is p-type doped.
Asymmetric doping explains “non”-NDR behavior

## Slide 20: Experimental Id-Vd Characteristics with NDR
Asymmetric doping explains “non”-NDR behavior
Experiment
EfS
EfD
VDS=0 V
P++++
N
VG=0 V
Thermionic branch
hole

## Slide 21: Experimental Id-Vd Characteristics with NDR
Maximum NDR peak occurs when effective doping is symmetric.
NDR due to Esaki-diode like behavior.
Experiment
EfS
EfD
VDS=0 V
P++++
N
VBG=0 V
VBG=1.5 V
P++
N++

## Slide 22: Experimental Id-Vd Characteristics with NDR
Maximum NDR peak occurs when the doping is symmetric.
NDR due to Esaki-diode like behavior.
Experiment
EfS
EfD
VDS>0 V
Esaki-diode
EfS
EfD
VDS=0 V
P++
N++
VG=1.5 V

## Slide 23: Id-Vd Characteristics: NDR
Experiment
Maximum NDR peak occurs when the doping is symmetric.
NDR due to Esaki-diode like behavior.
EfS
EfD
EfS
EfD
EfS
EfD

## Slide 24: Quantum Transport Simulation vs Experiment
VG
EfS
EfD
N++
P++
P
N
G1
G2
30 nm
30 nm
Open questions
  Can quantum transport model capture Id-Vd quantitatively?

## Slide 25: Graphene Modeling (pz vs p/d tight binding)
p/d
  Better match with DFT than simple pz.
  Explicit treatment of hydrogen atoms
Bandgap
m=3n+1=7
T. Boykin, M. Luisier, G. Klimeck, et al., JAP2011

## Slide 26: Scattering Theory
Scattering theory is needed for quantitative approach
Ballistic simulation→ scattering theory
1 μm
Experiment | Simulation
1μm | Ballistic
Calculate mean free path λ and B from experiment by fitting
S. Kim, W.Hwang, et al. (unpublished)
LSQ fit
=0.3
Notes: =Iscatt/Iball

## Slide 27: Quantum Transport Simulation vs Experiment
VG
EfS
EfD
N++
P++
NA/ND=1.1x1013/cm2
EfS
EfD
RSD=300 Ωμm

## Slide 28: Quantum Transport Simulation vs Experiment
VG
EfS
EfD
N++
P++
NA/ND=2.2x1013/cm2
EfS
EfD
RSD=300 Ωμm

## Slide 29: Quantum Transport Simulation vs Experiment
VG
EfS
EfD
N++
P++
NA/ND=4.4x1013/cm2
EfS
EfD
RSD=300 Ωμm

## Slide 30: Quantum Transport Simulation vs Experiment
VG
EfS
EfD
N++
P++
`
NA/ND=5.5x1013/cm2
EfS
EfD
Experimental data is quantitatively captured.
RSD=300 Ωμm

## Slide 31: Graphene Nanoribbon Tunneling Transistor
p-i-n structure with varying doping concentrations
Varying width from source to drain
31
= 30 nm
EOT= 1nm
Vdd= 0.3 V
Electrostatic doping opens a door way to easy band-engineering
Notes: Electrostatic doping opens…

## Slide 32: Optimizing GNRTFETs
Band-engineering for low OFF-current and high ON-current
  2008, Q. Zhang, A. Seabaugh, et al., IEDL (WKB): SS<60 mV/dec
  2009, P. Zhao, J. Guo, et al., Nano Letters. (pz TB): assymetric doping effects - reduction of ambipolar characteristics
  2010, J. Chauhan, J. Guo, INEC. (pz TB): underlap - reduction of ambipolar characteristics
  2010, P. Michetti, et al., APL (pz TB): thermionic current/VDS effects
  2010, Y, Kathami et al., DRC (pz TB): heterostructure-varying width to increase ON-current
Almost all the study have been done with pz TB model. What if p/d TB?
What are the combined effects of doping/width on thermionic/tunneling current in heterostructure GNRTFET?
Can GNRTFET compete with silicon FET?
Theory

## Slide 33: GNRTFET Id-Vg (Ballistic)
33
There is trade off between ION and IOFF when the width is changed.
ITRS LP off-current
requirement
# of modes↓
norm. by width
EG↑
w↓
Notes: Add pz vs p/d IV comparison
p-i-n structure

## Slide 34: GNRTFET Id-Vg (Ballistic)
34
Flat
norm. by width
Sharp
Different shape of I-V curve due to different current mechanism.
Notes: Add pz vs p/d IV comparison
p-i-n structure

## Slide 35: Current Mechanism in GNRTFET with w>3.4 nm
log(DOS)
J(E)=T(E)×(fS(E)-fD(E))
EFS
EFD
Thermionic
Thermionic
Tunneling
35
OFF-state, VG=0 .1 V
2.2x1012cm-2
2.2x1012cm-2
4.8 nm
Itunneling dominates the Ioff for GNRTFETs with small width (w>3.4 nm).
Sharp: width>3.7 nm
Notes: Show the decision making steps

## Slide 36: GNRTFET Id-Vg (Ballistic)
36
Flat
norm. by width
Different shape of I-V curve due to different current mechanism.
Notes: Add pz vs p/d IV comparison
p-i-n structure

## Slide 37: Current Mechanism in GNRTFET with w<3.4 nm
log(DOS)
J(E)=T(E)×(fS(E)-fD(E))
EFS
EFD
Thermionic
Thermionic
Tunneling
37
OFF-state, VG=0 .1V
2.2x1012cm-2
2.2x1012cm-2
3.4 nm
Ithermal dominates the Ioff for GNRTFETs with small width (w<3.4 nm).
Flat: width<3.7 nm
Notes: Show the decision making steps

## Slide 38: Id-Vg Characteristics Comparison
GNR: Lg=30 nm, VDS=0.3 V
38
3.4 nm
2.2x1012cm-2
2.2x1012cm-2
60 mV/dec
ITRS LP off-current
norm. by width
IOFF slightly larger than ITRS requirement
Band-engineering
Minimize IOFF
Maximize ION
Notes: Put two lines for ITRS off/on current

## Slide 39: Reducing OFF current with Heteronegous/Assymmetric Structure
NS↑6.6x1012cm-2→n↓
ND↓1.1x1012cm-2→λ↑
EFS
EFD
39
Thermionic
Thermionic
Tunneling
3.4 nm
1.9 nm
Thermionic current can be reduced with changing size or doping.
  Width variation
  Asymmetric doping
log10DOS
P.Zhao,, NanoLett. (2009)
Lam et al., JJAP (2010)
J.Knoch,VLSITech. (2009)
width↓
Eg↑
p↓
J.Knoch,VLSITech. (2009)
J(E)=T(E)×(fS(E)-fD(E))
width↓
Eg↑
NS↑ → SS↑
λ
Bad for ON-current
Notes: Add J(E) for original homo junction

## Slide 40: Id-Vg Characteristics Comparison
Through band-engineering off-current can be reduced significantly.
40
GNRTFET
60 mV/dec
×~1/40
ITRS LP off-current
norm. by width
symmetric, homojunction
asymmetric, heterojunction
Notes: Put two lines for ITRS off/on current

## Slide 41: Id-Vg Characteristics Comparison
41
60 mV/dec
0.5 V
Lg=10 nm
D=3 nm
P=fCVdd2×1/4
Vdd×1/2
Vdd×1/4
P=fCVdd2×1/16
3.4 nm
1.9 nm
6.6x1012cm-2
1.1x1012cm-2
GNR: Lg=30 nm
ITRS LP off-current
0.25 V
norm. by width/dia
LP2012 (ITRS): 0.9 V
GNRTFET
SiNWFET
Significant reduction of power consumption with optimized GNRTFET
~400 μA/μm
Notes: different fonts for equation. new template, light color.

## Slide 42: Edge Roughness Effects on GNRTFET w=5.1 nm
Edge roughness is known to degrade the off-current of GNRTFETs
Tunneling current is dominant compared to thermionic current
M.Luisier, G. Klimeck, APL2009
DOS/band diagram
w=5.1 nm
Edge roughness limited mobility compared with experimental data → Edge roughness quantitative description?
How much edge roughness affect GNRTFETs with a small width (w<3.4 nm) and p/d TB model?
pz TB

## Slide 43: Edge Roughness Limited Mobility
The effects of edge roughness on mobility is calculated through the slope of R vs L
43
Generate random variable v
from 0 to 1 for each edge C atom.
Compare v with P (e.g. 0.05)
If v<P remove the atom, if not do not.
Edge roughness generation procedure
Edge roughness effects
S
D
Vd
Id
C
H
250 samples each

## Slide 44: Edge Roughness Limited Mobility
The effects of edge roughness on mobility is calculated through the slope of R vs L
44
Generate random variable v
from 0 to 1 for each edge H atom.
Compare v with P (e.g. 0.05)
If v<P remove the H atom, if not do not.
Edge roughness generation procedure
S
D
Vd
Id
Hydrogen passivation effects
C
H
250 samples each

## Slide 45: Width-dependent Mobility
45
Hydrogen roughness limited mobility is 2 order of magnitude larger than edge roughness limited mobility
Edge roughness P=3 % describes experimentally fabricated GNRs mobility.
Edge roughness
Hydrogen roughness
Exp. Wang, PRL2008
n~0.95x1013/cm2
(This work)

## Slide 46: Edge Roughness Effects in GNRTFET w=3.4 nm
OFF-current decrease/Vth shift: edge-roughness effects on Ithermal
ON-current decrease: edge-roughness scattering (B~63%)
P=3 %
46
3.4 nm
1.9 nm
NA=6.6x1012cm-2
ND=1.1x1012cm-2
30 samples
∆Vth=9mV
ION(rough)=270 μA/μm
ION(ball) =424 μA/μm
B=63 %
x1/4
=18.4 mV
Vth,shift

## Slide 47: Edge Roughness Effects on Current Spectrum
47
log10DOS
EFS
EFD
Edge roughness scattering reduces thermionic current.
Tunneling current increases at some resonant states, but overall decreases due to scattering.
Edge-roughness mainly reduces OFF-current for small width.

## Slide 48: Summary/Conclusion
Power problems can be overcome by TFETs.
GNRs satisfy requirements for good TFETs.
GNRTFETs can be next generation devices if the following obstacles are overcome
  Easily realizable doping/p-n junction
  OFF-state current is minimized
  Edge roughness is controlled.
This study has shown that
  Electrostatic doping is possible and p-n junction with NDR is demonstrated and quantitatively analyzed.
  OFF-state current can be minimized through engineering bandstructure with doping/width - importance of thermionic current.
  Edge-roughness with small probability (P=3%) degrades electron mobility significantly - good edge quality is required.
  Edge roughness can decrease off-current in GNRTFET, but can degrade the on-current at the same time.

## Slide 49: Acknowledgement
Post-Doc/Research Faculty team (Purdue)
  Prof. M. Povolotskyi, Prof. T. Kubis, Prof J. Fonseca
Collaboration/Discussion
  Prof. T. Boykin (U. of Alabama)
  Dr. Kwok (SRC), Prof. D. Antoniadis (MIT)
  Prof. A. Seabaugh, Prof. W. Hwang, Prof. D. Jena (ND)
  Prof. Gerhard Klimeck
  Prof. Mathieu Luisier
  Prof. Mark Lundstrom
  Prof. Supriyo Datta
Overall guidance and direction (committee members)
49

## Slide 50: Acknowledgement

## Slide 51
Thank you!

## Slide 52: Quantum Confinement in Si Inversion Layer
SC-CV matched QM-CV with increasing tox by 0.3 nm.
~0.9 nm*εSi/ ε SiO2~0.3 nm
Metal
Oxide
Silicon

## Slide 53: DD for bulk callibrated with MC
Bulk: Bude, SISPAD, 2000 Lg>40 nm
Monte Carlo Simulation (Bulk)
µ: mobility, E: longitudinal electric field, vsat: saturation velocity

## Slide 54: How to determin vsat?
β=1
Granzner, 2006
Assump.:Monte-Carlo simulation captures the ballistic transport correctly, the ballistic transport in SOI is similar to bulk

## Slide 55: Impacts of the ballistic mobility
Experimental data
  Unstrained: A. Cros et al., IEDM, 2006
  Strained: F. Andrieu et al., VLSI Tech. Dig., 2005
Low Vds

## Slide 56: Intel 32 nm (Id-Vg)
Benchmarked with experimental data at LG=32 nm and 20 nm
Experimental data: Natarajan et al., IEDM, 2008

## Slide 57: Nanowire Transistors
Promising SS/Mobility
Y. Cui, NanoLetters, 2003
Diameter: 5 nm
(Hole) Mobility: average 560 cm2/Vs
Projected SS~60 mV/dec @ Lg=50 nm
N.Singh, IEDL, 2006
Lg=180 nm

## Slide 58: Scaled Nanowire FETs
Very small nanowires with a short channel
Still not clear what will happen at a channel length 4.1 nm.
S. Suk, IEDM, 2007 (Samsung)
Diameter: down to 2 nm @Lg=30 nm
Ion~1100 µA/µm (normalized with circ.)
Mobility ~125 cm2/Vs
SS ~ 78 mV/dec
IBM,2010
IEEE spectrum
Diameter: down to 3 nm @Lg=234 nm
Mobility ~40 cm2/Vs
J. W. Sleights, IEDM, 2011

## Slide 59: MOSFET Electrostatics
Conduction-band edge profile
log Id
Vg
image:http://en.wikipedia.org/wiki/MOSFET

## Slide 60: Short Channel Effects
Conduction-band edge profile
log Id
Vg
image:http://en.wikipedia.org/wiki/MOSFET
DIBL increase
Vth shift
SS degradation

## Slide 61: Short Channel Effects
Conduction-band edge profile
log Id
Vg
image:http://en.wikipedia.org/wiki/MOSFET
DIBL increase
Vth shift
SS degradation
Reduce Tox-utilizing high-K
Halo doping
Tox

## Slide 62: Nanowire Transistors
Year | Author /Journal | Diameter (nm) | Lg (nm) | EOT (nm) | SS (mV/dec) | Mobility (cm2/Vs) | Ion (µA/µm)
2003 | Y.Cui,N.Lett. | 5 | 800 | 600 | >174 | 560 | 200
2006 | Singh,IEDL | 5 | 180 | 9 | 63 | 750 | 1500 (dia.)
2006 | K.Yeo,IEDM | 4 | 15 |  | 71 |  | ~1440 (dia.)
2007 | S.Suk,IEDM | >2 | 30 | 1 | 80 | 190 | ~1100 (cir.)
2011 | J.S.Sleights, IEDM | >3 | 234 |  |  | ~50 | 
Gate
Source
Drain

## Slide 63: Bandstructure Effects
Hydrogen Passivation
2nd subband
1st subband
Edge Roughness
AGNR-13
AGNR-12
2nd subband
1st subband
AGNR 13
AGNR 12

## Slide 64: Mobility vs Experiment
Edge roughness dominates the experimental mobility at even small probability!!
Hydrogen passivation less effective than edge roughness
Experiment: Wang, PRL2008
Hydro. Pass.
Edge roughness
n~ 0.95x1013/cm2

## Slide 65: Fundamental Limit of Conventional Transistor
Vg↑
log f(E), DOS(E)
Hot injection
Subthreshold Swing = 1/Subthreshold Slope
SS≥60 mV/dec
Vg
Vdd
log Id
0
Threshold
Hot injection limits the SS of conventional transistors.
p
Metal
n+
n+
Oxide
D
S
Vg
Id
x
E
Ef
`

## Slide 66: SiNW vs. DG
Ballistic Simulation Results
 | ION(µA/µm)
NW | 3068
DG | 1766
x1.7
NW
DG
DG Data: Mehdi Salmani

## Slide 67: SiNW/GNR FET (quasi-1D)
SiNWFET
GNR FET
Gate
Source
Drain

## Slide 68: Scaling Transistors
Lch can be scaled very aggressively with quasi-1D structure.
Vdd is not easy to scale. WHY?
ITRS2012
DD/QT Simulation Results

## Slide 69: CPU clock scaling blocked
Free lunch is over, Herb Sutter,
Dr. Dobb’s Journal, 2005
Size scaling!
Power problem becomes very serious.
→Frequency stopped increasing

## Slide 70: MOSFET vs TFET: Injection Mechanism
Problem with VDD Scaling:
Subthreshold Swing (SS) limited to 60 mV/dec
Large ION/IOFF ratio => large VDD
High Power Consumption
VDD scaling not possible:
  either increase of IOFF
  or decreases of ION
Solution: BTB Tunneling
No lower limit on the SS
Low Power Consumption
Various designs and materials
Less heat generation
Biggest Challenges:
High ION
Steep SS
Low IOFF
Hot Injection
Cold Injection
OFF
ON
VDD
VDD
ON
ON
OFF
From Gerhard Klimeck’s Physics Seminar 2010
Mathieu Lusier, OMEN
Inherent in TFET, but caused by external factors:IR,IT
Material Characteristics
9
Heat Problem
Heat Problem
Reduced

## Slide 71: Eniac vs. Intel Core Duo
106
103
105
104

## Slide 72: Derivation of effective mobility

## Slide 73: Quantitative Analysis: Simulation
chipworks
Simulate intrinsic device characteristics assuming series resistance reduces on-current by ~1/3
2D electrostatics: must
Quantum Transport for SOI/DG
:Ballistic+Scattering
Drift diffusion with quantum corrections
confinement (calibrated with 1D Schroe.-Poisson)
ballistic mobility (good match with exp.)
qausi-ballistic transport (calibrated with M.C.)
Calibrated with exp. (Samsung 20 nm/Intel 32 nm)
IEEE TED, 2013 submitted

## Slide 74: Fundamental Problem with Bulk MOSFET
2D electrostatic captured: intrinsic performance degradation of Bulk in shorter channel
Anlaytical model with arbitrary(?) parameters
Realistic simulation: 2D electrostatics
Decreasing!
Increasing??
ITRS 2012 (MASTAR) | QCDD (new ITRS)
No geometry input | 2D electrostatics
SS as a input | SS as an output
No SCE | SCE captured
Ion as a target | Ion as an output

## Slide 75: Fundamental Problem with Bulk MOSFET
2D electrostatic captured: intrinsic performance degradation of Bulk in shorter channel
Lg (nm) | Literature | Year
32 | S. Natarajan (Intel) | 2009
30 | H.Ohta (Fujitsu) | 2005
30 | E. Morifuji (Toshiba) | 2002
27 | Uejima (NEC) | 2007
20 | Cho (Samsung) | 2011
15 | B. Doyle (Intel) | 2002
15 | Bin Yu (AMD) | 2001
14 | A. Hokazono (Toshiba) | 2002
10 | B. Doyle (intel) | 2007
5 | H. Wakabayashi (NEC) | 2003
Decreasing!
Increasing??

## Slide 76: SOI/FinFET (quasi-2D)
=1/4×LG
=1/2×LG
SOIFET
FinFET
SOI/DG FinFET better electrostatics → reduced short channel effects
Quantum Transport

## Slide 77: How to calculate mobility or mean free path
µ0 is long channel mobility:
1. Experiment
2. Calculations
a) Benchmark with experiment like what we did for IBM 22nm SOI (lack of experiments)
b) Atomistic modeling (very expensive) c) Simple available mobility models for bulk (it wont work well for ultra scaled devices)

## Slide 78: Difficult Supply Voltage Scaling
Subthreshold Swing = 1/Subthreshold Slope
SS≥60 mV/dec
Vg
Vdd
log Id
0
Supply voltage scaling is hampered by unscalable SS
Short channel effects make it even worse.
ITRS2012
2012
2026 (Old ITRS)
2026 simulation
Stop scaling Vdd/LG
or at least slow down scaling

## Slide 79: Tunneling Current/Thermionic Current
OFF | NS↑ | ND↑ | S/D Width↑
Ith | ↓ | ↓ | ↑
Itunneling | N/A | ↓ | ↑
SS | ↑ | N/A | ↑
ON | NS↑ | ND↑ | Width↑
Itunneling | ↑ | N/A | ↓

## Slide 80: Fabrication of GNRs (ND)
Wafer scale multiple GNRs
Picture: Wansik Hwang

## Slide 81: Id-Vg Characteristics
EOT=90 nm
Back-gate
Poor SS

## Slide 82: Electrostatic dopiong
SG2=2 V
W. Hwang (unpublished)
D. Efetov, P. Kim, 2010, PRL

## Slide 83: Ballistic Simulation Result
Ballistic simulation

## Slide 84: Graphene Nanoribbon for Tunneling Transistors
Graphene nanoribbon:
  Low bandgap/effective mass compared to other material
  Small screening length (1D)
3n+1 group
84
Material

## Slide 85: Closer Look at ID-VD
VG
EfS
EfD
P+++
N+
VG
EfS
EfD
N++
P++
EfS
EfD
N++++
P

## Slide 86: Bandstructure Effects
Hydrogen Passivation
2nd subband
1st subband
Edge Roughness
AGNR-13
AGNR-12
2nd subband
1st subband
AGNR 13
AGNR 12

## Slide 87: Edge roughness effects on p/d vs pz model
p/d vs pz: current increases when w=4.7 nm.
p/d
pz
w=4.7 nm
w=4.7 nm
P=3 %
P=3 %