## Slide 1
Outfall Reconnaissance Monitoring The why and how of testing direct sources into watersheds…
Chris Jones, Richard Dewitt, & Leslie Schick

## Slide 2: Our common cause…
A Storm Water Pollution Prevention Plan (SWPPP) or Municipal Separate Storm Sewer System (MS4) require an Illicit Discharge Detection Elimination (IDDE) Program.

## Slide 3: What is an Illicit Discharge?
A discharge to an MS4 that is not composed entirely of stormwater except permitted discharges and fire fighting related discharges 40 CFR 122.26(b)(2)
  Unique frequency, composition & mode of entry
  Interaction of the sewage disposal system & the storm drain system
  Produced from “generating sites”

## Slide 5: Dry Weather vs Wet Weather
  Dry Weather could potentially contribute more pollutants than wet weather as sources could be:
    Sewage/septage
    washwater (aka gray water)
    Paints
    automotive waste
    Oils (including animal)
    landscaping irrigation

## Slide 6
Storm drain systems empty directly into natural waterways (streams, rivers, and wetlands), and do not go to a water treatment plant.
So, any pollution that makes its way into storm drains can damage the environment and pose risks to human health.
Rain water can easily carry pollution from parking lots, streets, and lawns, such as litter, oil, or fertilizer into storm drains and from there into waterways that we use for drinking water, fishing, swimming and so on.

## Slide 7: www.accesskent.com Could still have Illicit Discharges…
Goal 2 - eliminate /correct
Goal 1 - Identify Sources

## Slide 9
Chris Jones on the “planning” stage of monitoring…

## Slide 10
The Survey Phase:
Table Top Reconnaissance
Field Survey
Mapping

## Slide 11
Communities with Minimal, Clustered, and Severe Illicit Discharge Problems
Table Top
Basic Orientation
Indentifying Key Areas

## Slide 12
Identifying clusters help to identify pollution potential
Commercial -Industrial
Residential - Subdivisions

## Slide 13: Field Survey
Boots on the ground reconnoiter.
Items needed, boots, water, map and pencil.
Walk the banks, paddle a kayak, make a note on the map for each outfall (pipe) sticking out of the bank or flowing into the waterway.

## Slide 14: Mapping
Basic, take the information gained from the table top, and field surveys and pin it on a map.
Utilize Geographic Information Systems or basic Google maps and pins.

## Slide 17
The Testing Phase:
Establish monitoring standards.
Monitoring potential (non-point source) pollution.
Correlation to stream quality.

## Slide 18
Outfall with channel to stream.
Notice of any concern?
Outfall ID - ST12500

## Slide 20
Why a concern for monitoring?
Outfall

## Slide 21
Run-off from?
Remediation Site
Industrial Complex
Agri-Business
Commercial
&
Construction
Residential
Industrial
Outfall

## Slide 22
Outfall Inspection
Outfall Condition – Cracks, Stains, Odors , Is it dry or flowing.
Abnormal Vegetation or Poor Pool Quality.
Outfall Testing – (with flow).
Testing Parameters
Temperature
pH
E. Coli
Chlorine
Ammonia
Nitrate/Nitrite
Hardness
Turbidity
Detergents
  Phosphorus
Testing standards are based upon current Indiana Water Quality Standards.
Test kits are the standard along with visual observation of color & smell.
WWTP – Provides advanced E.Coli testing in their lab for the MS4.

## Slide 23
Outfall Inspection
Outfall Condition – Cracks, Stains, Odors , Is it dry or flowing.
Abnormal Vegetation or Poor Pool Quality.
Outfall Testing – (with flow).
Testing Parameters
Temperature
pH
E. Coli
Chlorine
Ammonia
Nitrate/Nitrite
Hardness
Turbidity
Detergents
Phosphorus
Testing standards are based upon current Indiana Water Quality Standards.
Test kits are the standard along with visual observation of color & smell.
WWTP – Provides advanced E.Coli testing in their lab for the MS4.

## Slide 24
Outfall Inspection
Outfall Condition – Cracks, Stains, Odors , Is it dry or flowing.
Abnormal Vegetation or Poor Pool Quality.
Outfall Testing – (with flow).
Testing Parameters
Temperature
pH
E. Coli
Chlorine
Ammonia
Nitrate/Nitrite
Hardness
Turbidity
Detergents
  Phosphorus
Testing standards are based upon current Indiana Water Quality Standards.
Test kits are the standard along with visual observation of color & smell.
WWTP – Provides advanced E.Coli testing in their lab for the MS4.
Indiana Water Quality Standards
Temperature Summer Maximum limit 32.2C (89.6F)
pH Range of 6 – 9 pH units
Conductivity Range between 150- 500 s/cm
Ammonia Range around 0.5 ppm
Chlorine Range around 0.4 ppm
Phosphorus Range less than 0.03 ppm
E. Coli Range less than 235 CFU/100ml
Nitrate/Nitrite Range less than 0.03 ppm
(If ammonia level exceeded.)
Turbidity Not to exceed 40 NTU
Hardness No range – regional geology
Detergents Range 0 – 1 ppm
Dissolved Oxygen Less than 4.0/ml

## Slide 26
Investigating a Source – Investigate up the trunk of the outfall and sample stream.
Remediation Site
Industrial Complex
Agri-Business
Commercial
&
Construction
Residential
Industrial
Outfall
Point Sources
Industrial/Commercial
Sewage
Wash Water
Waterline Breaks
IDDE/Dumping
Construction
Post-Construction

## Slide 27
Investigating a Source – Investigate up the trunk of the outfall and sample stream.
Remediation Site
Industrial Complex
Agri-Business
Commercial
&
Construction
Residential
Industrial
Outfall
Point Sources
Industrial/Commercial
Sewage
Wash Water
Waterline Breaks
IDDE/Dumping
Construction
Post-Construction
Resolution:
Eliminate pollution source.
Immediate Clean-up or Remediation of source.

## Slide 28
On-going Monitoring:
Annual outfall monitoring of all water body outfalls.
Awareness of pollution potential hot spots – (Rule 6 Facilities).
Maintain a public education Illicit Discharge Detection Elimination program.
Goal – to maintain a healthy watershed.