## Slide 1: Water Quality Predictors for Key Indiana Reservoirs
Indiana Watershed Leadership Academy
Final Project Presentation
Garrison Inn
Ft. Harrison State Park
Indianapolis, IN
20 May 2015
By
Morgan Bennett
Carol Newhouse
Kelsey Owens

## Slide 2: Motivation for this Project
Climate changes are affecting water supplies across the nation and globally
Growth and well-being of society is dependent on readily available water supply
Current efforts and/or future needs to build water supply reservoir(s) in Indiana
Wondering if history had anything to teach us

## Slide 3: Discovery Steps
List of Impoundments/Reservoirs in Indiana
Mapping of Impoundments and their Watersheds
Data Gathering from On- and Off-line Sources

## Slide 4: First Step
List of Impoundments/Reservoirs in Indiana
  Over 600 lakes/reservoirs in state
  Easily 150+ impoundments
    21 major river impoundments
    16 large water supply impoundments
    35 local/state/federally owned
    11 other working impoundments
    75+ privately owned impoundments
  Narrowed list to most similar waterbodies

## Slide 5: Basic Literature Search (online)
Removed host of small water supply reservoirs and recreational impoundments
Removed few cooling water reservoirs
Ended up with 18 key reservoirs to consider

## Slide 6: Key Reservoirs
Shafer
Freeman
Kokomo #2
Morse
Eagle Creek
Geist
Cecil M. Harden
Cagles Mill
Patoka

## Slide 7: Key Reservoirs
Cedarville
J. Edward Roush
Mississinewa
Salamonie
Prairie Creek
Brookville
Lemon
Monroe
Mounds

## Slide 8: Second Step
Mapping of impoundments and their watersheds
  Online tools
    Google Maps
    Indiana Maps
  Defining data layers
  Scale

## Slide 9: Prairie Creek
Some with rather small watersheds (Group 1)
Size relation = 11.3%
1 acre of water drains <9 acres of land
Best example
1:6400

## Slide 10: Geist Reservoir
1:250,000
Most have moderately sized watersheds (Group 2)

## Slide 11: Geist Reservoir
1:250,000
Size relationship 1.0-2.0% (Geist = 1.3%)

## Slide 12: Geist Reservoir
1:250,000
1 acre of water drains 75-100 acres of land

## Slide 13: Kokomo #2
1:250,000

## Slide 14: Kokomo #2
Few have rather large to ‘humongous’ watersheds draining into them (Group 3)
Size relationship = 0.5% or less
  0.42% Kokomo
1 acre of water drains 238 acres of land (Kokomo)
  Cedarville – 1 acre of water drains 2,000 acres
  Shafer & Freeman – 1 acre drains 10,000 acres
These are the hardest working bodies of water in Indiana

## Slide 15: “Hard working”?
How well do they fulfill the purpose(s) for which they were built?
  Parameters might be ‘okay’ for hydroelectric use
  Or problematic for water storage use (storm or drinking), due to decreased storage volumes
  Or challenging for those with drinking water intakes

## Slide 16: Map View
Group 1 (ratio >3.0%)
Group 2 (ratio 1.0-2.0%)
Group 3 (ratio < 0.5%)

## Slide 17
Prairie Creek
Row crops (brown) and pasture/hay (yellow)
Forested near lake (green)
Small amount development along county roads

## Slide 18
Highly developed shore vs. ag shore
Uniformly mixed woods and pastures with a scattering of row crops

## Slide 19
Proposed Mounds Reservoir in Madison County
Size =
2,100 acres
Drains
259,840 acres

## Slide 20
Proposed Mounds Reservoir in Madison County
Lots of agricultural land
Plus urban / commercial / industrial use areas

## Slide 21: Proposed Mounds Reservoir
  Encompasses seventeen 12-digit HUCs (PC had 1)
Notes: Important to consider land uses in all of those upstream Hydrologic Unit Code areas.
Also, important to consider that control of those areas is in the hands of other political jurisdictions and their land use, zoning and drainage policies and practices.

## Slide 22: Third Step
Data gathering from off- and online sources
  IU/SPEA website (1988-2014)
  2014 List of Waterbody Impairments
  Historic files from IDEM
    Lake sediment and fish tissue sampling
    National Eutrophication Survey (EPA)
    Pertinent correspondence
    USGS and other reports
    Volunteer data

## Slide 23: Trophic Information and Designated Use Support
Water Quality Indicators for Lake Lemon |  |  | 
Indicator | Value | Data Source | Last Updated
Area (Acres) | 1650 | * | 2008
Trophic Status | Eutrophic | * | 2008
Trophic Trend | Fluctuating | * | 2008
Support for Designated Uses |  |  | 
Recreational Use | Not Assessed | ** | 2008
Fishable Use | Impaired: 5B | ** | 2008
Aquatic Life Use | Not Assessed | ** | 2008
Total Number of Impairments | 1 | ** | 2008
Cause of Impairment(s), If Any | Mercury in Fish Tissue | *** | 2008

## Slide 24: Data Crunching
  Comparing individual water quality parameters (collected to calculate Indiana Trophic State Index scores)
PO4
Secchi
Plankton
DO
Nitrogen

## Slide 25: At First, Data Gaps
  Epilimnion and hypolimnion data unwieldy
  Water column averages easier and in keeping with other state lake assessments
  Historical data consulted for outliers and representativeness

## Slide 26: Still, CHAOS…

## Slide 27: Waterbody to Watershed Ratio
  Area : Area
  Volume : Area
Adapted from Hoosier Riverwatch image

## Slide 28: Reservoir Area : Watershed Area
  Resulted in multiple groups

## Slide 29: Res. Volume : W’shed Area
  Fell nicely into three (3) groups (#2 >> Mounds group)

## Slide 30
  Cursory graphing to see which data appeared to be closely related…
Pulling it All Together

## Slide 31
  …or not so closely related
Pulling it All Together

## Slide 32
  Compared average values by parameter
Pulling it All Together
Chart: Trophic Score Index
| Eagle Creek | Morse | Salamonie | Brookville | Cecil M. Harden | Geist | Mississinewa | Cagles Mill
 | 65 | 64 | 44 | 43 | 36 | 32 | 26 | 23

## Slide 33
  Brookville appears as outlier here, due to lake not being stratified. Apparently lower gate was open causing mixed water column throughout.
Chart: Secchi Disk
| Brookville | Mississinewa | Eagle Creek | Cagles Mill | Salamonie | Cecil M. Harden | Geist | Morse
 | 2.1 | 0.9 | 0.8 | 0.8 | 0.8 | 0.7 | 0.6 | 0.6

## Slide 34
Chart: % Water Column with DO of 0.1 or greater
| Brookville | Geist | Salamonie | Cagles Mill | Mississinewa | Morse | Cecil M. Harden | Eagle Creek
 | 83.3 | 81.96 | 39.59 | 36.4 | 36 | 33.6 | 24 | 22

## Slide 35
Chart: % Sat. of DO at 5’ Depth
| Geist | Salamonie | Cecil M. Harden | Eagle Creek | Morse | Cagles Mill | Mississinewa | Brookville
 | 147.4 | 140 | 133 | 128.5 | 120.5 | 92.2 | 73 | 51.4

## Slide 36
Chart: Blue-Green Algae Dominance (Taste and Odor)
| Morse | Eagle Creek | Cecil M. Harden | Salamonie | Geist | Brookville | Cagles Mill | Mississinewa
 | 99.7 | 97.9 | 86.3 | 81.8 | 80.9 | 68.8 | 38 | 2.6

## Slide 37
Chart: Plankton Count
| Morse | Eagle Creek | Brookville | Salamonie | Geist | Mississinewa | Cecil M. Harden | Cagles Mill
 | 127177226 | 18338731 | 2045878 | 45176 | 22957 | 1916 | 1574 | 1430

## Slide 38
  Determined which parameters showed significant difference between three groups
Pulling it All Together
Chart: Secchi Disk Reading
| Group 1 | Group 2 | Group 3
 | 1.375 | 0.9125 | 0.69

## Slide 39
  Determined which ones correlated to water quality
Pulling it All Together
Chart: Total Phosphorus
| Group 1 | Group 2 | Group3
 | 0.090125 | 0.11181 | 0.1907

## Slide 40
Chart: Nitrate + Nitrite as N
| Group 1 | Group 2 | Group 3
 | 0.43938 | 1.6017 | 1.7941
Chart: Organic Nitrogen
| Group 1 | Group 2 | Group 3
 | 1.1141 | 1.2175 | 1.5174
Notes: Group 2 is where Mounds Reservoir will fall, if built as proposed.

## Slide 41
Chart: Chlorophyll a
| Group 1 | Group 2 | Group3
 | 6.6475 | 24.07 | 26.664
Notes: Keep in mind that Group 2…(next slide)

## Slide 42
Chart: Chlorophyll a
| Group 1 | Group 2 | Group3
 | 6.6475 | 24.07 | 26.664
Notes: (cont’d) … is where Mounds Reservoir will fall, based on watershed to lake ratio.

## Slide 43: Lessons Learned
Working with water data as a whole
There is a lot of data available, but it is scattered and not all is available online
Improvements in lake trophic scores following Indiana’s ban on phosphates have maintained themselves
Drawing water from different lake depths effects DO and stratification
Watershed size : waterbody volume ratio’s effect on water quality was supported by Indiana’s reservoir data despite the significant differences in land use and topography across Indiana’s reservoirs

## Slide 44: More Lessons Learned
Importance of erosion control
Need for nutrient
Sewers are better than septic tanks
Use of various forms of technology (hard and soft)
Murphy says “the greater your need for particular software package is, the more likely it will be taken offline for maintenance or upgrades”
Working as a team!!!

## Slide 45: What’s Next?
Comparing additional impoundments which have similar size ratios to see if they respond the same
More complete assessment of land use types and impervious surfaces (running various models)
Running better statistics on groups and parameters to verify significant differences
Further data analysis to determine anomalies vs. general variability
Create online guidance document for public use

## Slide 46: Thank You!