## Slide 1
Front of Card
Back of Card
(name with color banner for parameter type Chemical (yellow), Biological (green) or physical (blue)
Definition:
Water Quality Impacts:
Sources:
Common examples
Source Examples:
Typical targets for Indiana waters or “ideal /detrimental” assessment of waterbody
Targets:
Indiana or US EPA requirements or guidance limits or “N/A” for not applicable
Limits:
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
NP
(name with color banner for parameter type Chemical (yellow), Biological (green) or physical (blue)
This is the “example / explanation” card
Cut lines
Non-point source symbol
point source symbol
(A list of common sources or causes)
(A brief description of its affects on water quality)

## Slide 2
Front of Card
Back of Card
WATER QUALITY QUICK-CARDS
These cards provide a basic understanding of the main parameters that scientists collect to gain an understanding of the health of a water body and its biota. Some of the parameters require laboratory analysis while others can be directly measured in the waterbody.
For all of these parameters, it is important to collect numerous measurements and track the results over time. Multiple readings on any waterbody using the same locations and methods will better allow for the identification of adverse impacts or changes in the water body.
WATER QUALITY QUICK-CARDS
Overview
Overview Continued
Blank
Blank
Each of the cards have been designed in a standard layout in order to provide identicle key details for each of the water quality parameters. The color banner across the top of each card is used to indicate if the parameter is a biological (green), chemical (yellow) or physical (blue) reading.
For additional information please reference the document: https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf

## Slide 3
Front of Card
Back of Card
Glossary of Terms:
Biome – a community of organisms that together create the “biology” in and near the water
Biota – The characteristic set of organisms within a region or waterbody
Blooms – A distinct rapid growth in plant or bacteria (e.g. algae)
DNR – Indiana Department of Natural Resources
Eutrophication – an increase in nitrogen and phosphorus develops an imbalance in the water thereby creating large blooms and creating an environment that limits or alters the biome
IDEM – Indiana Department of Environmental Management
IN - Indiana
MCL – Maximum Contaminant Level
NP – (Non-point source) A source of material that results in environmental impacts or contamination of a waterbody and enters the water over a large diffuse area as opposed to a Point Source (PS)
(continued on back)
Glossary of Terms (continued):
OEPA – Ohio Environmental Protection Agency
Photosynthetic – The ability of an organism to utilize sunlight as a source of energy
ppb – parts per billion (1 in 1,000,000,000)
ppm – parts per million (1 in 1,000,000)
PS – (Point Source) A source of material that results in an environmental impact and can be attributed to a know location(s) as apposed to a Non-Point Source.
Secchi Disk – An engineered viewing disk that measures the depth of light traveling through the water and used to measure the clarity of the water
US EPA – United States Environmental Protection Agency
WQS – Water Quality Standard
WWTP – Waste Water Treatment Plant
Blank
Blank

## Slide 4
Front of Card
Back of Card
Chemical Parameters
Chemical parameters are collected to understand some of the key compounds that may indicate contamination or changing conditions of the water body. There are numerous chemical measurements that can be measured, however the following six parameters are the most common measurements that indicate water quality conditions.
As with all other parameters it is important to collect numerous measurements and track the results over time.
Total Phosphorus
The total concentration of the most common phosphorus containing molecules in our environment. This includes: organic phosphorus, orthophosphate, and polyphosphates (least common). Phosphorus is usually a limiting nutrient in natural aquatic biome.
Any elevated concentrations nutrients, such as phosphorus, can dramatically increase microbial and algal growth, stress fish and aquatic insect communities and fluctuate dissolved oxygen (DO) levels.
Definition:
Water Quality Impacts:
Sources:
grass clippings, leaves, lawn fertilizers, WWTPs, agricultural runoff, field tiles, industry, manure application on agricultural fields and its runoff
Source Examples:
<0.3 mg/L (IDEM Target)
Targets:
Limits:
<0.08 mg/L OEPA criteria to protect aquatic communities
Levels >0.03 mg/L can produce nuisance algae blooms in lakes
NP
Total Phosphorus
Elevated levels often occur during high flow conditions due to storm water runoff. Many WWTPs do not treat for phosphorus and therefore can elevate levels during low flow conditions.
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
Chemical Parameters
There is a Quick Card for each of the following chemical parameters:
Total Phosphorus,
Ammonia,
Biochemical Oxygen Demand,
Nitrate + Nitrite,
Total Nitrogen, and
Total Kjeldahl Nitrogen

## Slide 5
Front of Card
Back of Card
Ammonia
A colorless gas that is very soluble in water. It is one of the most common forms of nitrogen due to human activity related to biological-based waste in streams. Ammonia (NH₃) is a toxic form of nitrogen with a strong pungent odor, formed when organic matter breaks down in water. Ammonia levels are dependent on pH and Temp (>pH and temp = more toxic ammonia).
Fish communities are extremely sensitive to ammonia. Fish can begin to die when ammonia reaches 0.2 mg/L.
Definition:
Water Quality Impacts:
Sources:
grass clippings, leaves, agricultural nutrient application, WWTPs
Source Examples:
WQS dependent on pH and temperature but in general: max 0.0075 mg/L - 0.0294 mg/L; average 0.0005 mg/L - 0.0294 mg/L
Targets:
> 0.06 mg/L can impact fish; > 2.0 mg/L can kill tolerant fish
Limits:
NP
Ammonia
Biochemical Oxygen Demand (BOD)
Biochemical oxygen demand (BOD) is the measure of oxygen used by aerobic (oxygen-consuming biota like fish and bacteria) as they break down organic wastes over a specific time period. The more biota the more demand it will have on the oxygen levels in the water.
The greater the BOD the more oxygen is demanded by the biota. If there are a lot of plants using the oxygen it can reduce the amount of oxygen available to native biome such as fish and stress and kill them
Definition:
Water Quality Impacts:
Sources:
grass clippings, leaves, large algal or plant blooms, stagnant water conditions
Source Examples:
1 - 2 mg/L (clean water); 3 - 5 mg/L (fairly clean); 6 - 9 mg/L (excess organic matter); 10+ mg/L (very poor water quality)
Targets:
there is no limit, this is based on site-specific aquatic ecology
Limits:
NP
Biochemical Oxygen Demand (BOD)
Natural break-down of plant material in the water (this can be dramatically increased due to human activity such as grass or lawn material dumping in or near a water body).
There is an unnatural demand on the available oxygen for other biota (such as fish) when there are large blooms of plant materials, such as algae. The plants outcompete other biota by using all the available oxygen.
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf

## Slide 6
Levels > 1 mg/L indicate human influence
>0.005 mg/L causes eutrophic or highly productive conditions in lake systems;
Median concentration of 0.02 mg/L in IN lakes (2010)
Front of Card
Back of Card
Nitrate + Nitrite
Nitrogen is the most abundant element in the Earth's atmosphere. The nitrogen cycle is one of the major chemical sequence to produce biological activity. Nitrate and Nitrite are the two basic molecules of inorganic nitrogen and therefore often measured together. Nitrate is much more stable and common in the earth’s waters than Nitrite.
Nitrates can be toxic at high concentrations and even limit oxygen in low concentrations. Elevated levels can cause eutrophication of lakes and areas of low dissolved oxygen in salt water (i.e. Gulf Of Mexico Hypoxia).
Definition:
Water Quality Impacts:
Sources:
Animal farms, agricultural runoff, fertilizers, industry, WWTPs
Source Examples:
< 10 mg/L (IDEM Drinking Water Standard)
<1 mg/L (OEPA criteria for warm water habitat)
Targets:
Limits:
NP
Nitrate + Nitrite
NA
Orthophosphate
Orthophosphate is an inorganic form of phosphorus, a nutrient required for the basic processes of life but, when it is highly concentrated can cause eutrophication.
The amount of orthophosphate constitutes an index of the amount of phosphorus available for algal growth. Excessive algal growth can cause low DO, algal blooms, taste and odor problems and lower recreational value.
Definition:
Water Quality Impacts:
Sources:
grass clippings, leaves, lawn fertilizers, WWTPs, agricultural runoff, field tile runoff, industry, manure application on agricultural fields
Source Examples:
Targets:
Limits:
NP
Orthophosphate
Elevated levels often occur in the Spring as a result of tile drains in agricultural land use. Many WWTPs do not treat for nitrogen and therefore can elevate levels during low flow conditions.
Elevated levels often occur during high flow conditions due to storm water runoff. Other forms of phosphorus can be converted to orthophosphate and other acids.
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf

## Slide 7
Front of Card
Back of Card
Total Nitrogen
The total concentration of the most common nitrogen containing molecules in our environment. This includes: total kjeldahl nitrogen, ammonia nitrogen, nitrate, and nitrite.
Elevated nutrient levels can impact algal growth, fish and aquatic insect communities and DO levels. Elevated levels lead to excess plant growth and decay, low DO and reductions in water quality.
Definition:
Water Quality Impacts:
Sources:
grass clippings, leaves, lawn fertilizers, WWTPs, agricultural runoff, field tiles, industry, manure application on agricultural fields
Source Examples:
< 10 mg/L (IDEM Target)
Targets:
Limits:
NP
Total Nitrogen
US EPA Proposed Criteria:
Central Corn Belt Plains – <0.66 mg/L; Eastern Corn Belt Plains - <0.4 mg/L; S Michigan/N IN Drift Plains - <0.58 mg/L; Huron/Erie Lake Plain - <0.65 mg/L; Interior Plateau - <0.28 mg/L; Interior River Lowland - <0.54 mg/L
Total Kjeldahl Nitrogen (TKN)
This is a summation of the two most common forms of nitrogen (ammonia + organic nitrogen) and are related to the discharge of biologically active waters.
Elevated nutrient levels can impact algal growth, fish and aquatic insect communities and DO levels. High levels result from sewage and manure discharges to waters.
Definition:
Water Quality Impacts:
Sources:
grass clippings, leaves, lawn fertilizers, WWTPs, agricultural runoff, field tiles, industry, manure application on agricultural fields
Source Examples:
Targets:
NP
Total Kjeldahl Nitrogen (TKN)
Elevated levels often occur in the Spring as a result of tile drains in agricultural land use. Many WWTPs do not treat for nitrogen and therefore can contribute to elevate levels during low flow conditions.
Too much creates eutrophication of streams and lakes and decreases the resources values, for recreation, fishing, hunting and aesthetic enjoyment.
Decaying organic material (plants, animal waste, urban and industrial disposal of sewage.
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf

## Slide 8
Front of Card
Back of Card
Chlorophyll a
Chlorophyll a is one of the most important pigments used for photosynthesis. It is what causes the green coloring of algae and plants. Chlorophyll a is the most common pigment in algae so sampling for it allows for an indirect estimate of the amount of algal biomass in surface waters.
Chlorophyll a sampling can indicate the amount of algae in the water. The right amount of algae is needed to maintain a balanced food web .
Definition:
Water Quality Impacts:
Sources:
grass clippings, leaves, agricultural nutrient application
Source Examples:
US EPA proposed criteria by ecoregion:
Central Corn Belt Plain - 2 ug/L
Eastern Corn Belt Plain - inconclusive
S Michigan/IN Drift Plains - 3.5 ug/L
Huron/Erie Lake Plain - 3.2 ug/L
Interior Plateau - 3.9 ug/L
Interior River Lowland - 1.5 ug/L
Targets:
Chlorophyll a
Chlorophyll a can be used as a direct indicator of an overactive plant growth in the environment. Overproduction of plant growth (e.g. algae) can stress the rest of the biome.
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
NP
Biological Parameters
Biological information is collected to understand key characteristics about the overall condition of the waterbody based on the biota. Some parameters may lead to public health advisories while others indicate potential water quality problems. There are numerous chemical measurements that can be measured, however the following 4 parameters are common measurements that indicate water quality conditions.
As with all other parameters it is important to collect numerous measurements and track the results over time.
Biological Parameters
There is a Quick Card for each of the following biological parameters:
Chlorophyll a
E. coli
Fish and Macroinvertebrate Index of Biotic Integrity (IBI)
Blue – Green Algae

## Slide 9
NA
Front of Card
Back of Card
< 125 CFU/100 mL geometric mean (5 samples collected 5 consecutive weeks) or < 235 CFU/100 mL from a single sampling event
E. coli is a bacteria found in the fecal waste of warm-blooded mammals (i.e. humans, cattle, wildlife). E. coli measurements are used only as an indicator of contamination by fecal waste materials.
E. coli indicates there is likely fecal waste in streams and additional toxic microbes could also be present. These microbes can lead to illness or infections (i.e. nausea, diarrhea, dysentery, hepatitis) after swimming in polluted water.
Definition:
Water Quality Impacts:
Sources:
WWTPs, combined sewers, failed septic systems, dog poop, animal operations, manure application on agricultural land
Source Examples:
Targets:
Limits:
NP
Fish and Macroinvertebrate Index of Biotic Integrity (IBI)
An index of Biotic Integrity (IBI) is a statistically based scientific tool used to identify and classify water pollution problems through the inventory of plainly visible fish and bugs in the water body. High scores indicate a good healthy biom and waterbody.
The IBI is a standardized way to compare sites along a stream across geographic areas. Comparing scores over time can show water quality improvement or degradation.
Definition:
Water Quality Impacts:
Sources:
NA (This is a standardized classification of a the health of a waterbody)
Source Examples:
Excellent 53-60; Good 45-52; Fair 35-44; Poor 23-34; Very Poor < 22
Targets:
The scores range from 0-60 and a score < 36 is impaired
Limits:
An IBI is calculated using 12 metrics, including # of individuals, species diversity, # of deformities, and other trophic and community characteristics. Scoring and metrics vary depending on the ecoregion and the drainage area.
Escherichia coli (E. coli)
Escherichia coli (E. coli)
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
E. Coli is a direct result of contamination with warm-blooded fecal matter. Typically direct contamination or runoff or drainage from poorly managed waste streams flowing into the water.
Fish and Macroinvertebrate Index of Biotic Integrity (IBI)

## Slide 10
Front of Card
Back of Card
Blue Green Algae
A group of photosynthetic bacteria found in a wide range of water bodies. Periods of significant growth occur during the warm season (between May and October in Indiana).
This algae can produce toxins which can cause skin irritation, sickness and death to livestock and dogs. The algae can create taste and odor problems and fish kills as the decaying algae consumes oxygen.
Definition:
Water Quality Impacts:
Sources:
grass clippings, leaves, lawn fertilizers, sediment runoff, failing septic systems, agricultural nutrient application, WWTPs
Source Examples:
Health Advisory if algal cell counts > 100,000 cells/mL, microcystin toxin level > 6 ppb, cylindrospermopsin toxin > 5ppb or anatoxin-a toxin > 80 ppb
Targets:
Swimming beaches will close if microcystin toxin reaches 20 ppb
Limits:
NP
Warm temperatures combined with elevated levels of nutrients in the water.
Blue Green Algae
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
Blank
Blank
Blank

## Slide 11
Score ranges from 0 - 75
Front of Card
Back of Card
0 - 15 is Oligotrophic (highest quality); 16 - 31 is Mesotrophic (intermediate); 32 – 46 Eutrophic (low quality); > 47 Hypereutrophic (lowest quality)
A standardized multi-metric index using physical, chemical and biological data from a lake. The index is used to classify lakes based on eutrophication using nutrient levels, DO levels, water clarity, and plankton cell counts.
Eutrophication of lakes impact the fish by creating low DO zones, create problems for drinking water facilities, cause odor problems and decreases recreational value.
Definition:
Water Quality Impacts:
Sources:
N/A (This multifaceted indexing system used by the IN Clean Lakes Program.)
Source Examples:
Targets:
Limits:
This index requires few resources and little training. Understanding lake classification can help guide approaches to lake management. Trophic state data can be useful when repeated from year to year.
Indiana Trophic State Index
Indiana Trophic State Index
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
Physical Parameters
Physical characteristics of waterbodies are determined by senses of touch, sight, smell and taste. The information collected is used to understand some of the properties, functions, and landscape influences of the waterbody. There are numerous physical measurements that can be measured, however the following 12 parameters are common measurements that indicate physical stream characteristics and/or water quality conditions.
As with all other parameters it is important to collect numerous measurements and track the results over time.
Physical Parameters
There is a Quick Card for each of the following physical parameters:
Carlson’s Trophic State Index (CTSI)
Citizens Qualitative Habitat Evaluation Index (CQHEI)
Dissolved Oxygen (DO)
Electrical Conductivity (EC)
Indian Trophic State Index
pH
Qualitative Habitat Evaluation Index (QHEI)
Richards-Baker Flashiness Index
Rosgen Stream Classification System
Suspended Sediment Concentration (SSC)
Temperature
Total Dissolved Solids (TDS)

## Slide 12
Front of Card
Back of Card
Carlson’s Trophic State Index (CTSI)
The Carlson TSI is a measure of the trophic status of a body of water using several measures of water quality including: transparency or turbidity (using a secchi disk), chlorophyll-a concentrations (algal biomass), and total phosphorus levels. This index is a simple and quick way to demonstrate the associations between water clarity, nutrients and overall algal biomass, to classify and rank lakes.
This parameter does not have impacts it measures the overall health of the lake.
Definition:
Water Quality Impacts:
Sources:
N/A (This is a standard assessment tool. Often used in volunteer lake programs.)
Source Examples:
< 40 Oligotrophic (highest quality); 40 - 50 Mesotrophic (intermediate) 50 - 60 Eutrophic (low quality); > 60 Hypereutrophic (lowest quality)
Targets:
Scores from 0 - 100
Limits:
Carlson’s Trophic State Index (CTSI)
High nutrient levels lead to Eutrophic and Hypereutrophic classification. Eutrophication of streams and lakes often decreases the resources value, hindering the recreation, fishing, hunting and aesthetic enjoyment.
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
Blank
Blank
Blank

## Slide 13
N/A
Front of Card
Back of Card
< 1,200 microhoms/cm (IDEM Standard)
Electrical conductivity is the measure of the ability of water to pass an electrical current. There are a variety of solids that can occur in the dissolved phase depending on the inherent capacity of the water body to maintain this suspended or dissolved load of solids.
This measurement is typically a sign of a change in water chemistry and large variations could indicate contamination. However, its measurement alone will not be a direct impact to the waterbody.
Definition:
Water Quality Impacts:
Sources:
Excessive algae or plant growth or higher temperatures in the waterbody, industry, mining activities, limestone
Source Examples:
Targets:
Limits:
NP
Dissolved Oxygen (DO)
Dissolved oxygen measurements quantify the amount of oxygen that is dissolved in the water. DO is temperature and pressure sensitive.
DO levels vary in natural waters, however it is most typical to speak about low DO readings due to contamination that then affects the waterbodies’ ability to maintain biota.
Definition:
Water Quality Impacts:
Sources:
Stagnant water, excessive algae or plant growth or higher temperatures in the waterbody
Source Examples:
> 4 mg/L (IN WQS) < 12 mg/L (IDEM Target)
Targets:
< 2 mg/L does not allow aerobic (oxygen-using) biological processes. Most surface water bodies should have > 4 mg/L to help with healthy aquatic life. Very high DO is an indicator of high nutrients
Limits:
Dissolved Oxygen (DO)
Dissolved and suspended solids can increase the electrical conductivity. Distilled water or deionized water will have no conductivity. All natural waters will always have some level of EC.
The following will lower DO:
Stagnant water
Influx of nutrients
Excessive bio-activity
High DO is an indicator excess nutrients or highly agitated water body (e.g. fast flowing river).
Electrical Conductivity (EC)
Electrical Conductivity (EC)
NP
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf

## Slide 14
N/A
Lakes with water clarity less than 5 feet have poor water quality
Front of Card
Back of Card
< 500 mg/L (EPA drinking water recommendation)
Total dissolved solids (TDS) is the measure of amount of a broad array of molecules that are considered to be dissolved in the water. While TDS does not indicate contamination directly, and many natural waters have a very wide range of values (e.g. 1 ppm in rain water to >1,000 ppm in sea water) it is a good indicator measurement as it is quick, cheap and if done regularly can indicate the water is changes in chemistry over time.
Definition:
Water Quality Impacts:
Sources:
Bare soil, construction activities, stream bank erosion, storm water, pesticide use, road salt, agricultural land use, WWTPs
Source Examples:
Targets:
Limits:
NP
< 25 NTU (MN Standard)
< 10.4 NTU (EPA recommendation)
Turbidity
Turbidity (also called transparency) is the measure of water clarity. This is the measure of the scattering of light through the water. The higher the turbidity the less light can travel through the water.
Definition:
Water Quality Impacts:
Sources:
Bare soil, construction activities, stream bank erosion, storm water, WWTPs
Source Examples:
Targets:
Limits:
Turbidity
Total Dissolved Solids (TDS)
Total Dissolved Solids (TDS)
NP
Phosphorus and metals are attracted to sediment particles which increase nutrient levels and toxic metals in streams. High levels of sediment can stop light penetration reducing plant growth and when it settles can cover valuable habitat for aquatic animals
May give water a murky appearance and change the taste of drinking water. Levels are associated with water hardness and may increase corrosiveness.
Turbidity and transparency indicate
visibility in water. High turbidity has
often been linked to bacterial pollution. Increasing turbidity is correlated to storm events and stream flow. It is used as a good indicator of stresses to the aquatic system.
Essentially this is the measure of all minerals, metals, and salts dissolved in the water that are < 2 micrometers in size. Therefore the source could be any occurrence of added materials to the water body (e.g. excessive runnoff).
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf

## Slide 15
Fish, insects, zooplankton, algae and other species all prefer temperature ranges to varying degrees.
< 20 mg/L, water is clear
40 - 80 mg/L, water is cloudy
> 150 mg/L, water is dirty
Front of Card
Back of Card
Normal daily and seasonal temperature fluctuations shall be maintained.
Temperature is the measure of the degree of heat in a waterbody. Temperature above all other characteristics of a water body plays a major role in controlling chemical and biological activity.
Increased water temperature decreases the amount of oxygen available to aquatic organisms. Also some chemicals are more toxic to aquatic life at higher temperatures.
Definition:
Water Quality Impacts:
Sources:
Stagnant water, isolated pools, lack of shaded areas along stream banks, industry, impervious surfaces all increase temperature of the water body
Source Examples:
Targets:
Limits:
NP
Total Suspended Solids (TSS)
The total suspended solids (TSS) measurement quantifies all particles suspended and dissolved solids in water.
Definition:
Water Quality Impacts:
Sources:
Bare soil, construction activities, stream bank erosion, storm water, WWTPs
Source Examples:
< 30 mg/L (IDEM Target)
Targets:
Limits:
Total Suspended Solids (TSS)
Air temperature, amount of light hitting the water, water depth, turbidity, groundwater contributions and land use all impact stream temperatures.
Temperature
Temperature
NP
Phosphorus and metals are attracted to sediment particles which increase nutrient levels and toxic metals in streams. High levels of sediment can stop light penetration reducing plant growth and when it settles can cover valuable habitat for aquatic animals
Suspended materials include soil particles (clay, silt and sand), algae, plankton, microbes and other substances, which typically range in size from 0.004 mm (clay) to 1.0 mm (sand).
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf

## Slide 16
NA
Front of Card
Back of Card
A method for classifying streams and rivers based on common patterns of channel characteristics (i.e. river patterns, profiles, dimensions and substrate).
The stream levels are classified using channel and land use characteristics to determine sediment supply, stream sensitivity to disturbance, potential for natural recovery, channel response to changes in flow regime and fish habitat potential.
Definition:
Water Quality Impacts:
Sources:
Limits:
< 25 mg/L (EPA recommendation for excellent fisheries)
25 – 80 mg/L (EPA recommendation for good to moderate fisheries)
Suspended Sediment Concentration (SSC)
Suspended sediment concentration (SSC) is a measure of the solid-phase material suspended in a water-sediment mixture and is usually expressed in mg/L.
Definition:
Water Quality Impacts:
Sources:
Bare soil, construction activities, stream bank erosion, storm water, WWTPs
Source Examples:
Targets:
Limits:
Suspended Sediment Concentration (SSC)
Rosgen Stream Classification System
Rosgen Stream Classification System
NP
Suspended materials include soil particles (clay, silt and sand) only. Regular monitoring of SSC can help
detect trends that might indicate increasing erosion.
Phosphorus and metals are attracted to sediment particles which increase nutrient levels and toxic metals in streams. High levels of sediment can stop light penetration reducing plant growth and when it settles can cover valuable habitat for aquatic animals.
NA
NA
Not used to determine water quality but can be used for stream restoration studies.
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf

## Slide 17
Productivity of aquatic ecosystems is reduced considerable with pH < 5
Front of Card
Back of Card
9 SU > pH > 6 SU
pH is the measure of the concentration of hydrogen ions in a solution (water or other). The measure is stated in a standard units from 0 to 14 with 7 being natural and typically ideal for municipal processes. If pH is < 7 it is considered “acidic” and > 7 it is “basic”. It is measured in standard units (SU).
pH indicates whether the water can support aquatic life. pH also has effects on the toxicity of other substances (i.e. iron, aluminum, mercury).
Definition:
Water Quality Impacts:
Sources:
Mining activities, industry, wetlands
Source Examples:
Targets:
Limits:
NP
Richards-Baker Flashiness Index
An index used to quantify the frequency and rapidity of short-term changes in stream flow caused by storm events.
The index is a tool for diagnosing the scale of a stream channel or stability problem and can be used in determining sites to install management practices.
Definition:
Water Quality Impacts:
Sources:
Changes in land use will increase flashiness of a stream.
Source Examples:
The R-B index is influenced by the size of the watershed, percent of impervious surface area, and amount of tile drainage so target levels are not recommended. Instead index values can be analyzed over time to develop trends. )
Targets:
Daily flow is needed, so the index can only be calculated for sites and time periods where continuous flow data exists
Limits:
Richards-Baker Flashiness Index
pH is sensitive to many water quality characteristics. Even temperature can change the pH level of a solution. pH can be affected by organic material, acid precipitation, bedrock and soil composition, and industry and mining activities.
pH
pH
A tool used to reduce sediment loads
entering a stream due to stream bank
erosion.
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf

## Slide 18
Score ranges from 0 - 114
Front of Card
Back of Card
(70-100) "Exceptional Warm Water Habitat”
(61-69) "Warm Water Habitat (WWH)
(50-60) "Warm Water Habitat," but some features are lacking
(0-49) "Modified Warm Water Habitat”
The CQHEI is a physical habitat index that was developed by the Ohio Environmental Protection Agency to be used as a "citizens" companion to the QHEI used by State professionals. The purpose of the index is to provide a measure of the stream habitat and riparian health that generally corresponds to physical factors affecting aquatic life.
Habitat is strongly correlated to the biological communities living in a stream. This index provides much more description of the habitat characteristics so that anyone can understand the terminology.
Definition:
Water Quality Impacts:
Sources:
Targets:
Limits:
Qualitative Habitat Evaluation Index (QHEI)
The QHEI is a physical habitat index that was developed by the Ohio Environmental Protection Agency in 1989 to evaluate stream and river habitat characteristics important to biological communities. The purpose of the index is to provide a measure of the stream habitat and riparian health that corresponds to physical factors affecting aquatic life.
Habitat is very strongly correlated to the biological communities a stream can support. Species of fish and aquatic bugs have different habitat requirements. A variety of habitat types supports a more diverse biological community.
Definition:
Water Quality Impacts:
Sources:
Sunfish live in pools, darters live in riffles, some suckers require flowing. water
Source Examples:
Excellent ≥ 70; Good 55-69; Fair 43-54; Poor 30-42; Very Poor <30
Targets:
The scores range from 0 - 100 and < 50 is viewed as being impaired although not used to impair streams on the IN 303(d) list.
Limits:
The characteristics used to calculate the index include bottom type, hiding places, stream shape and human alterations, riparian areas and erosion, stream depth velocity, riffles and runs.
The characteristics used to calculate the index include substrate, riparian zone, streambank erosion, channel morphology, instream cover (i.e. woody debris, boulders), riffle, run and pool quality, and gradient.
Citizens Qualitative Habitat Evaluation Index (CQHEI)
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
https://engineering.purdue.edu/watersheds/monitoring/MonitoringWaterinIndiana.2012.1.pdf
Qualitative Habitat Evaluation Index (QHEI)
Citizens Qualitative Habitat Evaluation Index (CQHEI)