## Slide 1: Wetland Creation
Why and How
Char Ison and Caleb Asbury

## Slide 2: What is a Wetland
A wetland contains land that is wet, although it may not be wet year round. Water must be in large enough quantities (either at the surface or in groundwater) during the growing season. Most wetlands are associated with shallow water and aquatic plants. Wetlands are often characterized as a transition from upland to aquatic habitat.

## Slide 3: Types of Wetlands
Types:
  Bog, swamp, fen, prairie pothole, marshes (tidal and non-tidal), wet meadow, vernal pool, etc.
Categories:
  Emergent and forested
Wetland types differ primarily by where their water comes from (groundwater, surface water, and precipitation) as well as other factors (landscape position, latitude, pH, salinity, soils, inundation frequency, etc.)

## Slide 4: Wetland Importance
Water purification
Water storage
Prevent saline intrusion
Groundwater recharge and discharge
Flow regulation and flood mitigation
Critical habitats for plants and animals
Biodiversity

## Slide 5: Reasons to Make a Wetland
Stormwater treatment
Landscaping (rain garden)
Treatment of heavy metals, sewage, etc.
Sediment and nutrient uptake and capture
Mitigate (offset for) damages to wetlands made during construction or development

## Slide 6: How to Create a Wetland
Caleb Asbury, Davey Resource Group

## Slide 7: Wetland Permitting
Permitting is required if:
  Impacting a wetland by dredging or filling
    Required through the Clean Water Act
    The US EPA oversees the CWA
    The US Army Corps of Engineers provides enforcement for “waters of the US”
    IDEM regulates “water of the state”

## Slide 8: Wetland Permitting
Permitting is required if:
  Indiana Division of Natural Resources
    Lowering of 10 Acre Lakes
    Lake Preservation Act
    Navigable Waterways Act
    Flood Control Act
  Local zoning and ordinances may require permitting
  County Surveyors must be aware if the wetland will affect a regulated drain

## Slide 9: Wetland Creation Example
Real world example in Laotto, IN
Wetland creation from scratch
Hydrology comes from precipitation
Hydrology controlled by water control box

## Slide 10: First, Find a Site
A suitable site must be found for wetland creation
  Looking for water inputs
  Existing wetland vegetation
  Soils with hydric properties
Also will need permission from landowner

## Slide 11: Design
Professional Survey
Engineers
  Must design a wetland that provides adequate hydrology, soils, and vegetation
  These are the three large components required for mitigation projects to succeed.

## Slide 12: Coordination
Keep all stakeholders involved
  Landowner
  Regulatory agencies
  County Surveyor
  Client (entity causing mitigation process)
  Engineers/surveyors
  Earthwork contractor
Submit mitigation plan to regulatory agencies for approval--it contains goals required for eventual mitigation release

## Slide 13: Construction
Can we build it? Yes we can! They said it was OK!
Microtopography is a good thing
Lots of planting

## Slide 14: Maintenance
Make sure the goals of the mitigation plan are being met
Keep invasive species out
Additional seeding and planting may be required--keep in touch with agencies

## Slide 15: Apply for Release
Generally:
  IDEM regulated mitigation sites (isolated wetlands) and USACE-IDEM (“waters of the US”) must meet goals for 3 consecutive years
  Mitigation typically lasts 5 years or 10 years.
  The mitigation process is extended if goals are not met in this timeframe

## Slide 16: Hopefully Ending with...

## Slide 17: Questions?
Thank you all for listening and we hope you learned something!