## Slide 1: ECE 255
Jan 9, 2018 Lecture
Instructor: Weng Cho Chew

## Slide 2: Clicker Test Question 1
Have you used clicker in class before?
Yes
No

## Slide 3: Clicker Test Question 2
Have you registered your clicker on Black Board?
Yes
No

## Slide 4: ECE 255
Small Signal Model
Diode Normal Breakdown | Bipolar Junction Transistor Q (Ic, VCE) | Field-effect Transistor Q (IDS, VDS)
Introduction to Semiconductor Drift Currents Diffusion Currents
Bipolar Junction Transistor Based Amplifier Voltage Gain, Av Input, Output Resistance Common-Emitter Common-Collector Common-Base | Field-effect Transistor Based Amplifier Voltage Gain, Av Input, Output Resistance Common-Source Common-Drain Common-Gate
DC Analysis
Small Signal Model
Bipolar Junction Transistor Based Amplifier Low cutoff frequency High cutoff freqency | Field-effect Transistor Based Amplifier Low cutoff frequency High cutoff freqency
AC Analysis
Frequency Analysis
Basic Knowledge

## Slide 5: The Start of the Modern Electronics Era
Bardeen, Shockley, and Brattain at Bell Labs - Brattain and Bardeen invented the bipolar transistor in 1947.
The first germanium bipolar transistor. Roughly 50 years later, electronics account for 10% (4 trillion dollars) of the world GDP.

## Slide 6: Evolution of Electronic Devices
Vacuum
Tubes
Discrete
Transistors
SSI and MSI
Integrated
Circuits
VLSI
Surface-Mount
Circuits

## Slide 7: Moore’s Law
The number of transistors in a dense IC doubles approximately every two years.

## Slide 8: Device Feature Size
Feature size reductions enabled by process innovations.
Smaller features lead to more transistors per unit area and therefore higher density.
ISSCC--International Solid-State Circuits Conference
ITRS--International Technology Roadmap for Semiconductors

## Slide 9: Rapid Increase in Density of Microelectronics
Memory chip density versus time
ISSCC--International Solid-State Circuits Conference
ITRS--International Technology Roadmap for Semiconductors

## Slide 10: Figure 1.6 Digital Signals

## Slide 11: Figure 1.7
Analog Signal
Digital Signal

## Slide 12: Figure 1.8

## Slide 13: The Inventors of the Integrated Circuit
Jack Kilby
Andy Grove, Robert Noyce, and Gordon Moore with Intel 8080 layout.

## Slide 14: The Kilby Integrated Circuit
Semiconductor die
Active device
Electrical contacts
(wiki) As of 2016, the largest transistor count in a commercially available
single-chip processor is over 7.2 billion—the Intel Broadwell-EP Xeon.

## Slide 15: Full Periodic Table (Carbon Column, Most Important)

## Slide 16: Semiconductor Materials (cont.)
Semiconductor | Bandgap Energy EG (eV)
Carbon (diamond) | 5.47
Silicon | 1.12
Germanium | 0.66
Tin | 0.082
Gallium arsenide | 1.42
Gallium nitride | 3.49
Indium phosphide | 1.35
Boron nitride | 7.50
Silicon carbide | 3.26
Cadmium selenide | 1.70
IV
IV
IV
IV
III-V
III-V
III-V
III-V
IV
II-VI

## Slide 17: Solid-State Electronic Materials
Electronic materials fall into three categories:
  Insulators Resistivity () > 105 -cm
  Semiconductors 10-3 <  < 105 -cm
  Conductors  < 10-3 -cm
Elemental semiconductors are formed from a single type of atom, typically Silicon.
Compound semiconductors are formed from combinations of column III and V elements or columns II and VI.
Germanium was used in many early devices.
Silicon quickly replaced germanium due to its higher bandgap energy, lower cost, and is easily oxidized to form silicon-dioxide insulating layers.

## Slide 18: Bandgaps of Different Materials

## Slide 19: Bandgap in Semiconductor

## Slide 20: Covalent Bond Model
Silicon diamond lattice unit cell.
(stackable)
Corner of diamond lattice showing four nearest neighbor bonding.
(non-stackable)
View of crystal lattice along a crystallographic axis.

## Slide 21: Silicon Covalent Bond Model (cont.)
Near absolute zero, all bonds are complete. Each Si atom contributes one electron to each of the four bond pairs.
Increasing temperature adds energy to the system and breaks bonds in the lattice, generating electron-hole pairs.
Holes and electrons are charge carriers.

## Slide 22: Electron-hole Concentrations
A vacancy is left when a covalent bond is broken.
The vacancy is called a hole.
A hole moves when the vacancy is filled by an electron from a nearby broken bond (hole current).
Hole density is represented by p.
For intrinsic silicon, n = ni = p.
The product of electron and hole concentrations is pn = ni2.
The pn product above holds when a semiconductor is in thermal equilibrium (not with an external voltage applied).

## Slide 23: Intrinsic Carrier Concentration
Recombination and thermal generation causes n and p to remain constant.
The density of intrinsic carriers in a semiconductor as a function of temperature and material properties is:
EG = semiconductor bandgap energy in eV (electron volts)
k = Boltzmann’s constant, 8.62 x 10-5 eV/K
T = absolute temperature, K
B2 = material-dependent parameter, 1.08 x 1031 K-3 cm-6 for Si
B=7.3 x 1015 K-3/2 cm-3 for Si
Bandgap energy is the minimum energy needed to free an electron by breaking a covalent bond in the semiconductor crystal.

## Slide 24: Example 3.1 from S&S

## Slide 25: Intrinsic Carrier Concentration (cont.)
Electron density is n (electrons/cm3) and ni for intrinsic material n = ni.
Intrinsic refers to properties of pure materials.
ni ≈ 1010 cm-3 for Si
Intrinsic carrier density (cm-3)

## Slide 26: Donor Impurities in Silicon
Phosphorous (or other column V element) atom replaces silicon atom in crystal lattice.
Since phosphorous has five outer shell electrons, there is now an ‘extra’ electron in the structure.
Material is still charge neutral, but very little energy is required to free the electron for conduction since it is not participating in a bond.
n type doped silicon with phosphorous. Electron carrier density (concentration) n is increased.

## Slide 27: Doping to Change Carrier Density
Minority carrier
Majority carrier

## Slide 28: Acceptor Impurities in Silicon
Boron (column III element) has been added to silicon.
There is now an incomplete bond pair, creating a vacancy for an electron.
Little energy is required to move a nearby electron into the vacancy.
As the ‘hole’ propagates, charge is moved across the silicon.

## Slide 29: Acceptor Impurities in Silicon (cont.)
Hole is propagating through the silicon.
p type doped silicon with phosphorous. Hole carrier density or concentration p is increased.

## Slide 30: Example 3.2 of S&S

## Slide 31: Prior Concepts You Need to Know
Kirchhoff’s Voltage and Current Laws
Thevenin & Norton Theorem:
  Any linear electrical network with voltage and current sources and only resistors can be replaced at terminals by an equivalent voltage source, Vth, and an equivalent resistance, Rth.

## Slide 32: Clicker Question 1 (0 Point)
What is the intrinsic carrier density (ni) of Si at room temperature:
1010 cm-3
1022 cm-3
104 cm-3

## Slide 33: Clicker Question 2 (0 Point)
How many Si bonds are broken by thermal energy at room temperature?
10%
100%
~1 per 1013 bonds
50%

## Slide 34: Clicker Question 3 (0 Point)
Si: T=300K, ND=1017/cm3, is it n type or p type?
n type
p type
intrinsic

## Slide 35: Clicker Question 4 (0 Point)
Si: T=300K, ND=1017/cm3, hole concentration p=?
1017/cm3
0/cm3
1010/cm3
103/cm3