## Slide 1
Design for Stability
Direct Analysis Method
CE 470 (Fall 2016)
Saahastaranshu R. Bhardwaj

## Slide 2: How Will You Design??

## Slide 3: Stability
“the capacity of a compression member, element, or frame to remain in position and support load, even if forced slightly out of line or position by an added lateral force” (Galambos, 1998)
Figure from NASCC: The Steel Conference 2014, Session N40, Geschwindner
Slide from Dr. Liu’s presentation

## Slide 4: AISC Design for Stability
Stability to be provided for structure as whole, and each elements.
Discusses the effects that need to be considered
Any rational method considering these effects can be used
Methods identified
  Chapter C: Direct Analysis Method (DAM)
  Appendix 7: Alternative Methods (effective length method & first order analysis methods) subject to constraints

## Slide 5: 5 factors that influence stability
Member, component, and connection deformations
Second-order effects (P-D and P-d)
Geometric imperfections (out-of-plumbness or out-of-straightness)
Stiffness reductions due to inelasticity (residual stresses)
Variability in component and system stiffness
Slide from Dr. Liu’s presentation

## Slide 6: Second Order Effects
Slide from Dr. Liu’s presentation

## Slide 7: Chapter C DAM: Analysis Requirements
Consider axial, flexural, and shear deformations in members, and connection deformations: accounted for directly by analysis
Consider second order effects: perform rigorous analysis or use approximate method in Appendix 8
All loads influencing the stability need to be considered. For LRFD, use combinations. For ASD, use 1.6 times the combinations for analysis, divide the demands by 1.6

## Slide 8: Second Order Analysis
Rigorous non-linear analysis in the software considering second order effects
Approximate second order analysis (Appendix 8)
  Multipliers B1 and B2 to consider the second order effects

## Slide 9: Chapter C DAM: Initial Imperfections
Directly model the imperfections
Use Notional Loads
Slide from Dr. Liu’s presentation

## Slide 10: Chapter C DAM: Initial Imperfections
Slide from Dr. Liu’s presentation

## Slide 11: Chapter C DAM: Stiffness
Reduce stiffness contributing to stability by 20%
Further reduce flexural stiffness by a factor , depending of the ratio of axial compression demand and yield strength

## Slide 12: Chapter C DAM: Available Strengths
Provisions of Chapters D, E, F, G, H, I, J, K.
Effective length, K=1

## Slide 13: 5 factors that influence stability (DAM)
Member, component, and connection deformations:
addressed directly in analysis
Second-order effects (P-D and P-d) : rigorous second-order analysis or first-order with B1-B2
Geometric imperfections (out-of-plumbness [notional loads or direct modeling] or out-of-straightness [column design equations; and reduced stiffness for effect on structure stiffness]
Slide from Dr. Liu’s presentation

## Slide 14: 5 factors that influence stability (DAM)
Stiffness reductions due to inelasticity (residual stresses) : column design equations; and reduced stiffness for effect on structure stiffness
Variability in component and system stiffness: in resistance and safety factors!
Slide from Dr. Liu’s presentation

## Slide 15: App. 7 Effective Length Method (ELF): Limitations
Gravity loads supported primarily by vertical columns, walls or frames

## Slide 16: App. 7 Effective Length Method (ELF)
Required Strength: Analysis same as for DAM, except stiffness reduction is not applied. Notional load is applied, second order analysis is performed.
Available Strength: with provisions of Chapters D-K.
  K needs to be calculated for each case
  Alignment charts provided in the commentary can be used

## Slide 18: Comparison
AISC C-C2.3

## Slide 19: How Will You Design??

## Slide 20: Direct Analysis Method: Example
SAP 2000 is used to analyze the frame shown below, using the provisions of Chapter C.

## Slide 21: DAM Example: Assumptions
The loads provided are factored loads from combinations
Self-weight is included in the loads provided
Since there is a lateral load applied, notional load is considered in one direction

## Slide 22: DAM Example: Procedure
Check if the software to be used considers the P-Δ and P-δ effects
This is done using the benchmarking problems provided in the commentary to Chapter C
An elastic first order analysis is performed, then a second order analysis based on Chapter C is performed
The results of both the analysis are compared

## Slide 23: DAM Example: Benchmarking

## Slide 24: DAM Example: Elastic Analysis
The frame is modeled with W shapes chosen according to the section properties in problem (Beam section: W 27x84 , Column Section: W 10x45).
Linear Static Loading category is selected and the given loads are applied.
Model is analyzed and member forces and story drifts are noted.

## Slide 25: DAM Example: Non-Linear Analysis
The Loading is changed to Non-Linear static category and P-Δ effects are selected (to take care of second order effects).
P-δ effects are considered by creating nodes along the length of the members.
The top ends of columns are offset by H/500 (to take care of initial out-of plumbness, instead of applying notional load). Notional load can be applied by selecting notional loads from ‘More’ submenu under Load patterns.

## Slide 26: DAM Example: Non-Linear Analysis
The stiffness of all beam columns is reduced by 20% by using area and inertia reduction factors (to take into account the residual stresses in the elements). Can also be done by reducing E value (will need to be changed again if design is performed by the software)
For central column, Pr > 0.5×Py . Hence, its flexural stiffness needs to be further reduced by Instead of doing this, an additional Notional Load of 0.1% of the Gravity Load is applied at the corresponding locations of the gravity loads (SAP has option to automatically calculate , but one needs to design and then go back and analyze again).
Model is analyzed and member forces and story drifts are noted.

## Slide 27: DAM Example: Comparison

## Slide 28: DAM Example: Conclusion
The moment magnification is of the order of 2.5. This is due to high magnitude of forces being applied.
The second order drift is about three times the first order drift.
When designed, it is observed that the member demands (considering second order effects) exceed the member design strengths.

## Slide 29: Thanks!!