## Slide 2: Stress Calculation at the Gauss Points
For all finite elements, the strain are likely to vary over the element and likely to be more accurate at some locations than others.
It so happens that the locations of greatest accuracy are apt to be the same Gauss points that were used for integration of the stiffness matrix.
Consider the Figure 4.7-2, which shows a portion of a beam in which shear strain is gamma-xy constant along the x-axis.
The shear strain calculated by FE displays a quadratic variation that is most accurate at x-coordinates of the Gauss points

## Slide 3: Stress Calculation at the Gauss Points
It is common practice to use an order 2 Gauss rule (four points) to integrate K of four- and eight- node plane elements, and to compute strains and stresses at these same points.
Similarly for 3D elements we often use eight Gauss points for stiffness integration and stress calculation.
Stresses at nodes or at other element locations are obtained by extrapolation or interpolation from Gauss point values.
Thus, the element stress field is represented by bi- or trilinear in isoparametric coordinates
For eight-node elements this is a polynomial of lower degree than contained in the B matrix, and therefore some information has been discarded. Nevertheless, accuracy is greatest when the element stress field is a polynomial fitted to the Gauss point values.