# CE 595: Finite Elements in Elasticity

# HW#1 Problem

# Problem #1

Given: A cantilevered beam has a length L, constant cross-sectional area A, constant moment of inertia , and a variable Young’s modulus . It is loaded by a vertically upward line load . Assume that there is no body force present and that bending strain energy is the only significant contributor to internal work.

Required: Using the Rayleigh-Ritz method on the Principle of Virtual Displacements, derive an approximate expression for the vertical deflection  of the beam’s centerline using the approximating function , where , , and  are unknown constants.

Hint: Bending strain is computed by , and bending stress is computed by . Be sure to write your volume integrals in the form  and remember how  is defined!