# ECE 438	Assignment No. 1	Spring 2023

1.	For the signals  shown below, do the following:

i.	Sketch x[n] by hand, i.e. don’t use Matlab or Python

ii.	Calculate the metrics , , , , , and  by hand.

iii.	Sketch y1[n] and y2[n] by hand, where y1[n] and y2[n] are, respectively, the result of downsampling with D = 3, and upsampling with D = 3.

a.

b.

2.	For the CT signal

,

do the following:

a.	Sketch  by hand, i.e. don’t use Matlab or Python

b.	Sketch  by hand, i.e. don’t use Matlab or Python

3.	For each signal x[n] below, do the following:

i.	Use MATLAB or Python to compute the result of the following two filtering operations:

- Use MATLAB or Python to generate stem plots for , , and  for . Plot all three signals on the same page, using the subplot command.

- Describe in detail the effect that each filter has on the signal.

Note:  Be sure to turn in printouts of all MATLAB or Python code.

a.

b.

4.	For each system below, determine whether or not it is:

i.	linear,

ii.	time-invariant,

iii.	memoryless

For the properties i) and ii), if you think it holds, prove it.  Otherwise, find a counter-example.  In addition, find the response to an impulse (unit sample).

a.

b.

c.