## Slide 1: Joint Design of CMY Screen Sets Using DBS

## Slide 2: About the Author
Y. Yang and J. Allebach, “Joint Design of Plane-Dependent FM Screen Sets Using DBS Algorithm,” Proceedings of CIC27 – IS&T’s 27th Color Imaging Conference, 21-25 October 2019, Paris FRANCE.
This presentation is part of Yi Yang’s Preliminary Examination presentation – 10 July 2020.

## Slide 3
Background
Kang H R. Digital color halftoning[M]. SPIE press.
Lee J H, Allebach J P. Colorant-based direct binary search halftoning[J]. Journal of Electronic Imaging, 11(4): 517-528.
Allebach J P. DBS: retrospective and future directions[C],Color Imaging: Device-Independent Color, Color Hardcopy, and Graphic Arts VI. International Society for Optics and Photonics, 4300: 358-376.
1. AM and FM1
Method | Operation | Image Quality | Speed | Implementation Complexity
Screening | Pixel comparison | Good | Fast | Simple
DBS | Iterative search | Excellent | Slow | Complex
AM
FM
2. Independent and Dependent2
3. Screening and DBS
algorithm 3
Independent
Dependent

## Slide 4: Motivation
Our goal: Combine advantages of Screening and DBS
Keys:
  Color representation.
  High quality.
  Speed and complexity.
  Jointly design FM, dependent screens set for C, M and Y colorants.
  Using the DBS algorithm.
  Simple and fast to use.
  Great halftoned image quality.

## Slide 5: Outline of Topic 1:
Background and Motivation
Color DBS Algorithm and Screens Design
Joint Design Algorithm
Implement and Results
Comparison Results
Conclusion

## Slide 6: DBS Halftoning Algorithm
* Allebach J P. DBS: retrospective and future directions[C]//Color Imaging: Device-Independent Color, Color Hardcopy, and Graphic Arts VI. International Society for Optics and Photonics, 4300: 358-376.

## Slide 7: DBS Search Heuristic
* Allebach J P. DBS: retrospective and future directions, Color Imaging: Device-Independent Color, Color Hardcopy, and Graphic Arts VI. International Society for Optics and Photonics, 4300: 358-376.
the

## Slide 8: Screening method
* Allebach J P. Advanced topic in digital halftoning – 17-19 October 2016.
Screening is a Thresholding Process
  Simple point-to-point transformation of each pixel in the continuous-tone image to a binary value.
  Process requires no memory or neighborhood information.
The following are equivalent terms in Halftoning:
Threshold matrix, Screen, Dither matrix, Mask

## Slide 9
* Allebach J P. Advanced topic in digital halftoning – 17-19 October 2016.
Level-by-level design:
Design by generating uniform pattern for each gray level.
Must follow stacking constraint*.
Screens Design -- Level-by-level design of the dot profile function
Dot profile function (halftone pattern) * :
Stacking constraint:

## Slide 10: Outline of Topic 1:
Background and Motivation
Color DBS Algorithm and Screens Design
Joint Design Algorithm
Implement and Results
Comparison Results
Conclusion

## Slide 11: Quality Conditions for the Designed Screens Set
The pattern of each colorant (C, M, or Y) should be arranged as uniform as possible.
The overall composite pattern that consists of all three colorants should be as uniform as possible.
keep dot-off-dot as much as possible during the process of design screens.
For obtaining homogeneous halftone images, all levels patterns of screens need to satisfy the following conditions*.
* Je H. Lee and Jan P. Allebach, “CMYK Halftoning Algorithm Based on Direct Binary Search". Color and Imaging Conference. Vol. 6.
Fig 14-2. The zoomed-in details (16×16) of a dot-on-dot pattern.
Fig 14-1. The zoomed-in details (16×16) of a dot-off-dot pattern.
Pattern has:
Secondary colors:
B = C + M
G = C + Y
R = M + Y
Tertiary Color:
K = C + M + Y
Pattern only has Primary Colors:
C, M, and Y

## Slide 12
Error Metrics for Joint Design Algorithm
Spatial coordinates:
Discrete image:
HVS filter:
Perceived discrete image:
Continuous-tone
Halftone
Perceived error through HVS is：
Error between original continuous-tone image and the halftone image is:
* Used Nasanan's HVS model

## Slide 13
Monochrome Error Metric：
Dual Error Metric：
Error Metrics for Joint Design Algorithm

## Slide 14
Design the starting Level.
Select a certain level as the starting level.
Generate an initial pattern for this level.
Optimize the initial pattern by reducing error metric to obtain a homogeneous pattern for this level.
Level-by-Level design of darker levels below and lighter levels above the starting Level.
  Add/ Remove certain number of dots from previous level pattern to get an initial pattern.
  Optimize the initial pattern by reducing error metric to obtain a homogeneous pattern.
Apply color control for each level.
Pipeline of Joint Design Screens

## Slide 15: Designing the starting Level
Fig 16-1. A CMY color pattern as a combination of three different C, M and Y patterns.
Select a certain level as the starting level.
The screen is assumed to be L levels and n colorants:
Choice:
floor (L/n) th level
Reason: (almost) full covered by color dots.
In our work, the starting level is = 85 th level.
Generate three initial patterns with a certain number of dots.

## Slide 16
Apply swap-only DBS algorithm to iteratively compute the Dual Error Metric between two different colorants.
Current pixel
swap2
swap3
swap1
Fig 17-1. Possible swap trials between two colorants.
3. Optimize the initial patterns to obtain a homogeneous pattern.
Designing the starting Level
Iteration:
error not converges || (# iterations < threshold)
C with M
C with Y
M with Y

## Slide 17
Uniform combination pattern
Optimized pattern of Magenta
Optimized pattern of Cyan
Initial pattern of Cyan
Initial pattern of Magenta
The initial pattern of combination of Cyan and Magenta.
The optimized pattern of combination of Cyan and Magenta.
Initial
Optimized

## Slide 18
Uniform pattern of starting level
Fig 21-1. The initial and optimized pattern of combination of Cyan, Magenta and Yellow.

## Slide 19
The screen is assumed to be MxM pixels; and L is the number of levels in the screen.
Lighter levels:
Randomly remove M2/L dots from C, M and Y starting pattern respectively to get the pattern of the next lighter level.
Perform trial swaps between newly removed dots with existing dots to reduce the Monochrome Error Metric(Eq.1) of each pattern independently.
Apply constraints to guarantee the composite pattern is totally dot-off-dot.
Darker levels:
Randomly add M2/L dots into the C, M and Y starting pattern respectively to get the new pattern of the next darker level.
Perform trial swaps between newly added dots of different colorants to reduce the Dual Error Metric(Eq.2 ).
Apply several constraints to control the appearance of secondary colors.
Level-by-level Design Method

## Slide 20
Secondary colors:
Red
Green
Blue
Tertiary color:
Black
Apply color control.
Reasons
Steps

## Slide 21
Uniform patterns for lighter/ darker levels
Figure 24-1. The patterns for Magenta colorant in the 1st, 2nd, and 3rd levels.
Magenta colorant
Figure 24-2. The patterns for the Magenta colorant in the 85th, 130th and 160th levels

## Slide 22: Outline of Topic 1:
Background and Motivation
Color DBS Algorithm and Screens Design
Joint Design Algorithm
Implement and Results
Comparison Results
Conclusion

## Slide 23
CMY joint screens set implement
Separate a color image into R, G and B channels
Apply gamma de-correction to each channel
Convert components of RGB to CMY color space.
The halftoning rule is:
If C_channel[i,j] < C_screen[i,j], print a cyan dot at [i,j];
If M_ channel[i,j] < M_screen[i,j], print a magenta dot at [i,j];
If Y_ channel[i,j] < Y_screen[i,j], print a yellow dot at [i,j].
Where C, M and Y screens are jointly designed screens for cyan, magenta and yellow.

## Slide 24
Halftoning results
Figure 27-1. Continuous-tone color image
Figure 27-2. Image halftoned using jointly designed screen set.

## Slide 25: Outline of Topic 1:
Background and Motivation
Color DBS Algorithm and Screens Design
Joint Design Algorithm
Implement and Results
Comparison Results
Conclusion

## Slide 26
Figure 29-1. Comparison of the zoomed-in detail of same regions in the two halftone images.
Comparison
Image halftoned by independently designed screens.
Image halftoned by jointly designed screens.
Lighter tone
No secondary colors:
(red, green, blue).
Mid tone
Darker tone
Has a lot of tertiary color.
Has secondary colors:
(red, green, blue).
No secondary colors:
(red, green, blue).
Has secondary colors and tertiary color :
(red, green, blue, black).
Has secondary color, and a small amount of tertiary color.

## Slide 27
Figure 30-1. Comparison of the zoomed-in detail of same regions in the two halftone images.
Dot profile.
This pattern has fewer secondary colors, does not have tertiary color or white holes.
Therefore, the overall image appears more uniform.
This pattern has numerous secondary colors, tertiary color and white holes.
Therefore, the overall image appears grainy.
Comparison
Image halftoned by independently designed screens.
Image halftoned by jointly designed screens.

## Slide 28: Outline of Topic 1:
Background and Motivation
Color DBS Algorithm and Screens Design
Joint Design Algorithm
Implement and Results
Comparison Results
Conclusion

## Slide 29
Conclusion
We investigated the advantages and disadvantages of the main color halftoning algorithms and proposed a method that can combine the Screening and the DBS.
We showed our results having better quality than regular Screening halftoning, and simpler to use than the color DBS halftoning.
We designed joint screens sets for Cyan, Magenta, and Yellow colorants, which can be used to halftone color images directly by pixel comparison.
It is convenient to store and simple to use, which is suitable for generating various color halftone images.