## Slide 1
Jiayin Liua , Altyngul Jumabayevaa, Yujian Xua, Yin Wanga, Tal Frankb, Shani Gatb,
Orel Bat Morb, Yotam Ben-Shoshanb, Robert Ulichneyc, and Jan Allebacha
aSchool of Electrical and Computer Engineering,
Purdue University, West Lafayette, IN 47907, U.S.A.;
bHewlett-Packard Indigo Division, Rehovot, Israel;
cHewlett-Packard Laboratories USA, Cambridge, MA 02142, U.S.A.
New results for aperiodic, dispersed-dot halftoning*
*This work was supported by HP Inc., Indigo Division, Israel

## Slide 2: MS-MP-CLU-DBS Screen Design Using DBS

## Slide 3: About the authors (1/3)

## Slide 4: About the authors (2/3)
P. Goyal, M. Gupta, C. Staelin, M. Fischer, O. Shacham, J. Allebach, “Clustered-Dot Halftoning with Direct Binary Search,” IEEE Trans. on Image Processing, Vol. 22, pp. 473-487, February 2013.

## Slide 5: About the authors (3/3)
Liu, A. Jumabayeva, Y. Xu, Y. Wang, T. Frank, S. Gat, O. Bat Mor, Y. Ben-Shoshan, R. Ulichney, and J. Allebach, “New results for aperiodic, dispersed-dot halftoning,” Color Imaging XXV: Displaying, Processing, Hardcopy, and Applications, (Part of IS&T Electronic Imaging 2020), R. Eschbach, G. Marcu, and A. Rizzi, Eds., Burlingame, CA, 26 January - 30 January 2020.

## Slide 6: Big picture
FM (Frequency modulation) halftoning (aperiodic and dispersed-dots) is increasingly popular with traditional analog offset lithographic printing.
There is a desire from customers in the commercial market to use this capability with high-end digital presses based on electrophotographic printing (EP) technologies.
However, the inherent instability of the EP process challenges the achievement of satisfactory print quality with dispersed-dot, aperiodic halftoning.
The direct binary search (DBS) algorithm is widely considered to represent the gold standard of dispersed-dot, aperiodic halftone image quality.
We continue our previous efforts to adapt DBS from dispersed-dots to clustered-dots to use with the Indigo liquid EP printing technology.

## Slide 7: What we will specifically talk about today?
Overview of DBS and CLU-DBS
MS-MP-CLU-DBS Screen Design

## Slide 8: Direct Binary Search (DBS) Framework
perceived original continuous-tone image
perceived halftoned image
perceptually filtered error
mean-squared perceptually filtered error
Human visual system (HVS) filter
halftoned image
original continuous-tone image

## Slide 9: Dispersed-dots to clustered-dots
Since printers using electrophotographic (EP) technology cannot render isolated dots stably, what we found is that clustered-dots halftones would give us a better print quality without losing details in highlights or shadows.
The DBS optimization framework had been modified to design stochastic, clustered-dot texture, by using filters with different sizes in the initialization and update steps of the algorithm.

## Slide 10: Cost metric for CLU-DBS*
* P. Goyal, M. Gupta, C.Staelin, M. Fischer, O. Shacham and J. Allebach “Clustered-Dot Halftoning With Direct Binary Search ”
IEEE Transactions on Image Processing, vol. 22, no.2, pp. 473–487, Feb. 2013.

## Slide 11: CLU-DBS
Difference between Conventional DBS and CLU-DBS
Initialization filter
Update filter
Difference

## Slide 12: Factors influencing CLU-DBS halftone texture
Seed halftone
Filter type
Filter scale parameter
Relation between halftone frequency and filter size
Multi-Pass refinement
Multi-State refinement

## Slide 13: MP-CLU-DBS
Multi-pass (MP) refinement
    Is used to refine the halftone texture.
    A pass is a complete refinement consisting of multiple iterations of the CLU-DBS algorithm.
Iteration 1
Iteration n
…...
Seed
Halftone
Initialization
filter
Update
filter
DBS
Final halftone
CLU-DBS
Iteration 2
Single pass:
Multi-pass:
Each re-optimization is carried out with the original filters, and this leads to a homogenous texture.
Seed
Halftone
CLU-DBS
CLU-DBS
CLU-DBS
…...
Optimal
Halftone
From Pass 1
Optimal
Halftone
From Pass 2
Optimal
Halftone
From Pass n
MP-CLU-DBS

## Slide 14: Halftone Result of MP-CLU-DBS
Pass 1
Pass 2
Pass 3
Pass n
……
Original image
Halftone result based on MP-CLU-DBS
Gray level = 127/255

## Slide 15: MS-MP-CLU-DBS
Multi-stage (MS) optimization
    Is the core part of the algorithm.
    Starting with a seed halftone, the key idea is to build up the continuous-tone (CT) image stage-by-stage.
    The absorptance value of the continuous-tone image in each stage is controlled by attenuation factors.

## Slide 16: MS-MP-CLU-DBS
MP-CLU-DBS
…...
Stage 1 halftone result
Stage 2 halftone result
Stage K halftone result
Stage 1
MP-CLU-DBS
MP-CLU-DBS
Stage 2
Stage K
MS-MP-CLU-DBS:
Original image
Gray level = 127/255
continuous-tone
image
Halftone
result
Stage 1
Stage 2
Stage 3
Stage 4
Stage 5
5 stages in all
attenuation factors: {0.2, 0.4, 0.6, 0.8, 1.0}
Gray level = 7.5/255
Seed
Halftone
Seed
Halftone
Stage 1
continuous-
tone image
Stage 2
continuous-
tone image
Stage K
continuous-
tone image

## Slide 17: MS-MP-CLU-DBS applied to a continuous-tone folded ramp
MS = 5; MP = 10

## Slide 18: Outline
Overview of DBS and CLU-DBS
MS-MP-CLU-DBS Screen Design
    Screen design procedure
    Desired LPI (halftone frequency)
    Halftone quality and metrics

## Slide 19: Screen Design
A screen is a threshold matrix that can be used to halftone any input image by pixel-wise comparison of the image with the screen. A screen is constructed by designing halftones for each gray-level in the tonal range in some specified sequence with stacking constraints applied.
Generating a halftone from a screen is much faster than generating a halftone by directly applying MS-MP-CLU-DBS.
Our goal of the screen is to generate a halftone that would have texture quality similar to that of direct MS-MP-CLU-DBS.

## Slide 20: MS-MP-CLU-DBS based screen design
Generate a threshold matrix that is based on MS-MP-CLU-DBS
    Giving an initial level that is between 0-255 (in our case, gray-level of 127), and generate a continuous-tone patch size of 256 256.
    Use MS-MP-CLU-DBS to generate desired halftone of gray-level 127.
      Set seed halftone level to be 7.57, where absorptance of seed halftone has function of , is desired frequency in lpi and R is the printer resolution in dpi. =280 lpi, R=1625.6 dpi. *
      MS=5 and MP=10.
    Add or delete a sufficient number of dots to or from the initial halftone to reach the exact gray-level of 127.
    Use toggle-only to generate levels below the initial level with stacking constraints by removing 256 pixels at each level.
      Each new dot is removed in a greedy fashion by exploring all possible locations and picking the one that either deceases the cost the most or increases it the least.
    Use toggle-only to generate levels above the initial level with stacking constraints by adding 256 pixels at each level.
      Each new dot is added in a greedy fashion by exploring all possible locations and picking the one that either deceases the cost the most or increases it the least.
    Generate threshold matrix based on the above procedure.
* M. Gupta, PhD Dissertation, “Clustered-dot Halftoning with Direct Binary Search”, Jan. 2010

## Slide 21: An example
Initial level of 127
Level: 126
Generated from Initial level of 127
with stacking constraints by removing 256 dots
Difference
dots
=
Gaussian parameters: ,
Screen size: 256 256
Patch size: 256 256

## Slide 22: Comparison with direct MS-MP-CLU-DBS
Generated from Screen
Generated from direct MS-MP-CLU-DBS
Gaussian parameters: ,
Screen size: 256 x 256
Seed halftone: 7.57

## Slide 23: Outline
Overview of DBS and CLU-DBS
MS-MP-CLU-DBS Screen Design
    Screen design procedure
    Desired LPI (halftone frequency)
    Halftone quality and metrics

## Slide 24: Desired LPI (halftone frequency)
From our previous work, we noted that applying Gaussian filters with various values of would cause the frequency of the halftone to vary.
We tried several Gaussian filters to get a combination that the halftone generated would have better print quality and reach to desired halftone frequency (260 lpi ~ 280 lpi).
For each combination, we generated a screen from it and applied the screen to constant continuous-tone patches to get halftones.
Our method to determine the frequency associated with a halftone is to locate the maximum in the Radially Averaged Power Spectrum (RAPS) curve, computed from the Fourier transform of the halftone*.
We found that applying the combination of , to the screen design would give us a better texture quality and a very stable halftone frequency of 268.21 lpi.
* R. Ulichney, “Dithering with blue noise,” Proc. IEEE, vol. 76, pp. 56–79, Jan. 1988.

## Slide 25: Level 16
Gaussian parameters: ,
Screen size: 256 256
: 268.21 lpi

## Slide 26: Apply the new screen to a folded ramp
,

## Slide 27: Outline
Overview of DBS and CLU-DBS
MS-MP-CLU-DBS Screen Design
    Screen design procedure
    Desired LPI (halftone frequency)
    Halftone quality and metrics

## Slide 28: Halftone quality and metrics
Parameters:
    Screen size: 256256
    Total number of levels: 256
    Gray-levels that I generated: 16, 32, 48, 64, 80, 96, 112, 128, 144, 160, 176, 192, 218, 224, 240.
Pair Correlation
2D Fourier Spectrum Magnitude
Radially Average Power Spectrum

## Slide 29: Pair Correlation
Level 16
Level 64
Level 128
D. L. Lau, G. R. Arce, and N. C. Gallagher, “Green-noise digital halftoning,”
Proc. IEEE, vol. 86, pp. 2424–2444, Dec. 1998.
Notes: average separation of clusters

## Slide 30: 2D Fourier Spectrum Magnitude
Level 16
Level 64
Level 128

## Slide 31: Radially Average Power Spectrum
Level 16
Level 64
Level 128
: 268.21 lpi
: 268.21 lpi
: 268.21 lpi
R. Ulichney, “Dithering with blue noise,” Proc. IEEE, vol. 76, pp. 56–79, Jan. 1988.

## Slide 32: Conclusion
We have performed a screen design based on MS-MP-CLU-DBS to generate aperiodic clustered-dots halftones to use with the Indigo liquid EP printing technology.
We have explored a combination of Gaussian filters, and chose a combination that yields good halftone quality and the desired LPI based on the maximum in the Radially Averaged Power Spectrum (RAPS) curve.
We have shown that our screen design has a very stable LPI.
We have used several metrics to validate our screen-based halftone quality.

## Slide 33: Thank you!