## Slide 1: A Microscopic View of Bursts, Buffer Contention, and Loss in Data Centers
Ehab Ghabashneh, Yimeng Zhao, Cristian Lumezanu, Neil Spring, Srikanth Sundaresan, Sanjay Rao

## Slide 2: Introduction
Data center traffic patterns are crucial for network design tasks.
Data center traffic is bursty.
Bursts can collide on ToR switch. ASIC is dynamically shared. Thus, loss.

## Slide 3: Introduction
0
50
100
0
100
150
200
250
300
Link Utilization (%)
Time (ms)
Burst Threshold
This work aims to:
Characterize bursts
  Burst Length
  Burst Frequency
  # of connections (incast level)

## Slide 4: Introduction
0
50
100
0
100
150
200
250
300
Link Utilization (%)
Time (ms)
Burst Threshold
This work aims to:
Characterize bursts
  Burst Length
  Burst Frequency
  # of connections (incast level)
Characterize contention

## Slide 5: Introduction
0
50
100
0
100
150
200
250
300
Link Utilization (%)
Time (ms)
Burst Threshold
This work aims to:
Characterize bursts
  Burst Length
  Burst Frequency
  # of connections (incast level)
Characterize contention
Study how the interplay between burstiness and contention impacts loss

## Slide 6: Measurement Constraints
Low per-packet processing, to run at line rate
Low storage overhead, to keep history of all server-links
Programmable, deployable, and maintainable at scale

## Slide 7: Switch-based monitoring is insufficient!
1He etal. “Understanding switch buffer utilization in CLOS data center fabric”. Buffer-workshop stanford 2019.
2Benson etal. “Network traffic characteristics of data centers in the wild”. SIGCOMM 2010.
3Kandula etal. “The nature of data center traffic: measurements & analysis”.SIGCOMM 2009.
4Roy etal. “Inside the social network’s (datacenter) network”. SIGCOMM 2015
Time (min)
0
5
10
15
20
25
Link Utilization (%)
0
50
100
Existings traffic monitoring are switch-based.
Coarse grained [1-4]

## Slide 8: Switch-based monitoring is insufficient!
Time (min)
0
5
10
15
20
25
Link Utilization (%)
0
50
100
Link Utilization (%)
Time (ms)
0
50
100
0
400
800
1200
1600
2000
Existing traffic monitoring are switch-based.
Coarse grained [1-4]
  Cannot correlate loss with link utilization
Fine grained [5]
1He etal. “Understanding switch buffer utilization in CLOS data center fabric”. Buffer-workshop stanford 2019.
2Benson etal. “Network traffic characteristics of data centers in the wild”. SIGCOMM 2010.
3Kandula etal. “The nature of data center traffic: measurements & analysis”.SIGCOMM 2009.
4Roy etal. “Inside the social network’s (datacenter) network”. SIGCOMM 2015
5Zhang etal. “High-resolution measurement of data center microbursts”. IMC 2017.

## Slide 9: Switch-based monitoring is insufficient!
Time (min)
0
5
10
15
20
25
Link Utilization (%)
0
50
100
Link Utilization (%)
Time (ms)
0
50
100
0
400
800
1200
1600
2000
Existing traffic monitoring are switch-based.
Coarse grained [1-4]
  Cannot correlate loss with link utilization
Fine grained [5]
  Cannot run on scale due to intensive overhead
1He etal. “Understanding switch buffer utilization in CLOS data center fabric”. Buffer-workshop stanford 2019.
2Benson etal. “Network traffic characteristics of data centers in the wild”. SIGCOMM 2010.
3Kandula etal. “The nature of data center traffic: measurements & analysis”.SIGCOMM 2009.
4Roy etal. “Inside the social network’s (datacenter) network”. SIGCOMM 2015
5Zhang etal. “High-resolution measurement of data center microbursts”. IMC 2017.

## Slide 10: Contributions
Millisampler lightweight network traffic characterization tool
  Operates at fine, configurable time scales
  Deployed at every host in our fleet
  Instrumenting hosts allows for richer context
Host-centric large scale characterization of bursts, contention, and loss
  91.4% of bursts experience contention
  Drop in buffer share due to contention > 70% in some cases
  Low contended racks experienced 2.9X higher loss than highly contended ones

## Slide 11: What is Millisampler?
Millisampler comprises user-space code to collect network info at fine granule time-scales.
Millisampler memory footprint comprises of 2000 64-bit counters per CPU core for each metric it tallies:
  Ingress/Egress total and retx
  Ingress ECN marked bytes
  Number of active connections

## Slide 12: SyncMillisampler for contention
For synchronized bursts across servers contending for ToR switch buffer, we developed SyncMillisampler.
SyncMillisampler has centralized control plane to schedule concurrent runs across servers in a rack.

## Slide 13: Snapshot of SyncMillisampler run

## Slide 14: Large scale analysis of bursts, contention, and loss
Bursts Characterization
Contention Characterization
Bursts and contention correlation with loss

## Slide 15: Dataset
Single weekday in 2022
Two Meta regions (regA and RegB)
  Multiple data centers per region
  1000’s of racks
Randomly select 1000 racks to sample, and repeat!
  44.8K runs → 4.08M server-runs → 8.16B samples
Validated results from additional three weekdays

## Slide 16: Large scale analysis of bursts, contention, and loss
Bursts Characterization
  Burst are frequent. Median run experience 7.5 bursts/sec
  Bursts are short. Median burst length is 1-2 ms
  The number of active connections is 2.7X higher during burst
Contention Characterization
Bursts and contention correlation with loss

## Slide 17: Large scale analysis of bursts, contention, and loss
Bursts Characterization
Contention Characterization
Bursts and contention correlation with loss

## Slide 18: How buffer is shared across servers?
ToR Switch uses dynamic threshold (DT) algorithm for sharing buffer across all servers.
Balance competing goals of avoiding loss and fairness.
⍺ is a knop

## Slide 19: Contention Characterization: Motivation
What is the degree of contention in data center racks? How does contention vary across racks ?
How does contention vary within a rack across timescales ranging from milliseconds to an entire day?

## Slide 20: How contention looks across racks ?
Racks average contention follows different distribution per region
  RegA is bimodal
  RegB is uniform
Yet, similar spread of average contention
Busy Hour
Average

## Slide 21: Does contention vary across the day?
avg per run  (mean, min, and max)
Low contended racks
Low contention variation.
Highly contended racks
Always highly contended
Increase ⍺ ?

## Slide 22: Contention variation within the run: RegA
22.4K rack runs
Drop in buffer
share >= 70%
Drop in buffer share
Low contended runs. Small change in contention  huge drop in buffer share
High contended runs.
Small yet stable buffer share.

## Slide 23: Contention interplay with task placement
60% to 100% of servers in the highly contended racks run the same task
The task placement algorithm favored co-locating ML workloads densely in a single rack
Low contended racks are more tasks diversified. Only 25% of servers in median rack run the same task

## Slide 24: Large scale analysis of bursts, contention, and loss
Bursts Characterization
Contention Characterization
Bursts and contention correlation with loss

## Slide 25
Contention, Bursts, and Loss: Motivation
How does contention impact losses?
How do burst properties interplay with contention impact losses?

## Slide 26: How does contention impact loss?
RegA-Typical
RegA-High
91.4% of bursts are contended.
Surprisingly, bursts in RegA-Typical are experiencing more loss 2.9x higher than RegA-High.

## Slide 27: How do burst properties and contention impact loss?
Buffer absorbs short bursts
long bursts Stable loss
contended bursts Higher loss, and takes longer to stabilize
Burst Length

## Slide 28: How do burst properties and contention impact loss?
Incast
Contended bursts with heavy incast experience 2-3X of the loss for the not contended.

## Slide 29: Conclusion
Millisampler is a lightweight network traffic tool that:
  Takes host-centric perspective to data collections
  Collect traffic at time-scales of milliseconds
  Operationally deployed across all hosts in meta network
Data center scale joint analysis of contention, traffic burstiness, and loss
  91.4% Bursts experience contention, and hence variable buffers
  Racks average contention follows different distribution and widely varies across racks
  Low contended racks experience 2.9X more loss than highly contended ones
  15% of runs experience > 70% drop in buffer share
Watch out for the dataset which we will be releasing soon