## Slide 1
BeauCoup:
Answering many network traffic queries, one memory update at a time!
Xiaoqi Chen, Shir Landau-Feibish, Mark Braverman, Jennifer Rexford
1[bo’ku] Adv. many, a lot.
1

## Slide 2: Network traffic query
Internet
DDoS:
Are there many Source IPs sending to one particular Destination IP?
Select DstIP where distinct(SrcIP)>1000
Key
Attribute
Threshold

## Slide 3: Many network traffic queries
Query | Key | Attribute | Threshold
DDoS | DstIP | SrcIP | 1000
Worm | SrcIP | DstIP | 300
PortScan | SrcIP,DstIP | DstPort | 100
… | … | … | …
Internet
DDoS?
Worm?
Port Scan?
…
Different keys/attrs, need multiple data structures

## Slide 4: Many network traffic queries
I have 42 queries
Run 42 data structures?
I can’t…
Spec for today’s commodity programmable switch:
XX Tbps aggregated throughput
YY MB data-plane memory
Can only access ZZ bytes of memory per packet
(True for CPU, FPGA, etc., as well… Moore’s law!)

## Slide 5: One memory update at a time?
Constant memory update per packet, regardless of the number of queries?
Game plan:
  Each query uses only o(1) memory update per packet on average
  Combine many different queries, on average uses O(1)
  Coordinate, at most O(1) per packet

## Slide 6: Today’s talk
Challenge: many queries, few memory updates
Achieving o(1) memory access: coupon collectors
System design: query compiler + data plane program
Evaluation

## Slide 7: The coupon collector problem
C
D
A
4 different coupons, collect all of them
Random draws
How many total draws are required?
B
?

## Slide 8: BeauCoup coupon collector
f(10.0.1.15) -> Coupon
f(10.0.1.33) -> Coupon
f(10.0.1.15) -> Coupon
f(10.0.1.42) -> No Coupon
f(SrcIP) -> Coupon
?
Mapping
Select DstIP where distinct(SrcIP)>100
Collect different coupons
C
B
C
C
D
A
B
SrcIP: 10.0.1.15
DstIP: 162.249.4.107
SrcIP: 10.0.1.33
DstIP: 162.249.4.107
SrcIP: 10.0.1.42
DstIP: 162.249.4.107
Key: 162.249.4.107
Coupons:

## Slide 9: BeauCoup coupon collector
Generalization: (m, p, n)-coupon collector
m*p<1, most packets collect no coupon
f(SrcIP) -> Coupon
?
m=8 coupons in total
stop at n=4 different coupons
Example:
(m=8, p=1%, n=4)
Given a new SrcIP, each coupon is drawn with probability 1%

## Slide 10: System design
Query compiler: finds coupon collector configurations
  Stops near query thresholds, minimize error
  Hardware limits (e.g., memory access limit)
  Fairness across queries
Data plane program: collect coupons into in-memory table
  Simultaneously run many queries
  At most one coupon per packet
  Update queries on-the-fly

## Slide 11: Query compiler
γq= Γ / |Q| (fair allocation)
Compiler
Query set Q = {q1, q2, …}
Total memory update limit: Γ per packet
Per-query limit: γq per packet
Query qi
Key, Attribute,
Threshold
qi’s Collector Configuration
Total coupons: m
Each probability: p
Coupons to collect: n
Query qi
Key, Attribute,
Threshold
Query qi
Key, Attribute,
Threshold
qi’s Collector Configuration
Total coupons: m
Each probability: p
Coupons to collect: n
qi’s Collector Configuration
Total coupons: m
Each probability: p
Coupons to collect: n
Goal:
Stop near Threshold
Update limit m*p≤γq
HW limit, e.g., m≤32
For more detail on compiler heuristics, please refer to our paper.

## Slide 12: Query compiler
Query set Q = {q1, q2, …}
Query Compiler
Total coupons: m
Each probability: p
Coupons to collect: n
P4 Program
Switch Data Plane
Threshold=1000, γq =0.01
(m=20,p=1/2048,n=8)
Threshold=1000

## Slide 13: Stacking queries: same attribute
q1: f(SrcIP) -> Coupon . m1=4, p1=1/8
?
Hash function
h1(SrcIP) -> [0,1)
1
1/4
1/2
3/4
0
q1 #1
q1 #2
q1 #3
q1 #4
4 coupons for q1
q2: f(SrcIP) -> Coupon . m2=3, p2=1/16
?
q2 #1
q2 #2
q2 #3
3 coupons for q2
…
…

## Slide 14: One hash function for each attribute
q1: f(SrcIP) -> Coupon . m1=4, p1=1/8
?
q6: g(DstIP) -> Coupon . m6=3, p6=1/8
?
h1(SrcIP) ->
1
1/4
1/2
3/4
0
q1 #1
q1 #2
q1 #3
q1 #4
…
h2(DstIP) ->
1
1/4
1/2
3/4
0
q6 #1
q6 #2
q6 #3
…

## Slide 15: TCAM for selecting a coupon
Packet
SrcPort: 25012
DstPort: 443
SrcIP: 10.0.1.15
DstIP: 162.249.4.107
hA(SrcPort)=101010…
hB(DstPort)=111010…
hC(SrcIP)=1010111…
hD(DstIP)=0101011…
Match hA(SrcPort) | Query#,Coupon#
000***** | (5,1)
001***** | (5,2)
010***** | (5,3)
01101*** | (9,1)
… | …
Match hB(DstPort) | Query#,Coupon#
… | …
Match hC(SrcIP) | Query#,Coupon#
… | …
Match hD(DstIP) | Query#,Coupon#
000***** | (6,1)
001***** | (6,2)
010***** | (6,3)
01101*** | (8,1)
… | …
No coupon
q6 #3
Collect coupon (q6, #3)
No coupon
No coupon
Random tiebreak if >1 coupons

## Slide 16: Coupon collector table
Q , Key | Coupons
q4: 8.8.8.8:53 | 
q4: 1.1.1.1:53 | 
q5: 10.0.0.1 | 
q6: 10.0.1.33 | 
q6: 10.0.1.15 | 
1
4
2
3
1
4
2
3
1
2
3
4
3
1
2
3
1
2
3
2
Packet
SrcPort: 25012
DstPort: 443
SrcIP: 10.0.1.15
DstIP: 162.249.4.107
q6 #3
q6: SrcIP
q6 Coupon #3
Key: 10.0.1.15
Query q6
Key 10.0.1.33
3
Packet
SrcPort: 27000
DstPort: 443
SrcIP: 10.0.1.33
DstIP: 4.3.2.1
q6 #1
q6 Coupon #1
Key: 10.0.1.33
1
q6: DstIP, 1000
SrcIP 10.0.1.33 is sending to >1000 distinct DstIPs.
Space efficiency:
Keys from all queries multiplexed into one table
Only keep rows for “active keys” (at least one coupon)
Clear rows after timeout

## Slide 17: Installing queries into switches
The installed rules represent query set Q
Update queries on the fly, without recompiling P4
Table rules
Header field tuples
Key, Attribute, Threshold
Code Generator
Query Compiler
(m,p,n)
Rules Generator
P4 Compiler
Data plane program
Static
program
Dynamic
rules
Query set Q = {q1, q2, …}
code
Programmable Switch
Packets
Alerts

## Slide 18: Evaluation highlights
How efficient is BeauCoup?
We uses 4x~10x fewer memory access than the state-of-the-art to achieve the same accuracy.
What about fairness?
Equalized accuracy for same-threshold queries.
How much hardware resource?
On the Barefoot Tofino programmable switch, BeauCoup occupies <50% of each resource

## Slide 19: Accuracy metric: Mean Relative Error
Threshold
Wider
Narrow
x = Actual # of distinct
Error=|x - Threshold|
MRE= Error / Threshold

## Slide 20: Comparing accuracy
Memory Access Word Per Packet | Sampling1 | NitroSketch2 +UnivMon3 | HyperLogLog | BeauCoup
γq=1/10 | 82% | 33% | X | 17%
γq=1/42 | 290% | 84% | X | 31%
Mean Relative Error for distinct(SrcIP,DstIP)
1On estimating the number of flows. Spang & McKeown, Buffer Sizing Workshop 2019
2NitroSketch: Robust and General Sketch-based Monitoring in Software Switches. Liu et al., SIGCOMM 2019
3One Sketch to Rule Them All: Rethinking Network Flow Monitoring with UnivMon. Liu et al., SIGCOMM 2016

## Slide 21: Single-query accuracy
NitroSketch-Univmon1
BeauCoup
Sampling2
HyperLogLog
Stricter
Better
Better
4x~10x
1NitroSketch: Robust and General Sketch-based Monitoring in Software Switches. Liu et al., SIGCOMM 2019
2On estimating the number of flows. Spang & McKeown, Buffer Sizing Workshop 2019

## Slide 22: Across multiple queries
Total memory access per packet
Mean Relative Error
Key=SrcIP
Attribute= DstIP
Threshold=1000
Key=SrcIP
Attribute= DstIP+DstPort
Threshold=1000
Key=DstIP+DstPort
Attribute= SrcIP
Threshold=1000
Key=DstIP+DstPort
Attribute= SrcIP+SrcPort
Threshold=1000
Run |Q|=26 queries simultaneously
Fairness among queries: same accuracy

## Slide 23: Across multiple queries
Run |Q|=26 queries simultaneously
Intuition: high-threshold query is ”easier”, low-threshold query benefits from more memory access
Total memory access per packet
Mean Relative Error
Threshold=100
Threshold=500
Threshold=5000
Threshold=10000

## Slide 24: Hardware resource utilization (Tofino v1)
 | Matching Coupons | Extracting Query Key | Collecting Coupons | Teardown | Overall
TCAM | 39.6% | 2.3% | 0% | 0% | 13.2%
SRAM | 9.1% | 2.1% | 26.3% | 0% | 12.3%
Instruction | 25.0% | 7.3% | 5.4% | 3.1% | 12.8%
Hash Unit | 50.0% | 61.1% | 29.1% | 0% | 41.7%
h(Attribute)->
1/4
1/2
0
…
q6
q6: SrcIP
Key: 10.0.1.15
Q , Key | Coupons
q1:8.8.8.8 | 
q1:1.1.1.1 | 
1
2
3
1
2
3
3
Alerts!

## Slide 25
Scalable: built upon coupon collectors, runs many queries simultaneously
Versatile: change queries on the fly, without recompiling P4 program
Efficient: achieve the same accuracy using 4x-10x fewer memory accesses
Our code is open-source! github.com/Princeton-Cabernet/BeauCoup
BeauCoup:
Answering many network traffic queries, one memory update at a time!
Q&A on
Slack
Merci Beaucoup! Thank you!

## Slide 26
Face
Face