## Slide 1: Section 7 Bandstructure in 1D Periodic Potentials
Solid State Devices

## Slide 2: Section 7 Bandstructure – in 1D Periodic Potentials
Original
Problem
Periodic
Structure
E
U
Goal: Representation of “Infinite Systems”
Tunneling through finite open systems
7.1 Bandstructure - Problem Formulation
7.2 Bandstructure - Solutions
7.3 Band Properties
Reference: Vol. 6, Ch. 3 Daniel Mejia, Gerhard Klimeck (2019), "Periodic Potential Lab - Kronig Penney Model, " https://nanohub.org/resources/kronigpenneylab. (DOI: 10.21981/TT2Y-A185).

## Slide 3: Reminder Transmission through Repeated Wells
2 barriers =>1 resonance
3 barriers =>2 resonance
n barriers =>n-1 resonance
As the number of barriers are increased more and more energy resonances begin to appear and energy bands are formed.
20 barriers
30 barriers
10 barriers
What if the number of wells is infinite?

## Slide 4: Reminder: Five Steps for Closed System Analytical Solution
1)
Solution Ansatz
2N unknowns
for N regions
2)
Boundary Conditions at the edge
Reduces 2 unknowns
3)
Boundary Condition at each interface:
Set 2N-2 equations for
2N-2 unknowns (for continuous U)
Det (coefficient matrix)=0
And find E by graphical
or numerical solution
4)
5)
Normalization of unity probability
for wave function
Open
Open

## Slide 5: Reminder: Five Steps for Closed System Analytical Solution
1)
Solution Ansatz
2N unknowns
for N regions
2)
Boundary Conditions at the edge
Reduces 2 unknowns
3)
Boundary Condition at each interface:
Set 2N-2 equations for
2N-2 unknowns (for continuous U)
Det (coefficient matrix)=0
And find E by graphical
or numerical solution
4)
5)
Normalization of unity probability
for wave function
Open
Open
Periodic
Periodic
Edge => huge number of cells
Bloch Theorem
Interface => interfaces in periodic cell

## Slide 6: Reminder: Five Steps for Closed System Analytical Solution
1)
Solution Ansatz
2N unknowns
for N regions
2)
Boundary Conditions at the edge
Reduces 2 unknowns
3)
Boundary Condition at each interface:
Set 2N-2 equations for
2N-2 unknowns (for continuous U)
Det (coefficient matrix)=0
And find E by graphical
or numerical solution
4)
5)
Normalization of unity probability
for wave function
Open
Open
Periodic
Periodic
Edge => huge number of cells
Bloch Theorem
Interface => interfaces in periodic cell

## Slide 7: Periodic Potential Concept
e
Repeated indefinitely
As the number of barriers is increased the electrons see no difference between the actual structure and a structure that is simply modeled as being repeated indefinitely (Periodic).
-∞
∞
Finite barriers
e

## Slide 8: Choosing the Smallest Unit Cell
e
Repeated indefinitely
As the number of barriers is increased the electrons see no difference between the actual structure and a structure that is simply modeled as being repeated indefinitely (Periodic).
-∞
∞
Choose the smallest cell to reduce computational work load
e

## Slide 9: Solution Ansatz Choose the Simplest Basis Set
e
As the number of barriers is increased the electrons see no difference between the actual structure and a structure that is simply modeled as being repeated indefinitely (Periodic).
Choose the smallest cell to reduce computational work load
Decays in barriers
Propagation above barriers
e

## Slide 10: Finally an (almost) Real Problem …
U(x)
E
But N atoms have two 2N unknown constants to find ….
For large N, isn’t there a better way ?
a
b
L=a+b

## Slide 11: Reminder: Five Steps for Closed System Analytical Solution
1)
Solution Ansatz
2N unknowns
for N regions
2)
Boundary Conditions at the edge
Reduces 2 unknowns
3)
Boundary Condition at each interface:
Set 2N-2 equations for
2N-2 unknowns (for continuous U)
Det (coefficient matrix)=0
And find E by graphical
or numerical solution
4)
5)
Normalization of unity probability
for wave function
Periodic
Periodic
Edge => huge number of cells
Bloch Theorem
Interface => interfaces in periodic cell

## Slide 12: Periodic U(x) and Bloch’s Theorem Periodic U(x) and Bloch’s Theorem
U(x)
E
U(x)=U(x+a+b)=U(x+L)
a
b
not our old (k)
p =some period length

## Slide 13: Phase-factor for N-cells
E
1
3
N
U(x)
2

## Slide 14: Step 2: Periodic Boundary Condition
E
1
2
3
N-1
1
2
3
N-1
U(x)

## Slide 15: Step 3: Boundary Conditions
0
a
-b

## Slide 16: Step 4: Det(matrix)=0 for Energy-levels
0
a
-b
4)

## Slide 17: Reminder: Five Steps for Closed System Analytical Solution
1)
Solution Ansatz
2N unknowns
for N regions
2)
Boundary Conditions at the edge
Reduces 2 unknowns
3)
Boundary Condition at each interface:
Set 2N-2 equations for
2N-2 unknowns (for continuous U)
Det (coefficient matrix)=0
And find E by graphical
or numerical solution
4)
5)
Normalization of unity probability
for wave function
Periodic
Periodic
Edge => huge number of cells
Bloch Theorem
Interface => interfaces in periodic cell

## Slide 18: Five Steps for Periodic System Analytical Solution
1)
Solution Ansatz
4 unknowns
for 1 periodic cell
2)
Periodic Boundary Conditions
Imposes symmetry
3)
Boundary Condition in periodic cell:
Set 4 equations for 4 unknowns
Det (coefficient matrix)=0
And find E by graphical
or numerical solution
4)
5)
Normalization of unity probability
for wave function
Bloch Theorem

## Slide 19: Section 7 Bandstructure – in 1D Periodic Potentials
7.1 Bandstructure - Problem Formulation
  Kronig-Penney Model setup
  Bloch theorem
  Analytical solution process
7.2 Bandstructure - Solutions
  Bandgaps
  Comparison to finite system model
7.3 Band Properties
  Wave packets
  Effective mass
  Electrons and Holes
One Video Segment
One Video Segment
One Video Segment
status
Reference: Vol. 6, Ch. 3 Daniel Mejia, Gerhard Klimeck (2019), "Periodic Potential Lab - Kronig Penney Model, " https://nanohub.org/resources/kronigpenneylab. (DOI: 10.21981/TT2Y-A185).

## Slide 20: Section 7 Bandstructure – in 1D Periodic Potentials
7.1 Bandstructure - Problem Formulation
  Kronig-Penney Model setup
  Bloch theorem
  Analytical solution process
7.2 Bandstructure - Solutions
  Bandgaps
  Comparison to finite system model
7.3 Band Properties
  Wave packets
  Effective mass
  Electrons and Holes
One Video Segment
One Video Segment
One Video Segment
status
Reference: Vol. 6, Ch. 3 Daniel Mejia, Gerhard Klimeck (2019), "Periodic Potential Lab - Kronig Penney Model, " https://nanohub.org/resources/kronigpenneylab. (DOI: 10.21981/TT2Y-A185).

## Slide 21: Section 7 Bandstructure in 1D Periodic Potentials 7.2 Bandstructure - Solutions
Solid State Devices

## Slide 22: Section 7 Bandstructure – in 1D Periodic Potentials
7.1 Bandstructure - Problem Formulation
  Kronig-Penney Model setup
  Bloch theorem
  Analytical solution process
7.2 Bandstructure - Solutions
  Bandgaps
  Comparison to finite system model
7.3 Band Properties
  Wave packets
  Effective mass
  Electrons and Holes
One Video Segment
One Video Segment
One Video Segment
status
Reference: Vol. 6, Ch. 3 Daniel Mejia, Gerhard Klimeck (2019), "Periodic Potential Lab - Kronig Penney Model, " https://nanohub.org/resources/kronigpenneylab. (DOI: 10.21981/TT2Y-A185).

## Slide 23: Graphical solution to Energy Levels
z=E/U
k=0
kL=2pn/N
1
-1
Right Hand side is a set of N flat lines between -1 and 1
Left Hand side is an ocillatory function with damping

## Slide 24: Energy Band Diagram
z=E/U
0
k
k=0
k=2p/NL
z=E/U

## Slide 25: Brillouin Zone and Number of States
k
E
4 states per atom, N atoms => 4 bands, N states in each band

## Slide 26: GaAs Well Comparison – 30 Barriers
A GaAs structure with 6nm wells, 2nm barriers and 0.4eV barrier height is modeled as follows,
PPL-Periodic structure repeated indefinitely.
TB: 30 barriers using tight-binding.
TM: 30 barriers using transfer matrices.
It can be seen that the results of these three approaches agree well.

## Slide 27: GaAs Well Comparison – 80 Barriers
A GaAs structure with 6nm wells, 2nm barriers and 0.4eV barrier height is modeled as follows,
PPL-Periodic structure repeated indefinitely.
TB: 80 barriers using tight-binding.
TM: 80 barriers using transfer matrices.
It can be seen that the results of these three approaches agree well.

## Slide 28: InAs Well Comparison – 30 Barriers
An InAs structure with 6nm wells, 2nm barriers and 0.4eV barrier height is modeled as follows,
PPL-Periodic structure repeated indefinitely.
TB: 30 barriers using tight-binding.
TM: 30 barriers using transfer matrices.
It can be seen that the results of these three approaches agree well.

## Slide 29: Key Summary
Finite superlattice with large number of repeated cells approaches the periodic potential model

## Slide 30: Section 7 Bandstructure – in 1D Periodic Potentials
7.1 Bandstructure - Problem Formulation
  Kronig-Penney Model setup
  Bloch theorem
  Analytical solution process
7.2 Bandstructure - Solutions
  Bandgaps
  Comparison to finite system model
7.3 Band Properties
  Wave packets
  Effective mass
  Electrons and Holes
One Video Segment
One Video Segment
One Video Segment
status
Reference: Vol. 6, Ch. 3 Daniel Mejia, Gerhard Klimeck (2019), "Periodic Potential Lab - Kronig Penney Model, " https://nanohub.org/resources/kronigpenneylab. (DOI: 10.21981/TT2Y-A185).

## Slide 31: Section 7 Bandstructure – in 1D Periodic Potentials
7.1 Bandstructure - Problem Formulation
  Kronig-Penney Model setup
  Bloch theorem
  Analytical solution process
7.2 Bandstructure - Solutions
  Bandgaps
  Comparison to finite system model
7.3 Band Properties
  Wave packets
  Effective mass
  Electrons and Holes
One Video Segment
One Video Segment
One Video Segment
status
Reference: Vol. 6, Ch. 3 Daniel Mejia, Gerhard Klimeck (2019), "Periodic Potential Lab - Kronig Penney Model, " https://nanohub.org/resources/kronigpenneylab. (DOI: 10.21981/TT2Y-A185).

## Slide 32: Section 7 Bandstructure in 1D Periodic Potentials 7.3 Band Properties
Solid State Devices

## Slide 33: Section 7 Bandstructure – in 1D Periodic Potentials
7.1 Bandstructure - Problem Formulation
  Kronig-Penney Model setup
  Bloch theorem
  Analytical solution process
7.2 Bandstructure - Solutions
  Bandgaps
  Comparison to finite system model
7.3 Band Properties
  Wave packets
  Effective mass
  Electrons and Holes
One Video Segment
One Video Segment
One Video Segment
status
Reference: Vol. 6, Ch. 3 Daniel Mejia, Gerhard Klimeck (2019), "Periodic Potential Lab - Kronig Penney Model, " https://nanohub.org/resources/kronigpenneylab. (DOI: 10.21981/TT2Y-A185).

## Slide 34: Wave Packet and Group Velocity
k
t1
t2

## Slide 35: Group Velocity for a Given Band
t1
t2
momentum
force

## Slide 36: Effective Mass for a Given Band
k
1/m*
k
v
E
mass for each band
mass changes throughout the band

## Slide 37: Effective Mass is not Essential …
k
1/m*
k
v
E
??
k
Mass appears to be ill-defined
Integral description of the momentum and position change of wavepackets
Do not need effective mass
=> Effective mass is not a critical physical property!
=> Graphene is a material with such linear dispersion!

## Slide 38: Electron and Hole fluxes: Filled/Empty Bands
k
E
Need
inversion symmetry (number of states in +/-k identical)
Pauli exclusion principle
-k
EF
Empty bands carry no current
Full bands carry no current

## Slide 39: Partially filled bands
k
E
3
2
1
Empty bands carry no current
Full bands carry no current
Let’s imagine there is a way to get some electrons from the valence band into the conduction band!
Partial filling can be achieved by:
Optical excitation
Thermal excitation
Doping + a little thermal excitation

## Slide 40: Electron and Hole Fluxes: Partially Filled Bands
k
E
-ve charge moving with –ve mass
+ve charge moving with +ve mass
3
2
1
Shockley example – top view of parking lot

## Slide 41: Interpretation of the effective mass ?
k
1/m*
k
-k
E
m* not free mass
m* function of k
negative and positive (in the same band!)
But for Transport:
Some bands are more important than others
Some are always full
Some are always empty
Minimizing energy:
Electrons “fall” to the bottom
Holes “float” to the top
“Constant” Masses at:
Bottom conduction band
Top valence band

## Slide 42: Conclusions
Solution of Schrodinger equation is relatively easy for systems with well-defined periodicity.
Kronig-Penney model is analytically solvable. Real band-structures are solved numerically. Such solutions are relatively easy – we will do HW problems on nanohub.org on this topic.
Electrons can only sit in-specific energy bands.
Effective masses and band gaps summarize information about possible electronic states.
Effective mass is not a fundamental concept. There are systems for which effective mass can not be defined.
Of all the possible bands, only a few contribute to conduction. These are often called conduction and valence bands.

## Slide 43: Section 7 Bandstructure – in 1D Periodic Potentials
7.1 Bandstructure - Problem Formulation
  Kronig-Penney Model setup
  Bloch theorem
  Analytical solution process
7.2 Bandstructure - Solutions
  Bandgaps
  Comparison to finite system model
7.3 Band Properties
  Wave packets
  Effective mass
  Electrons and Holes
One Video Segment
One Video Segment
One Video Segment
Reference: Vol. 6, Ch. 3 Daniel Mejia, Gerhard Klimeck (2019), "Periodic Potential Lab - …., " https://nanohub.org/resources/kronigpenneylab. (DOI: 10.21981/TT2Y-A185).